| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | Protocol design principles and requirements |
| Source:* | Institut Mines-Telecom |
| Contact: | Soochang Park, IMT, soochang.park@telecom-sudparis.eu Noel Crespi, IMT, noel.crespi@mines-telecom.fr Antonio M. Ortiz, IMT, antonio.ortiz_torres@it-sudparis.eu Eric Farnier, ECOMETERING, eric.farnier@gdfsuez.com |
| Date:* | 2014-09-24 |
| Abstract:* | This contribution provides the description for the protocol design principles and requirements to include the proposed text in Section 5.4 of the TS-0004 (oneM2M Core Protocol Specification). |
| Agenda Item:* | 6 |
| Work item(s): | WI 009, oneM2M Protocol Development |
| Document(s) Impacted* | oneM2M TS-0004, oneM2M Core Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To include the proposed text in the TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

R01- reformed along with the rule to show up correction parts

R02- revised to achieve protocol specification visions

1

2	Proposal

In this contribution, we propose to insert the following text in the Section 5.4 of the TS (v-0.6.1) on oneM2M Core Protocol Specification.

-------------------------------- Proposed Text --------------------------

# Protocol Design Principals and Requirements

## Design Principles

### Scalability

When considering scalability as a requirement in the design of oneM2M protocols, one or several of the following mechanisms could be used:

- Wherever possible, ensure direct addressability to the CSEs hosting target resources, to minimize network hops.

- Asynchrony in terms of data processing, with the ultimate objective of minimizing the number of discarded packets.

- Caching mechanisms that allow all the received packets to be processed.

- Efficient load distribution to avoid bottlenecks and data loss.

- Data compression and/or aggregation, in order to reduce the amount of data sent through the network.

### Extensibility

The oneM2M protocols will be designed to allow continued development and to facilitate changes by means of standardized extensions.

The impact of the extensibility on the existing oneM2M protocol functions will be minimized.

As an example, extensibility can be related to one or more of the following aspects:

- Handling a different number of devices,

- Add, remove or modify oneM2M protocol functionality,

- New oneM2M protocol routines,

- New data types.

The design of extensible oneM2M protocols will consider and mitigate the risk of unintended consequences, such as interoperability issues, operational problems, or security vulnerabilities.

### Fault tolerance and Robustness

For the design of oneM2M protocols with the ability to handle expected and unknown errors, one or several of the following mechanisms will be exploited:

- Packet Reliability

  - For reliable transmission of data packets, loss packet recovery could be dealt with in appropriate handling methods along with network capacities, e.g., end-to-end, hop-by-hop, or hybrid.

  - Especially, in the low link quality of oneM2M, multiple data dissemination paths should be provided and maintained.

- Data Reliability

In order to take care of accuracy of data from data corruption data reliability should be achieved with dynamic criteria to measure data accuracy.

### Efficiency

Energy Efficiency:

•	As energy consumption directly affects the overall system performance, oneM2M protocols should consider energy efficiency, especially in resource constrained environments with battery-powered oneM2M devices.

•	Energy efficient oneM2M protocols will aim at reducing the overall energy consumption while maintaining the performance required by the oneM2M Applications.

### (Security)

*Security requirements included in WG4

### Inter-operability

API inter-operability between different protocol stacks is expected. For example, that means oneM2M API over HTTP/TCP/IP and Fiber needs to inter-operate with Zigbee in home network using oneM2M API.

### Heterogeneous Connectivity

OneM2M API should support many different architectural communications because there are many different scenarios of API pass/transport data.

### Self-operation and management

To deal with many different scenarios of API configuration, devices operated by oneM2M API should inter-work with the defined management protocols, e.g. security, discovery, bootstrapping, etc.