CHANGE REQUEST Group Name:* WG3 Source:* IBM Format:* TP13 Date:* 2014-09-13 Contact:* Peter Niblett (peter_niblett@uk.ibm.com); Reason for Change/s:* Updates to the XML schema material in TS-0004 Clause/Sub Clause Affected* 6.3 and 6.5 Agenda Item:* Contribution Work item(s): Document(s) Impacted* oneM2M-TR 0004 Core Protocol v 0 6 2 Intended purpose of document:* Decision Discussion Information Other <specify> Decision requested or recommendation:* Agree to make these changes to the TS (oneM2M-TS-0004)

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Proposal

Make the changes described below to Clauses 6.3 and 6.5.

These changes include:

- General editorial tidying up

- Change the filename for the Common Types file to be CDT-commonTypes-v1_0_0.xsd (i.e. removed the date from the filename)

- Change “id” to “ID” wherever it appears in element or type names (this if for consistency with TS-0001)

- Re-order the common attribute table, so that the attributes appear in the order defined by TS-0001.

- Remove m2m:nhURI (use xs:anyURI instead)

- Add cardinality to complex types table

- Add ResourceType, ResourceID and Link common attributes (from TS-0001)

- Add m2m:childResourceRef complex type

- Update the usage example in 6.5 to match the directives in Annex F

- Additional m2m-defined types

  - m2m:labelsType

  - m2m:timestamp (placeholder)

11. Remove table 6.5.1 (oneM2M Structured Data Types) as it is no longer needed

I have also added some comments relating to some of the new m2m: types

======================== START 1ST CHANGE ===========================

## Common Data Types

For wide acceptance by industrial markets, the present document describes structured and non-structured data for oneM2M Protocol using XML Schema Definition Language (aka XSD) [3].

Note that the actual data format is depends on chosen Protocol Bindings. Each protocol binding specification will specify the mapping rule between XSD version of data definitions and its native data format.

Any Data Types and XML elements defined for use in oneM2M protocols shall use the namespace:

http://www.onem2m.org/xml/protocols.

The present document, and any XML or XML Schema Documents produced by oneM2M shall use the prefix m2m: to refer to that namespace.

### Simple Data Types incorporated from XML Schema

Following 'built-in data types' are incorporated from XML Schema definition [3].

Note that name space identifier for 'http://www.w3.org/2001/XMLSchema' shall be referred to using the prefix xs: in the present document.

Table 6.3.2.1-1: Simple Data Types incorporated from XML Schema

| Data Type | Description | Notes |
| --- | --- | --- |
| xs:string | The string datatype represents character strings in XML |  |
| xs:boolean | boolean represents the values of two-valued logic. |  |
| xs:decimal | decimal represents a subset of the real numbers, which can be represented by decimal numerals. The value space· of decimal is the set of numbers that can be obtained by dividing an integer by a non-negative power of ten, i.e. expressible as i / 10 n where i and n are integers and n ≥ 0. Precision is not reflected in this value space; the number 2.0 is not distinct from the number 2.00. The order relation on decimal is the order relation on real numbers, restricted to this subset. |  |
| xs:float | The float datatype is patterned after the IEEE single-precision 32-bit floating point datatype IEEE 754-2008 [8]. Its value space is a subset of the rational numbers. Floating point numbers are often used to approximate arbitrary real numbers. |  |
| xs:double | The double datatype is patterned after the IEEE double-precision 64-bit floating point datatype IEEE 754-2008 [8]. Each floating point datatype has a value space that is a subset of the rational numbers. Floating point numbers are often used to approximate arbitrary real numbers. |  |
| xs:duration | duration is a datatype that represents durations of time. |  |
| xs:dateTime | dateTime represents instants of time, optionally marked with a particular time zone offset. Values representing the same instant but having different time zone offsets are equal but not identical. |  |
| xs:time | time represents instants of time that recur at the same point in each calendar day, or that occur in some arbitrary calendar day. |  |
| xs:date | date represents top-open intervals of exactly one day in length on the timelines of dateTime, beginning on the beginning moment of each day, up to but not including the beginning moment of the next day). For non-timezoned values, the top-open intervals disjointly cover the non-timezoned timeline, one per day. For timezoned values, the intervals begin at every minute and therefore overlap. |  |
| xs:hexBinary | hexBinary represents arbitrary hex-encoded binary data. |  |
| xs:base64Binary | base64Binary represents arbitrary Base64-encoded binary data. For base64Binary data the entire binary stream is encoded using the Base64 Encoding defined in RFC 3548 [9], which is derived from the encoding described in RFC 2045 [10]. |  |
| xs:anyURI | anyURI represents an Internationalized Resource Identifier Reference (IRI). An anyURI value can be absolute or relative, and may have an optional fragment identifier (i.e. it may be an IRI Reference). This type should be used when the value fulfills the role of an IRI, as defined in RFC 3987 [11] or its successor(s) in the IETF Standards Track. |  |
| xs:normalizedString | normalizedString represents white space normalized strings. The ·value space· of normalizedString is the set of strings that do not contain the carriage return (#xD), line feed (#xA) nor tab (#x9) characters. The lexical space· of normalizedString is the set of strings that do not contain the carriage return (#xD), line feed (#xA) nor tab (#x9) characters. The base type·of normalizedString is string. |  |
| xs:token | token represents tokenized strings. The ·value space· of token is the set of strings that do not contain the carriage return (#xD), line feed (#xA) nor tab (#x9) characters, that have no leading or trailing spaces (#x20) and that have no internal sequences of two or more spaces. The lexical space· of token is the set of strings that do not contain the carriage return (#xD), line feed (#xA) nor tab (#x9) characters, that have no leading or trailing spaces (#x20) and that have no internal sequences of two or more spaces. The base type·of token is normalizedString. |  |
| xs:language | language represents formal natural language identifiers, as defined by BCP 47[12]. |  |
| xs:integer | integer is derived from decimal by fixing the value of fractionDigits·to be 0 and disallowing the trailing decimal point. This results in the standard mathematical concept of the integer numbers. The ·value space· of integer is the infinite set {...,-2,-1,0,1,2,...}. The·base type of integer is decimal. |  |
| xs:nonNegativeInteger | nonNegativeInteger has a lexical representation consisting of an optional sign followed by a non-empty finite-length sequence of decimal digits (#x30-#x39). If the sign is omitted, the positive sign ('+') is assumed. If the sign is present, it must be "+" except for lexical forms denoting zero, which may be preceded by a positive ('+') or a negative ('-') sign. For example: 1, 0, 12678967543233, +100000. |  |
| xs:positiveInteger | positiveInteger is·derived·from nonNegativeInteger by setting the value of minInclusive·to be 1. This results in the standard mathematical concept of the positive integer numbers. The ·value space· of positiveInteger is the infinite set {1,2,...}. The base type·of positiveInteger is nonNegativeInteger. |  |
| xs:unsignedLong | unsignedLong is derived· from nonNegativeInteger by setting the value of ·maxInclusive· to be 18446744073709551615. The base type·of unsignedLong is nonNegativeInteger. |  |
| xs:unsignedInt | unsignedInt is ·derived·from unsignedLong by setting the value of·maxInclusive·to be 4294967295. The base type·of unsignedInt is unsignedLong. |  |
| xs:unsignedShort | unsignedShort is ·derived· from unsignedInt by setting the value of maxInclusive· to be 65535. The·base type·of unsignedShort is unsignedInt. |  |
| xs:dateTimeStamp | The dateTimeStamp datatype is derived·from dateTime by giving the value required to its explicitTimezone facet. The result is that all values of dateTimeStamp are required to have explicit time zone offsets and the datatype is totally ordered. |  |

Editor's Note:  How to choose the local time zone at timestamp is FFS.

### Additional Data Types used in oneM2M

This clause defines the  data types that are defined by oneM2M for use in the oneM2M API. These data types are used in request/response parameters and attributes of resource types.

#### Simple Data Types

Table 6.3.2.1-1 describes oneM2M-specific simple data type definitions. XML Schema datatype definitions for these data types can be found in the XSD file called

CDT-commonTypes-v1_0_0.xsd.

The types in table 6.3.2.1-1 are either:

- Atomic datatypes derived from XML Schema datatypes by restrictions other than enumeration

- List datatypes constructed from other XML Schema or oneM2M-defined atomic datatypes.

The oneM2M-defined enumeration datatypes are defined in clause 6.3.2.2.

Table 6.3.2.1-1: oneM2M Simple Data Types

| XSD type name | Type Name | Examples | Description |
| --- | --- | --- | --- |
| m2m:ID | Generic ID | (TBD) | Used to represent generic IDs generated and used within oneM2M |
| m2m:nodeID | Node ID | (TBD) | Used for Node IDs. The constraints on this type are different from those on Generic IDs |
| m2m:requestID | Request ID | (TBD) | Used for Request IDs. This type includes the ID of the target CSE as well as a part that varies for each ID |
| m2m:acpType | ACP Type | (TBD) | Used to represent an AccessControlPolicy identifier. This can be either a URI or an opaque token |
| m2m:labelsType | Labels |  | A list of tokens used as keys for discovering resources |
| m2m:networkaccessID | Network Access Identifier | user@realm | The networkaccessIdentifier is a standard way of identifying users who request access to a network as specified at IETF RFC 4282 [18]. |
| m2m:mgmtLink | Management Link | mynode/cmdhPolicyInstance1 | m2m:ID restricted to allowed types of instances of resource type <mgmtObj> |
| m2m:listOfM2MID | List of M2M identifiers |  | xs:list of elements of data type m2m:ID |
| m2m:listOfEventCat | List of (applicable) Event Categories | (default bestEffort latest 1 10) | xs:list of elements of data type m2m:eventCat |
| m2m:listOfMinMax | List of Time Limits | (10 2560) | xs:list of two xs:long values defining min and max limits of time intervals in units of milliseconds (value -1 representing infinite time) |
| m2m:backOffParameters | List of Backoff Parameters | (100 100 2000) | Ordered sequence of 3 values of data type xs:nonNegativeInteger representing backoffTime, backoffTimeIncrement, maximumBackoffTime (in units of milliseconds) |
| m2m:listOfBoolean | List of allowed values in the boolean value space domain | “True“, "False“, or "True False“ | Used to define the value space of the attribute “limitsDelAggregation” by imposing restrictions on the value space of xs:boolean |

======================== END 1ST CHANGE ===========================

======================== START 2ND CHANGE ===========================

#### Complex Data Types

Table 6.3.2.3-1describes oneM2M-specific complex data type definitions.  These types are all defined to be xs:sequence complex types. XML Schema datatype definitions for these data types can be found in the XSD file called

CDT-commonTypes-v1_0_0.xsd.

In addition, each oneM2M resource has a corresponding complex data type. These are described in Clause 6.5.

Table 6.3.2.3-1: oneM2M Complex Data Types

| XSD type name | Child Elements | Child Element Datatype | Cardinality [min..max] | Description |
| --- | --- | --- | --- | --- |
| m2m:filterCriteria | createdBefore | xs:dateTime |  | Used for fc (filter criteria) parameter in a request. |
|  | createdAfter | xs:dateTime |  |  |
|  | modifiedSince | xs:dateTime |  |  |
|  | unmodifiedSince | xs:dateTime |  |  |
|  | stateTagSmaller | xs:positiveInteger |  |  |
|  | stateTagBigger | xs:nonNegativeInteger |  |  |
|  | expireBefore | xs:dateTime |  |  |
|  | expireAfter | xs:dateTime |  |  |
|  | labels | m2m:labelsType |  |  |
|  | resourceType | m2m:resourceType |  |  |
|  | sizeAbove | xs:nonNegativeInteger |  |  |
|  | sizeBelow | xs:positiveInteger |  |  |
|  | contentType | m2m:typeOfContent |  |  |
|  | limit | xs:positiveInteger |  |  |
|  | attribute | m2m:attribute |  |  |
|  | filterUsage | m2m:filterUsage |  |  |
| m2m:eventCat | eventCatType | m2m:eventCatType |  | Used for ec parameter in request and eventCat attribute of <delivery> resource. |
|  | eventCatNo | xs:nonNegativeInteger |  |  |
| m2m:deliveryMetaData | TBD |  |  | Used for deliveryMetaData attribute in <delivery> resource. |
| m2m:aggregatedRequest | TBD |  |  | Used for aggregatedRequest attribute in <delivery> resource. |
| m2m:metaInformation | TBD |  |  | Used for metaInformation attribute in <request> resource. |
| m2m:content | TBD |  |  | Used for cn parameter in request/response and content attribute in <request> resource. |
| m2m:batchNotify | number | xs:nonNegativeInteger |  | Used for batchNotify attribute in <subscription> resource. |
|  | duration | xs:duration |  |  |
| m2m:eventNotificationCriteria | createdBefore | xs:dateTime |  | Used for eventNotificationCriteria of a <subscription> resource.. |
|  | createdAfter | xs:dateTime |  |  |
|  | modifiedSince | xs:dateTime |  |  |
|  | unmodifiedSince | xs:dateTime |  |  |
|  | stateTagSmaller | xs:positiveInteger |  |  |
|  | stateTagBigger | xs:nonNegativeInteger |  |  |
|  | expireBefore | xs:dateTime |  |  |
|  | expireAfter | xs:dateTime |  |  |
|  | sizeAbove | xs:nonNegativeInteger |  |  |
|  | sizeBelow | xs:positiveInteger |  |  |
|  | resourceStatus | m2m:resourceStatus |  |  |
|  | operationMonitor | m2m:operation |  |  |
|  | Attribute | m2m:attribute |  |  |
| m2m:aggregatedNotification | singleNotification | list of m2m:singleNotification |  |  |
| m2m:singleNotification | notificationEvent | list of m2m:notificationEvent |  |  |
|  | verificationRequest | xs:boolean |  |  |
|  | subscriptionDeletion | xs:boolean |  |  |
|  | subscriptionReference | xs:anyURI |  |  |
|  | creator | m2m:ID |  |  |
|  | notificationForwardingURI | xs:anyURI |  |  |
| m2m:notificationEvent | all resource specific attributes of subscribable resource types. | data type of each attribute (This is defined in the sub-clauses of clause 7.3) |  | Used for representation of resource at notification event. |
|  | resourceStatus | m2m:resourceStatus |  |  |
|  | operationMonitor | m2m:operationMonitor |  |  |
| m2m:timestamp | xxx |  |  |  |
|  | yyy |  |  |  |
| m2m:operationMonitor | operation | m2m:operation |  |  |
|  | originator | m2m:ID |  |  |
| m2m: externalID | accessId | m2m:networkaccessIdentifier |  | The identifier of the node for the underlying network provider. In 3GPP case, the accessId is mapped to External Identifier as specified in TS 23.003 [17]. |
|  | MSISDN | xs: string |  | The identifier of the node as specified in TS 23.003 [17], |
| m2m:actionStatus | action | xs:anyURI |  | Reference to the action (represented by a resource attribute) being performed |
|  | status | m2m:status |  | Indicates the status of the operation is successful, failure or in process. See Table 6.3.2.2 1 |
| m2m:childResourceRef | (base content) | xs:anyURI | [1..1] | URI of the child resource |
|  | name (XML attribute) | xs:string | [1..1] |  |
|  | type (XML attribute) | m2m:resourceType | [1..1] |  |

NOTE: List of subscribable resource types are <accessControlPolicy>, <CSEBase>, <remoteCSE>, <AE>, <container>, <contentInstance>, <schedule>, <locationPolicy>, <delivery>, <request>, <group>, <mgmtObj>, <mgmtCmd>, <execInstance>, <node>, <m2mServiceSubscription>, <nodeInfo>, <statsConfig>, <eventConfig> and <statsCollect>

### Resource common attributes

Resource common attributes are specified in oneM2M TS-0001 [6]. The type and values shall be supported according to the description given in table 6.3.3-1.

If a Resource is represented as an XML document then the resource attributes (if present) appear in the order listed in this table. They appear before any resource-specific attributes.

Table 6.3.3-1: Resource Common Attributes

| Attribute Name | Data Type | Default | Value restrictions | Notes |
| --- | --- | --- | --- | --- |
| resourceType | m2m:resourceType | In the absence of this attribute, the resource type can be inferred from the root element |  |  |
| resourceID | m2m:ID | Not applicable |  |  |
| parentID | xs:anyURI | Not applicable | Must be a non-hierarchical URI |  |
| accessControlPolicyIDs | m2m:acpType | Policy is inherited from the parent resource |  |  |
| creationTime | xs:dateTime | Not applicable |  |  |
| expirationTime | xs:dateTime | Absence of the attribute means that the resource has no explicit expirationTime |  |  |
| lastModifiedTime | xs:dateTime | Not applicable |  |  |
| stateTag | xs:nonNegativeInteger | Not applicable |  |  |
| labels | m2m:labelsType | Absence of this attribute means there are no labels |  |  |
| Link | xs:anyURI | Absence of this attribute means that this is not an announced resource |  |  |
| announceTo | list of xs:anyURI | Absence of this attribute means that this original resource has not be announced |  |  |
| announcedAttribute | list of xs:token | Absence of this attribute means that this original resource has not be announced |  |  |

Table 6.3.3-2 describes some complex types that group together the common attributes, to be used by Resource Type definitions.

Table 6.3.3-2: Complex Data Types declaring common attributes

| XSD type name | Child Elements | Child Element Datatype | Cardinality [min..max] | Description |
| --- | --- | --- | --- | --- |
| m2m:regularResourceType | name | xs:string | [1..1] | Declares the common attributes included in the majority of non-announceable resource types. |
|  | resourceType | m2m:resourceType | [0..1] |  |
|  | resourceID | m2m:ID | [1..1] |  |
|  | parentID | xs:anyURI | [1..1] |  |
|  | accessControlPolicyIDs | m2m:acpType | [0..1] |  |
|  | creationTime | xs:dateTime | [1..1] |  |
|  | expirationTime | xs:dateTime | [1..1] |  |
|  | lastModifiedTime | xs:dateTime | [1..1] |  |
|  | stateTag | xs:nonNegativeInteger | [1..1] |  |
|  | labels | m2m:labelsType | [0..1] |  |
| m2m:announceableResourceType | name | xs:string | [1..1] | Declares the common attributes included in an announceable resource types. |
|  | resourceType | m2m:resourceType | [0..1] |  |
|  | resourceID | m2m:ID | [1..1] |  |
|  | parentID | xs:anyURI | [1..1] |  |
|  | accessControlPolicyIDs | m2m:acpType | [0..1] |  |
|  | creationTime | xs:dateTime | [1..1] |  |
|  | expirationTime | xs:dateTime | [1..1] |  |
|  | lastModifiedTime | xs:dateTime | [1..1] |  |
|  | stateTag | xs:nonNegativeInteger | [1..1] |  |
|  | labels | m2m:labelsType | [0..1] |  |
|  | link | xs:anyURI | [0..1] |  |
|  | announceTo | list of xs:anyURI | [0..1] |  |
|  | announcedAttribute | list of xs:token | [0..1] |  |
| m2m:subordinateResourceType | name | xs:string | [1..1] | Declares the common attributes used by resource types that are subordinate children of other resources |
|  | resourceType | m2m:resourceType | [0..1] |  |
|  | resourceID | m2m:ID | [1..1] |  |
|  | parentID | xs:anyURI | [1..1] |  |
|  | creationTime | xs:dateTime | [1..1] |  |
|  | lastModifiedTime | xs:dateTime | [1..1] |  |
|  | stateTag | xs:nonNegativeInteger | [1..1] |  |
|  | labels | m2m:labelsType | [0..1] |  |

======================== END 2ND CHANGE ===========================

======================== START 3RD CHANGE ===========================

## Resource Data Types

## Description

Each oneM2M Resource Data Type is defined using XML Schema (XSD), and supplied as a separate XSD document.  This XML Schema defines the attributes of the Resource in accordance with oneM2M TS-0001 [6]. It represents an entire resource, in other words if a requestor retrieves an entire resource in XML format, the XML that is returned shall be valid with respect to the schema for that resource. Note that the payload of a Create or Update request primitive does not necessarily have to be valid according to the schema, as this payload is not required to contain values for all the resource attributes. In particular a resource might contain mandatory read-only primitives, and these would not appear in a Create or Update request.

Each Resource Type will be defined in a separate XSD file. The name of that file should be prefixed with 'CDT-' and  followed by the resource type name, version of the Core Protocol TS, and date of update.

### regularResourceType

#### Description

This type definition includes the common attributes used by the majority of M2M resources. It is included  in CDT-commonTypes-v1_0_0.xsd.

#### Reference

See clause 9.6.1 of [6].

#### Usage Example

<?xml version="1.0" encoding="UTF-8"?>
<xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema"	targetNamespace=http://www.onem2m.org/xml/protocols
   xmlns:m2m=http://www.onem2m.org/xml/protocols
	elementFormDefault="unqualified" >
	<xs:include schemaLocation="common_types-v1_0_0.xsd" />

	<xs:element name="container">
		<xs:complexType>
			<xs:complexContent>
           <!-- 	Inherit Common Attributes from regularResourceType     -->
				<xs:extension base="m2m:regularResourceType">		    
					<xs:sequence>
					    <!-- 			Resource Specific Attributes           -->

<xs:element name="creator" type="m2m:ID" />
						<xs:element name="maxNrOfInstances" type="xs:nonNegativeInteger" minOccurs="0" />
						<xs:element name="maxByteSize" type="xs:nonNegativeInteger" minOccurs="0" />
						<xs:element name="maxInstanceAge" type="xs:nonNegativeInteger" 	minOccurs="0" />
						<xs:element name="currentNrOfInstances" type="xs:nonNegativeInteger" />
						<xs:element name="currentByteSize" type="xs:nonNegativeInteger" />
						<xs:element name="latest" type="xs:anyURI"  minOccurs="0" />
						<xs:element name="locationID" type="xs:anyURI" minOccurs="0" />
						<xs:element name="ontologyRef" type="xs:anyURI"  minOccurs="0" />	
						<!-- 			Child Resources                          -->
						<xs:element name="childResource" type="m2m:childResourceRef"  minOccurs="0" 
											maxOccurs="unbounded"/>	
					</xs:sequence>
				</xs:extension>
			</xs:complexContent>
		</xs:complexType>
	</xs:element>
</xs:schema>

### announceableResourceType

#### Description

This type definition includes the common attributes used by M2M resource types that are capable of being announced.  In addition to the attributes of a regularResource, It includes (as optional)  the common attributes that are used by the announcement mechanism.

#### Reference

See clause 9.6.1 of [6].

#### Usage Example

<Text>

### subordinateResourceType

#### Description

This type definition includes the common attributes used by M2M resource types that are subordinate children of other resource types (for example the Instance child of a container). It excludes attributes like expirationTime, which are not defined for such resources.

#### Reference

See clause 9.6.1 of [6].

#### Usage Example

<Text>

Editor's Note: This is example of description for each Common Data Type, and remove this  sub clause when actual entries are added.

======================== END 3RD CHANGE ===========================

# Comments

This isn’t possible, since m2m:eventCat is currently defined as a complex type. We need either to delete this whole row, or make this a list of m2m:eventCatType

It might be better to make this a complex type

It might be better to make this a complex type

I think it would be simpler to define this in the only resource that needs it (cmdhLimits)

This looks a bit odd, as eventCatType is also an integer

I don’t think that we have agreed that these are in fact the datatypes that we want

# Text boxes

<?xml version="1.0"?>

<m2m:resourceData xmlns:m2m="http://www.onem2m.org/xml/protocols">

<m2m:resourceTypeId>containerType</m2m:resourceTypeId>

<m2m:container>

<m2m:name>container1</m2m:name>

</m2m:container>

</m2m:resourceData>