| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO |
| Title:* | CoAP Option Cleanup |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-10-31 |
| Abstract:* | CoAP Option Cleanup |
| Agenda Item:* | PRO |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | Technical Specification – Core Protocol (Draft version 0.7.1) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Rationale

- URI

ARC WG has had a consensus on how to forward a request/response.

pointOfAccess will be mapped to URI of host and port, and to will be mapped to URI of path.

- Request parameter mapping

We’ve discussed where to map for request parameters. The below is analysis for which parameters can be contained in response.

The proposal is to map parameters are in response to CoAP option If parameters need to be included in the response.

|  | Parameters | mapping to | change requests proposed in this contribution |
| --- | --- | --- | --- |
| both in request and response | primitive type | n/a |  |
|  | To | Request-target |  |
|  | From | From (header) |  |
|  | request identifier originating timestamp result expiration timestamp event category | new options | define new options for these |
|  | content | Message-body |  |
| only in request | operation | Method (POST/GET/PUT/DELETE) |  |
|  | resource type | Content-Type (header) |  |
|  | name request expiration timestamp operation execution time response type result persistence result content delivery aggregation group request identifier filter criteria discovery result type | query-string | put these to query string |
| only in response | response status code | new option (also partially mapped to Response-code and Reason-phrase) | define new option |

========================Start of 1st Change==========================

## Configuration of Options and Query String

This clause describes which information needs configuring to which CoAP options or query string.

## 6.2.1	Content Format Negotiation Options

The CoAP Accept option can be used to indicate which Content-Format is acceptable to an Originator. If a Hosting CSE supports the Content-Format specified in Accept option of the request, the Hosting CSE shall respond with that Content-Format. If the Hosting CSE doesn’t support the Content-Format specified in Accept option of the request, 4.06 "Not Acceptable" MUST be sent as a response, unless another error code takes precedence for this response.

Editor’s note: which content format supported in oneM2M needs to be clarified.

## 6.2.2	Token

Due to size limitation, Request Identifier is not mapped to Token option. However, Token may be used in CoAP layer to match a CoAP request and response.

## 6.2.3	URI Options

This clause describes how to configure CoAP Uri-Host, Uri-Port, Uri-Path, and Uri-Query.

Host and port part of the address specified in pointOfAccess attribute of <remoteCSE> resource shall be mapped to Uri-Host and Uri-Port respectively.

To parameter is mapped to Uri-Path, and query strings specified in clause 6.2.4 are serialized to Uri-Query.

## 6.2.3	New Options

## 6.2.3.1	Request Identifier

## Editor’s note: detail description need to be specified

# 6.2.3.2	Originating Timestamp

# Editor’s note: detail description need to be specified

# 6.2.3.3	Result Expiration Timestamp

Editor’s note: detail description need to be specified

# 6.2.3.4	Event Category

# Editor’s note: detail description need to be specified

# 6.2.3.5	Response Status Code

Editor’s note: detail description need to be specified

## 6.2.4	Query String

From, Role, Name, Request Expiration Timestamp, Response Type, Result Persistence, Operation Execution Time, Delivery Aggregation, Group Request Identifier, Result Content, Filter Criteria, and Discovery Result Type parameters shall be carried in query string in short name form.========================End of 1st Change==========================