| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | PRO-2014-0549-6_1_1_Request_Primitive_Mapping_Cleanup |
| Source:* | Hitachi |
| Contact: | He Xuan, xhe@hitachi.cn |
| Date:* | 2014-11-01 |
| Abstract:* | This contribution proposes modification of request primitive mapping cleanup based on V0_5_0. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes CoAP protocol binding related part to TS-0008. Added part is based on PRO-2014-0540-PublicReviewComments_TS-0008_ITS-JPO.

--------------------- Start of proposed modified text -------------------

## 6.1.1	Request primitive to CoAP Request

The oneM2M request operation shall be mapped to a CoAP Method according to the table 6.1.1.-1.

The CoAP request shall be constructed using the selected CoAP method, selected options as described in options.

CoAP message includes the 8-bit Code.  In case of a request, the Code field indicates the Request Method.  The Code field is limited to indicate all oneM2M request code, so additional information should be carry via the CoAP payload field.

CoAP defines a single set of options that are used in both requests and responses.  In case of a request, if CoAP defined options is limited to indicate all oneM2M options, additional information should be carry in the CoAP payload field.

Table 6.1.1-1: oneM2M Operation Mapping

| oneM2M Operation | CoAP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT |
| Delete | DELETE |
| Notify | POST |

In the case of mapping oneM2M operations to CoAP method POST, operations shall be presented via the op parameter:

The determination between the Create and Notify operations can be done by the given CoAP datatype.

The CoAP request shall be constructed using selected method, selected options as described in options.  As CoAP options are limited, sometimes additional information is carried in CoAP payload field.

--------------------- End of proposed modified text ---------------------