| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | PRO-2014-0550-6_3_Response_Code_Mapping_Cleanup |
| Source:* | Hitachi |
| Contact: | He Xuan, xhe@hitachi.cn |
| Date:* | 2014-11-01 |
| Abstract:* | This contribution proposes modification of response code mapping cleanup based on V0_5_0. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes CoAP protocol binding related part to TS-0008.

--------------------- Start of proposed modified text -------------------

## 6.3	Response Codes Mapping

## 6.3.1	Response Primitive to CoAP Response

The response primitive shall be correlated to the corresponding request primitive and the following rules shall be followed:

- The CoAP response shall be correlated to the CoAP request corresponding to the request primitive.

- If the response primitive has any resource representation, this shall be transported in the payload of the CoAP response.

- The status code of the response for successful and unsuccessful response shall be set according to the table below.

If the request is send from originator, Table 6.3.1-1 shall be used for mapping as successful cases, and Table 6.3.1-2 shall be used for unsuccessful cases:

# Table 6.3.2-1 Successful Cases

| Status Code | Status Code of CoAP |
| --- | --- |
| STATUS_CREATED | 2.01 Created |
| STATUS_ DELETED | 2.02 Deleted |
| STATUS_CHANGED | 2.04 Changed |
| STATUS_CONTENT | 2.05 Content |
| STATUS_ACCEPTED | ACK |

# Table 6.3.2-2 Unsuccessful Cases

| Numeric Code | Description | Status Code of CoAP | Description |
| --- | --- | --- | --- |
| 2000 | Location info not authorized | 4.01 | Unauthorized |
| 2001 | Unsupported resource | 5.01 | Not Implemented |
| 2002 | Unsupported attribute | 5.01 | Not Implemented |
| 2003 | Target not reachable | 5.05 | Proxying Not Supported |
| 2004 | Cannot forward, other reason | 5.00 | Internal Server Error |
| 2005 | No privilege | 4.01 | Unauthorized |
| 2006 | Already exists | 4.12 | Precondition Failed |
| 2007 | Create error - missing mandatory parameter | 4.02 | Bad Option |
| 2009 | Does not exist | 4.04 | Not Found |
| 2012 | Update error - unacceptable contents | 4.06 | Not Acceptable |
| 2015 | Create delivery - not able to take on responsibility | 4.01 | Unauthorized |
| 2016 | Group request identifier exists | 4.12 | Precondition Failed |
| 2022 | External Object not reachable | 5.02 | Bad Gateway |
| 2023 | Create mgmtObj - memory shortage | 4.13 | Request Entity Too Large |
| 2028 | External Object not found | 4.04 | Not Found |
| 2031 | Cancel execInstance - not cancellable | 4.03 | Forbidden |
| 2032 | Cancel execInstance - already complete | 4.00 | Bad Request |
| 2033 | Delete execInstance - not cancellable | 4.03 | Forbidden |
| 2034 | Delete execInstance - already complete | 4.00 | Bad Request |
| 2035 | Retrieve CSEBase - format error | 4.15 | Unsupported Content-Format |
| 2036 | CMDH rules -non compliant | 4.00 | Bad Request |
| 2037 | Target is not subscribable | 4.05 | Method Not Allowed |
| 2038 | Cannot initiate subscription verification | 5.03 | Service Unavailable |
| 2039 | Subscription verification failed - Originator | 5.03 | Service Unavailable |
| 4040 | Subscription verification failed - Creator | 4.00 | Bad Request |
| 2040 | Max number of member exceeded | 4.00 | Bad Request |
| 2041 | Member type inconsistent | 4.00 | Bad Request |
| 2042 | Management session cannot be established | 5.03 | Service Unavailable |
| 2043 | Management session establishment timeout | 5.04 | Gateway Timeout |

## 6.3.2	CoAP Response Code to oneM2M Response Code

If the CoAP response code is in the range 2.01 to 2.05, then the response shall be considered as a successful case. Table 6.3.2-1 shall be used for successful cases mapping.

Table 6.3.2-1 Successful Cases

| CoAP Response Code | oneM2M Response Code | Note |
| --- | --- | --- |
| Success 2.xx | 2.01 Created | STATUS_CREATED |  |
|  | 2.02 Deleted | STATUS_ DELETED |  |
|  | 2.03 Valid | - | Same as HTTP304 Not Modified |
|  | Changed | STATUS_CHANGED |  |
|  | 2.05 Content | STATUS_CONTENT |  |

If the CoAP response code is in the range of 4.00 to 4.15 or 5.00 to 5.05, then the response shall be considered as unsuccessful. Table 6.3.2-2 shall be used for unsuccessful cases mapping. Additional information about the error should be included.

Table 6.3.2-2 Successful Cases

| CoAP Response Code | oneM2M Response Code(Description) | Note |
| --- | --- | --- |
| Client error | 4.00 | 2032( Cancel execInstance - already complete) 2034 (Delete execInstance - already complete) 2036 (CMDH rules -non compliant) 4040 ( Subscription verification failed – Creator) 2040 (Max number of member exceeded) 2041 (Member type inconsistent) | 4.00 shall be used for multiple response, depends on parameters in additional information |
|  | 4.01 | 2000( Location info not authorized) 2005( No privilege) 2015 (Create delivery - not able to take on responsibility) | 4.01 shall be used for multiple response, depends on parameters in additional information |
|  | 4.02 | 2007 (Create error - missing mandatory parameter) |  |
|  | 4.03 | 2031 (Cancel execInstance - not cancellable) 2033 (Delete execInstance - not cancellable) | 4.03 shall be used for multiple response, depends on parameters in additional information |
|  | 4.04 | 2009 (Does not exist) 2028 (External Object not found) | 4.04 shall be used for multiple response, depends on parameters in additional information |
|  | 4.05 | 2037 (Target is not subscribable) |  |
|  | 4.06 | 2012 (Update error - unacceptable contents) |  |
|  | 4.12 | 2006 (Already exists) 2016 (Group request identifier exists) | 4.12 shall be used for multiple response, depends on parameters in additional information |
|  | 4.13 | 2023 (Create mgmtObj - memory shortage) |  |
|  | 4.15 | 2035 (Retrieve CSEBase - format error) |  |
| Server error | 5.00 | 2004 (Cannot forward, other reason) |  |
|  | 5.01 | 2001 (Unsupported resource) 2002 (Unsupported attribute) | 5.01 shall be used for multiple response, depends on parameters in additional information |
|  | 5.02 | 2022 (External Object not reachable) |  |
|  | 5.03 | 2038 (Cannot initiate subscription verification) 2039 (Subscription verification failed – Originator) 2042 (Management session cannot be established) | 5.03 shall be used for multiple response, depends on parameters in additional information |
|  | 5.04 | 2043 (Management session establishment timeout) |  |
|  | 5.05 | 2003 (Target not reachable) |  |

## 6.3.3	Additional Information

CoAP message includes the 8-bit Code.  In case of a request, the Code field shall indicate the Request Method; in case of a response, the Code field shall indicate a Response Code.

The Code field is limited to indicate all oneM2M response code, so additional information shall be carried via the CoAP payload field.

--------------------- End of proposed modified text ---------------------