| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | CR-Introduction of oneM2M procedures |
| Source:* | Institut Mines-Telecom |
| Contact: | Soochang Park, IMT, soochang.park@telecom-sudparis.eu Noel Crespi, IMT, noel.crespi@mines-telecom.fr Rebecca Copeland, IMT, rebecca.copeland.uk@gmail.com Eric Farnier, ECOMETERING, eric.farnier@gdfsuez.com |
| Date:* | 2014-11-12 |
| Abstract:* | This contribution provides the description for the protocol design principles and requirements to include the proposed text in Section 7 of the TS-0004 (oneM2M Core Protocol Specification). |
| Agenda Item:* | 6 |
| Work item(s): | WI 009, oneM2M Protocol Development |
| Document(s) Impacted* | oneM2M TS-0004, oneM2M Core Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To include the proposed text in the TS |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- providing introduction for section 7 to show summary of all work in section 7

- R01: putting more specific contents to introduce section 7

---------------------------- Start of change 1 ---------------------------------

# oneM2M Procedures

## Introduction

The following clauses describe prerequisites such as primitive format and procedure outline with three generic scenarios that are Originator, Receiver, and Resource Handling in accordance with CRUD+N operations. In addition, for specific resource type they provide common or resource specific attributes, data type definition for the attributes, and child resources as well as they explain resource specific procedures on CRUD operations to communicate with oneM2M compliant M2M Platform System by oneM2M protocols and APIs as follows:

- Primitive formats and generic procedures

- Common operations

- Resource type-specific definitions and procedures

- Notification definition and procedures

---------------------------- End of change 1 ---------------------------------

---------------------------- Start of change 2 ---------------------------------

## Resource Type-specific procedures and definitions

The following sub-clauses describe operation applicability of each resource type defined in clause 10.2 Resource Type-Specific Procedures [6] on reference points.

---------------------------- End of change 2 ---------------------------------

### Resource Type accessControlPolicy

#### Introduction

The <accessControlPolicy> resource is comprised of  privileges and selfPrivileges attributes which represent a set of access control rules  defining which entities (defined as accessControlOriginators) have the privilege to perform  certain operations (defined as accessContolOperations) within specified contexts (defined as accessControlContexts) and are used by the CSEs in making access decision to specific resources.

The detailed description can be found in clause 9.6.2 in Architecture TS [6].