| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | FUJITSU |
| Format:* | Face-to-Face Meeting |
| Date:* | 2014-11-09 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitus.com |
| Reason for Change/s:* | Notification handling is better to be specified separately. |
| CR against: Release* | v.0.7.2 |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The content attribute of the contentInstance resource will be specified string value, but original data may in different forms, e.g. binary, base64-encoded binary, and string.

Data type of m2m:encoding should be specified.

Example for proposed notification message format is:

<notification>

<creator>com.fujitsu.ems.hems-app1</creator>

<target>http://m2m.example.com/api/cl1</target>

<source>http://m2m.example.com/hems/home1</source>

<time>20141102T112030</time>

<event>

<originator>http://m2m.example.com/hems/home1/data1</originator>

<operation>CREATE</operation>

</event>

<reportError>false</reportError>

</notification>

and its XSD looks like:

<?xml version="1.0"?>

<xsd:schema xmlns:xsd="http://www.w3.org/2001/XMLSchema">

<xsd:element name="notification">

<xsd:complexType>

<xsd:sequence>

<xsd:element name="creator" type="m2m:ID"/>

<xsd:element name="target" type="xsd:anyURI"/>

<xsd:element name="source" type="xsd:anyURI"/>

<xsd:element name="event">

<xsd:complexType>

<xsd:choice>

<xsd:element name="resource" type="m2m:resourceTypeData"/>

<xsd:element name="resourceStatus" type="m2m:resourceStatus"/>

<xsd:sequence>

<xsd:element name="originator" type="xsd:anyURI"/>

<xsd:element name="operation" type="m2m:operation"/>

</xsd:sequence>

</xsd:choice>

</xsd:complexType>

</xsd:element>

</xsd:sequence>

<xsd:element name="reportError" type="xsd:boolean"/>

</xsd:complexType>

</xsd:element>

</xsd:schema>

### -----------------------Start of change 1-------------------------------------------

### -----------------------End of change 1---------------------------------------------

#### 7.2.2.x Notificaiton Handling

##### 7.2.2.x.1 Forwarding Notification

If the Reciever of the notification message is neither the Receiver CSE nor AE registered on the Receiver CSE, the notification message shall be forwarded to next-hop CSE on the path to deliver the message to the final destination.

NOTE: the determination of next-hop CSE for the message delivery is out-of-scope in TS-00004 of present release.

##### 7.2.2.x.2 Receive Notification

If the Receiver of the notification message is either the Receiver CSE or the AE which is registered on the CSE, the Receiver CSE shall check the syntax of message.

If the syntax check failed, the Reciever CSE shall return the response primitive as BAD_REQUEST, otherwise the Receiver CSE shall return the response primitive as ACK_REQUEST_RECEIVED.

Then, the Reciever CSE shall process the local procesures triggered by the received notification message.

When the local procedure results failure and required to report the result to Originator of the notification message, the Receiver CSE compose NOTIFY request primitive with responseStatus as content parameter.

NOTE: See clause 7.2.2.x.3 for further procedures regarding local procedures when the notification message is targeted to registered AE.

##### 7.2.2.x.3 Re-targeting Notification

When the Receiver of the notification message is AE which is registered on the Receiver CSE, following re-targeting notification shall be performed as local procedure on the Reciever CSE.

check existence of <pollingChannel> resource in <AE> resource of retargeting. If it exist, the message are queued to be fetched later through <pollingChannel> resource. When the message was succuessfully stored in the queue, the local procedure is regarded as successfully processed.

If <pollingChannel> resource does not exist, the Receiver CSE shall try to forward the notification message to one of the pointOfAccess in order until either successfully received on one of point of access, or failed on all of them.

In case of failure on delivery, and required to report the result to Originator of the notification message, the Receiver CSE compose NOTIFY request primitive reporting ‘notification target does not exist’ error.

##### 7.2.2.x.4 Aggregate Notifications

(TBD)

### -----------------------Start of change 2-------------------------------------------

### -----------------------End of change 2---------------------------------------------

#### m2m:batchNotify

Used for batchNotify attribute in <subscription> resource.

Table 6.3.4.7-1: Type Definition of m2m:batchNotify

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| number | xs:nonNegativeInteger |  |  |
| duration | xs:duration |  |  |

#### m2m:eventNotificationCriteria

Used for eventNotificationCriteria of a <subscription> resource.

Table 6.3.4.8-1:Type Definition of m2m:eventNotificationCriteria

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| createdBefore | xs:dateTime |  |  |
| createdAfter | xs:dateTime |  |  |
| modifiedSince | xs:dateTime |  |  |
| unmodifiedSince | xs:dateTime |  |  |
| stateTagSmaller | xs:positiveInteger |  |  |
| stateTagBigger | xs:nonNegativeInteger |  |  |
| expireBefore | xs:dateTime |  |  |
| expireAfter | xs:dateTime |  |  |
| sizeAbove | xs:nonNegativeInteger |  |  |
| sizeBelow | xs:positiveInteger |  |  |
| resourceStatus | m2m:resourceStatus |  |  |
| operationMonitor | m2m:operation |  |  |
| Attribute | m2m:attribute |  |  |

#### m2m:aggregatedNotification

Table 6.3.4.9-1: Type Definition of m2m:aggregatedNotification

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| notifications | xsd:complexType | 1 |  |

#### m2m: notification

Table 6.3.4.10-1: Type Definition of m2m: notification

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| creator | m2m:ID | 0..1 | creator information other than source (ex. APP-ID) |
| target | xs:anyURI | 1 | Receiver of notification |
| source | xs:anyURI | 1 | Originator of notification |
| time | m2m:timestamp | 1 | The timestamp of event occured |
| event | xsd:complexType choice of resourceData, resourceStatus, operationMonitor, or responceStatus | 1 |  |
| event/resource | choice of oneM2M resourceTypes | 0..1 |  |
| event/resourceStatus | m2m:resourceStatus | 0..1 |  |
| event/operation | m2m:operation | 0..1 | sequence with originator |
| event/originator | m2m:id | 0..1 | sequence with operation |
| reportError | xs:boolean | 0..1 | optionally specified to request failure report to Originator |

### -----------------------Start of Changes to References Section -------------