| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO |
| Title:* | CoAP Operation Mapping |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-11-14 |
| Abstract:* | CoAP Operation Mapping |
| Agenda Item:* | PRO |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | Technical Specification – CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Rationale

Since WG3 decides not to add ‘notification’ resource type, it reflects that decision.

========================Start of 1st Change==========================

## 6.1.1	Request primitive to CoAP Request

The oneM2M request operation shall be mapped to a CoAP Method according to the table 6.1.1.-1.

The CoAP request shall be constructed using the selected CoAP method, selected options as described in options.

CoAP message includes the 8-bit Code.  In case of a request, the Code field indicates the Request Method.  The Code field is limited to indicate all oneM2M request code, so additional information should be carry via the CoAP payload field.

CoAP defines a single set of options that are used in both requests and responses.  In case of a request, if CoAP defined options is limited to indicate all oneM2M options, additional information should be carry in the CoAP payload field.

Table 6.1.1-1: oneM2M Operation Mapping

| oneM2M Operation | CoAP Method |
| --- | --- |
| CREATE | POST |
| RETRIEVE | GET |
| UPDATE | PUT |
| DELETE | DELETE |
| NOTIFY | POST |

At the Receiver, CoAP request message with POST method shall be mapped to oneM2M CREATE or NOTIFY operation in accordance with the existence of resourceType parameter;  If resourceType parameter exists, then the operation is CREATE and if resourceType parameter doesn’t exist, the operation is NOTIFY.

========================End of 1st Change==========================