| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 14.2bis |
| Source:* | FUJITSU |
| Date:* | 2015-01-05 |
| Contact:* | Shingo Fujimoto, FUJITSU, Shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | From header is not appropriate use |
| CR against: Release* | 1.0 (DRAFT) |
| CR against: TS/TR* | TS-0009-V0.6.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

From header in HTTP/1.1 should be specified "mailbox" which is strictly defined in RFC.

5.5.1.  From

The "From" header field contains an Internet email address for a

human user who controls the requesting user agent.  The address ought

to be machine-usable, as defined by "mailbox" in Section 3.4 of

[RFC5322]:

In short word, mailbox should look like "<user-id>@<domain>" which is not compatible with oneM2M IDs.

Another problem is validation on the header by Reciver CSE.

The current specification does not explain how to prevent the Originator from faking its identity on the From parameter.

In case of TLS-PSK or Client Certificate based authentication is applied, there are not any way to verify the identity of the Originator when the message has been forwarded to other CSEs.

From above reasonings, this contribution proposed to introduced "X-M2M-Origin" HTTP header to indidate the identity of Originator and who verified it.

X-M2M-Origin header should not be specified by AE, but end-point CSE shall add  it when the identity is verified.

### -----------------------Start of change 1-------------------------------------------

### 6.4.7	Location

The Location header shall be mapped to the URI of the created resource. This header shall be present in the response primitive corresponding to a create request and shall not be present in any other request or response.

### 6.4.8	X-M2M-Origin

The X-M2M-Origin header shall be mapped to the From parameter of the request/response primitive.

The X-M2M-Origin header shall be added by the CSE which verified the Originator's identity.

Note: The verification of Originator's identity can be achieved by checking credential of the Registrar CSE when the Registree AE are not required to be authorized by the Registrar CSE.

The mapping between credential and CSE/AE-ID is up to the implementation.

The choiceof verification method is assumed that both Originator and Receiver is pre-configured during provisioning process in Release-1 specification.

When Receiver CSE detect addition of X-M2M-Origin header by un-authorized CSE, the message shall be rejected as status of STATUS_PRECONDITION_FAILED.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?