| CHANGE REQUEST |
| --- |
| Meeting:* | WG3 Protocol – PRO |
| Source:* | Ericsson |
| Date:* | TP 16 |
| Contact:* | 2015-03-15 |
| Reason for Change/s:* | George Foti |
| CR against: Release* | V1.0.1 |
| CR against: WI* | MNT/WI-0004 |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* | Annex A |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Annex A intrdocues the Diameter binding for the Mch interface

## -------Start  of First change---------------------------

## 5.2  Introduction

The oneM2M architecture is resource-based (oneM2M TS-0001 Functional Architecture [6]). The functionality of the system is exposed by means of APIs over all reference points specified in oneM2M TS-0001 Functional Architecture [6]. Operations upon resources hosted by a CSE are carried over an established channel that constitutes the communication on the reference points Mca and Mcc. All API operations could be fulfilled with the considerations in terms of scalability, extensibility, fault tolerance and robustness, energy efficiency, and self-operation.

For details of the Use of Offline Charging on the Mch see Annex

Each resource operation comprises a pair of primitives: Request and Response.

In order to provide a well-defined interface for the reference points in oneM2M TS-0001 [6] Functional Architecture, the following aspects need to be provided:

the collection of primitives carried over a specific reference point; and

the definitions and procedures of resource types in relation to the underlying protocols and reference points involved.

The current document provides:

Protocol design principles and requirements

Data type definitions;

Primitive definitions; and

XML definitions and schema.

NOTE:	The actual binding of the interface to a specific protocol is not part of the present document, but is specified in a separate Technical Specifications [22], [23],[24].

In accordance with the oneM2M architecture, each reference point is applicable to a wide range of underlying network technologies and transport protocols. oneM2M defines a set of bindings for specific underlying network technologies and transport protocols, these bindings are not limiting the applicability of the interfaces when used in other underlying networks and transport protocols. However, the behaviour of the interface needs to be respected in accordance to the present document and oneM2M TS-0001 Functional Architecture [6].

## -------End  of First change---------------------------

## -------Start  of Second change---------------------------

(Normative):
Binding Mch to Diameter for Charging

Diameter Commands on Mch

Accounting Request Command

The ACR command is sent from the Charging Function (CHF included within the SCA CSF) embedded within the M2M IN to the Charging Server using the Mch reference point. This command isused for Event Based requests.

The ACR message format is defined according to the Diameter Base Protocol in RFC 3588 [13]  as follows:

<ACR> ::= < Diameter Header: 271, REQ, PXY >

< Session-Id >

{ Origin-Host }

{ Origin-Realm }

{ Destination-Realm }

{ Accounting-Record-Type }

{ Accounting-Record-Number }

[ Acct-Application-Id ]

[ Destination-Host ]

[ Origin-State-Id ]

[ Event-Timestamp ]

* [ Proxy-Info ]

* [ Route-Record ]

[ Service-Context-Id ]

[ Service-Information ]

* [ AVP ]

Accounting Answer Command

The ACR command is sent from the Charging Server to the Charging Function (CHF included within the SCA CSF) embedded within the M2M IN in response to the ACR command and is used to acknowledge reception of the charging data. This command is used for Event Based responses.

The ACA message format is defined according to the Diameter Base Protocol in RFC 3588 [13] as follows:

<ACA> ::= < Diameter Header: 271, PXY >

< Session-Id >

{ Result-Code }

{ Origin-Host }

{ Origin-Realm }

{ Accounting-Record-Type }

{ Accounting-Record-Number }

[ Acct-Application-Id ]

[ User-Name ]

[ Origin-State-Id ]

[ Event-Timestamp ]

* [ Proxy-Info ]

* [ AVP ]

Mapping of M2M Recorded Information Elements to AVPs

The following table describes the mapping of the M2M Recorded Information Elements identified in TS-0001 to the Diameter AVPs.

| M2M Recorded Information Elements | Diameter AVP |
| --- | --- |
| M2M Service Subscription Identifier | Subscription-Id |
| Application Entity ID | Application-Entity-ID |
| External ID | External-ID |
| Receiver | Receiver |
| Issuer | Issuer |
| Hosting CSE-ID | Hosting-CSE-ID |
| Target ID | Target-ID |
| Protocol Type | Protocol-Type |
| Request Operation | Request-Operation |
| Request Headers size | Request-Headers-Size |
| Request Body size | Request-Body-Size |
| Response Headers size | Response-Headers-Size |
| Response Body size | Response-Body-Size |
| Response Code | Response-Status-Code |
| Time Stamp | M2M-Event-Record-Timestamp |
| M2M-Event-Record-Tag | Rating-Group |
| Control Memory Size | Control-Memory-Size |
| Data Memory Size | Data-Memory-Size |
| Access Network Identifier | Access-Network-Identifier |
| Additional Information | AVP |
| Occupancy | Occupancy |
| Group Name | Group-Name |
| maxNrOfMembers | Maximum-Number-Members |
| currentNrOfMembers | Current-Number-Members |
| Subgroup Name | Subgroup-Name |
| M2M-Node-Id | Node-Id |

Summary of AVPs used

The following table lists the Diameter AVPs specifically used for the offline charging interface.

In Table A.3-1, columns “Used in ACR” and “Used in ACA” identify at a protocol level if the AVP is mandatory, optional, or not allowed. When identified as optional here, an AVP may be considered mandatory for certain conditions as identified in Table 12.1.2.2-1 of TS-0001 [6].

The table contains the following information:

-	AVP Name: The name used in Diameter.

-	AVP Vendor ID: The entity defining the AVP code in the next column.

-	AVP Code: The AVP Code used in the Diameter AVP Header.

-	Used in ACR: Indicates if it is mandatory, optional or not used in the ACR command.

-	Used in ACA: Indicates if it is mandatory, optional or not used in the ACA command.

-	Used in CCR: Not in this release.

-	Used in CCA: Not in this release.

-	AVP Defined: A reference to where this AVP is defined.

-	Value Type: The Diameter format of the AVP data as defined in Basic or Derived AVP Data Format.

-	AVP Flag Rules: The rules for how the AVP Flags in the AVP Header may be set.

-	May Encrypt: Indicates if the AVP may be encrypted or not.

# Table A.3-1: Use Of Diameter AVPs

| AVP Name | AVP Vendor Id | AVP Code | Used in | Reference | Value Type | AVP Flag rules |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | ACR | ACA | CCR | CCA |  |  | Must | May | Should not | Must not | May Encr. |
| Access-Network-Identifier | ETSI | XXXX | O | - | - | - | [A.4.1] | Unsigned32 | M | P | - | V | Y |
| Acct-Application-Id | 0 | 259 | O | O | - | - | [5.4.1] | Unsigned32 | M | P | - | V | N |
| Accounting-Record-Number | 0 | 485 | M | M | - | - | RFC 3588 [13] | Unsigned32 | M | P | - | V | Y |
| Accounting-Record-Type | 0 | 480 | M | M | - | - | [5.4.2] | Enumerated | M | P | - | V | Y |
| Application-Entity-ID | ETSI | xxxx | O | - | - | - | [A.4.2] | UTF8String | M | P | - | V | Y |
| AVP | * | * | O | - | - | - | * | * |  |  |  |  |  |
| Control-Memory-Size | ETSI | XXXX | O | - | - | - | [A.4.5] | Unsigned32 | M | P | - | V | Y |
| Current-Number-Members | ETSI | XXXX | O | - | - | - | [A.4.6] | Unsigned32 | M | P | - | V | Y |
| Data-Memory-Size | ETSI | XXXX | O | - | - | - | [A.4.7] | Unsigned32 | M | P | - | V | Y |
| Destination-Host | 0 | 293 | O | - | - | - | RFC 3588 [13] | DiamIdent | M | P | - | V | N |
| Event-Timestamp | 0 | 55 | O | O | - | - | RFC 3588 [13] | Time | M | P | - | V | N |
| External-ID | ETSI | Xxxx | O | - | - | - | [A.4.8] | UTF8String | M | P | - | V | Y |
| Group-Name | ETSI | XXXX | O | - | - | - | [A.4.9] | UTF8String | M | P | - | V | Y |
| Hosting-CSE-ID | ETSI | Xxxx | O | - | - | - | [A.4.10] | UTF8String | M | P | - | V | Y |
| Issuer | ETSI | Xxxx | M | - | - | - | [A.4.11] | UTF8String | M | P | - | V | Y |
| Maximum-Number-Members | ETSI | XXXX | O | - | - | - | [A.4.12] | Unsigned32 | M | P | - | V | Y |
| M2M-Event-Record-Timestamp | ETSI | XXXX | M | - | - | - | [A.4.13] | Time | M | P | - | V | Y |
| M2M-Information | ETSI | Xxxx | M | - | - | - | [A.4.14] | Grouped | M | P | - | V | Y |
| Node-Id | 10415 | 2064 | M | - | - | - | TS 32.299 [29] | UTF8String | V,M | P | - | - | N |
| Occupancy | ETSI | XXXX | O | - | - | - | [A.4.16] | Unsigned32 | M | P | - | V | Y |
| Origin-Host | 0 | 264 | M | M | - | - | RFC 3588 [13] | DiamIdent | M | P | - | V | N |
| Origin-Realm | 0 | 296 | M | M | - | - | RFC 3588 [13] | DiamIdent | M | P | - | V | N |
| Origin-State-Id | 0 | 278 | O | O | - | - | RFC 3588 [13] | Unsigned32 | M | P | - | V | N |
| Protocol-Type | ETSI | XXXX | O | - | - | - | [A.4.17] | Enumerated | M | P | - | V | Y |
| Proxy-Info | 0 | 284 | O | O | - | - | RFC 3588 [13] | Grouped | M | - | - | P,V | N |
| Rating-Group | 0 | 432 | O | - | - | - | RFC 4006 [30] | Unsigned32 | M | P | - | V | Y |
| Receiver | ETSI | XXXX | O | - | - | - | [A.4.19] | UTF8String | M | P | - | V | Y |
| Request-Body-Size | ETSI | XXXX | O | - | - | - | [A.4.20] | Unsigned32 | M | P | - | V | Y |
| Request-Headers-Size | ETSI | XXXX | O | - | - | - | [A.4.21] | Unsigned32 | M | P | - | V | Y |
| Request-Operation | ETSI | XXXX | O | - | - | - | [A.4.22] | Enumerated | M | P | - | V | Y |
| Response-Body-Size | ETSI | XXXX | O | - | - | - | [A.4.23] | Unsigned32 | M | P | - | V | Y |
| Response-Headers-Size | ETSI | XXXX | O | - | - | - | [A.4.24] | Unsigned32 | M | P | - | V | Y |
| Response-Status-Code | ETSI | XXXX | O | - | - | - | [A.4.25] | Enumerated | M | P | - | V | Y |
| Result-Code | 0 | 268 | - | M | - | - | RFC 3588 [13] | Unsigned32 | M | P | - | V | N |
| Route-Record | 0 | 282 | O | - | - | - | RFC 3588 [13] | DiamIdent | M | - | - | P,V | N |
| Service-Context-Id | 0 | 461 | O | - | - | - | [A.4.26] | Grouped | M | P | - | V | N |
| Service-Information | 10415 | 873 | O | - | - | - | 32.299 [29] | Grouped | M | P | - | V | N |
| Session-Id | 0 | 263 | M | M | - | - | RFC 3588 [13] | UTF8String | M | P | - | V | Y |
| Subgroup-Name | ETSI | XXXX | O | - | - | - | [A.4.28] | UTF8String | M | P | - | V | Y |
| Subscription-Id | 0 | 443 | M | - | - | - | RFC 4006 [30] | Grouped | M | P | - | V | Y |
| Subscription-Id-Data | 0 | 444 | M | - | - | - | RFC 4006 [30] | UTF8String | M | P | - | V | Y |
| Subscription-Id-Type | 0 | 450 | M | - | - | - | RFC 4006 [30] | Enumerated | M | P | - | V | Y |
| Target-ID | ETSI | XXXX | O | - | - | - | [A.4.32] | UTF8String | M | P | - | V | Y |

OneM2M Specific AVP Usage

Access-Network-Identifier AVP

The Access-Network-Identifier AVP (AVP Code xxxx) is of type Unsigned32 and identifies the access network associated with the request triggering the M2M Event Record. The IN-CSE detects the link on which a request came from or was  sent to and that link maps to a specific Network and locally configured identifier.

Acct-Application-Id AVP

Since the protocol used on Mch is Diameter Accounting, this AVP shall contain the value of 3 as defined in RFC 3588 [1].

Accounting-Record-Type AVP

The Accounting-Record-Type AVP (AVP Code 480) is of type Enumerated and contains the type of accounting record being sent. The following value is currently defined for the Accounting-Record-Type AVP: EVENT_RECORD (value 1) for an Event Based request.

Application-Entity-ID AVP

The Application-Entity-ID AVP (AVP Code xxxx) is of type UTF8String and represents the identity of the M2M Application Entity when it is applicable. The format of the AE-ID is specified in clause 6.2.2.

Control-Memory-Size AVP

The Control-Memory-Size AVP (AVP Code xxxx) is of type Unsigned32 and represents the storage memory (in bytes) used to store control related information associated with the M2M event record (excludes data storage associated with container related operations).

Current-Number-Members AVP

The Current-Number-Members AVP (AVP Code xxxx) is of type Unsigned32 and represents the current number of members in a group as determined by the responses to a request transmitted to a group. This is the same as the attribute “currentNrOfMembers” for the group as described in Table 7.3.13.1-3.

Data-Memory-Size AVP

The Data-Memory-Size AVP (AVP Code xxxx) is of type Unsigned32 and represents the storage memory in bytes, where applicable, to store data  associated with container related operations.

External-ID AVP

The External-ID AVP (AVP Code xxxx) is of type UTF8String and contains the external ID used to communicate over Mcn where applicable. The format is the same as the M2M-Ext-ID in clause 6.2.

Group-Name AVP

The Group-Name AVP (AVP Code xxxx) is of type UTF8String and identifies the group associated with a request. It shall be included when the IN initiates a fanning operation. This is the same as the attribute “groupName” for the group as described in Table 7.3.13.1-3.

Hosting-CSE-ID AVP

The Hosting-CSE-ID AVP (AVP Code xxxx) is of type UTF8String and represents the identity of the hosting CSE for the request in case the receiver is not the host. The format of the CSE-ID is specified in clause 6.2.2.

Issuer AVP

The Issuer AVP (AVP Code xxxx) is of type UTF8String and identifies the issuer (i.e., from party) of the M2M request. This can be any M2M Node with format as per clause 6.2.2.

Maximum-Number-Members AVP

The Maximum-Number-Members AVP (AVP Code xxxx) is of type Unsigned32 and represents the maximum number of members of the group for the Create and Update operations. This is the same as the attribute “maxNrOfMembers” for the group as described in Table 7.3.13.1-3.

M2M-Event-Record-Timestamp AVP

The M2M-Event-Record-Timestamp AVP (AVP code xxxx) is of type Time and represents the time for recording the M2M event record.

M2M-Information AVP

The M2M-Information AVP (AVP code xxxx) is of type Grouped. Its purpose is to allow the transmission of service information elements used for OneM2M specific charging.

It has the following ABNF grammar:

M2M-Information :: = 	< AVP Header: xxxx>

[ Application-Entity-ID ]

[ External-ID ]
[ Receiver ]
[ Issuer ]
[ Hosting-CSE-ID ]
[ Target-ID ]
[ Protocol-Type ]
[ Request-Operation ]
[ Request-Headers-Size ]
[ Request-Body-Size ]
[ Response-Headers-Size ]
[ Response-Body-Size ]
[ Response-Status-Code ]
[ Rating-Group ]

[ M2M-Event-Record-Timestamp ]
[ Control-Memory-Size ]
[ Data-Memory-Size ]
[ Access-Network-Identifier ]
[ Occupancy ]
[ Group-Name ]
[ Maximum-Number-Members ]
[ Current-Number-Members ]
[ Subgroup-Name ][ Node-Id ]

* [ AVP ]

Node-ID AVP

The Node-Id AVP (AVP Code 2064) is of type UTF8String and includes an optional, operator configurable identifier string for the node generating the Accounting-Record-Number for the Diameter ACR.

Occupancy AVP

The Occupancy AVP (AVP Code XXXX) is of type Unsigned32 and represents the overall size (in bytes) of the containers generated by a set of AEs identified by the M2M Service Subscription Identifier

Protocol-Type AVP

The Protocol-Type AVP (AVP Code XXXX) is of type Enumerated and indicates the protocol used for the request. The values are given below:

0	HTTP

1	CoAP

3 .. 99	Reserved for OneM2M defined protocol types

100 .. 199	Operator and vendor specific protocol types

Rating-Group AVP

The Rating-Group AVP (AVP Code 432) is of type Unsigned32 and represents a classification of M2M event records for charging purposes. This is assigned by the IN and is M2M SP specific.

Receiver AVP

The Receiver AVP (AVP Code xxxx) is of type UTF8String and identifies the receiver (i.e., to party) of the M2M request. This can be any M2M Node with format as per clause 6.2.2.

Request-Body-Size AVP

The Request-Body-Size AVP (AVP Code xxxx) is of type Unsigned32 and represents the number of bytes of the body transported in the Request.

Request-Headers-Size AVP

The Request-Headers-Size AVP (AVP Code xxxx) is of type Unsigned32 and represents the number of bytes in the control information header in the Request.

Request-Operation AVP

The Request-Operation AVP (AVP Code xxxx) is of type Enumerated and identifies the type of operation requested. The values are defined in Table 6.3.3.2.5-1.

Response-Body-Size AVP

The Response-Body-Size AVP (AVP Code xxxx) is of type Unsigned32 and represents the number of bytes of the body transported in the Response.

Response-Headers-Size AVP

The Response-Headers-Size AVP (AVP Code xxxx) is of type Unsigned32 and represents the number of bytes in the control information header in the Response.

Response-Status-Code AVP

The Response-Status-Code AVP (AVP Code xxxx) is of type Enumerated and identifies the value of returned in the Response Status Code parameter of the Response. The values are defined in clause 6.6.3.

Service-Context-Id AVP

This AVP is of type UTF8String and contains a unique identifier of the Diameter charging specific document that applies the request. This is an identifier allocated by the service provider, by the service element manufacturer, or by a standardization body, and must uniquely identify a given Diameter charging specific document.

The format of the Service-Context-Id is:

"extensions"."Release"."service-context" "@" "domain"

The OneM2M specific values “service-context” “@” “domain” are:

ts00xx@oneM2M.org for OneM2M charging

The “Release” indicates the OneM2M Release the service specific document is based upon e.g. 1 for Release 1.

The “extensions” is operator specific information to any extensions in a service specific document.

Service-Information AVP

The Service-Information AVP (AVP code 873) is of type Grouped. Its purpose is to allow the transmission of additional OneM2M specific information elements.

The complete ABNF syntax is defined and maintained in 3GPP TS 32.299 [29]. The group structure includes zero or more occurrences of the Subscription-Id AVP and the M2M-Information AVP.

The format and content of the M2M-Information AVP which includes the OneM2M specific AVPs are specified in this document.

Subgroup-Name AVP

The Subgroup-Name AVP (AVP Code xxxx) is of type UTF8String and identifies the subgroup associated with a request. It shall be included when the IN initiates a fanning operation and one of the members of the group is a. This is the same as the attribute “groupName” for the subgroup as described in Table 7.3.13.1-3.

Subscription-Id AVP

The Subscription-Id AVP (AVP Code 443) is of type Grouped with structure defined in RFC 4006 [30]. The Subscription-Id AVP includes a Subscription-Id-Data AVP that holds the identifier and a Subscription-Id-Type AVP that defines the identifier type.

For M2M, this identifies the M2M Service Subscription ID associated with the request. This is determined by association maintained by the M2M SP as per clause 12.1.3 in TS-0001 Functional Architecture [6].

Subscription-Id-Data AVP

The Subscription-Id-Data AVP (AVP Code 444) is of type UTF8String as defined in RFC 4006 [30]. The Subscription-Id-Data is used to identify the M2M Service Subscription. The Subscription-Id-Type AVP defines which type of identifier is used.

Subscription-Id-Type AVP

The Subscription-Id-Type AVP (AVP Code 450) is of type Enumerated as defined in RFC 4006 [30]. It is used to determine which type of identifier is carried by the Subscription-Id AVP. The type(s) to be supported  is(are) determined by the M2M SP.

Target-ID AVP

The Target-ID AVP (AVP Code xxxx) is of type UTF8String and identifies the target URL for the M2M request if available.

Alternatively the Target-ID AVP can identify the target resource identifier with format defined in clause 6.3.3.

## ---end of Second change---------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?