| CHANGE REQUEST |
| --- |
| Meeting:* | TP16 |
| Source:* | InterDigital |
| Date:* | 2015-03-15 |
| Contact:* | Dale Seed, InterDigital, Dale.Seed@InterDigital.com |
| Reason for Change/s:* | More efficient way to encode operationMonitor |
| CR against: Release* | R1 |
| CR against: WI* | Active – WI-0009 (PRO) MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TS-0004-v1.0.1 |
| Clauses/Sub Clauses* | 10.2.12 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Currently TS-0004 defines m2m:eventNotificationCriteria as a complex data type that has the element  operationMonitor defined as a m2m:operation with a multiplicity of 0..5.

Defining operationMonitor as type m2m:operation  however is not as efficient as if it were defined with a type similar/same as m2m:accessControlOperations.

Comparing these two enumerated types (see below) one can see that m2m:accessControlOperations supports combinations of operations while m2m:operation does not.  Therefore an enumerated type like m2m:accessControlOperations is better suited for operationMonitor which requires combinations of operations.

This contribution proposes to rename and restructure m2m:accessControlOperations such that it is more generic and can be used by m2m:eventNotificationCriteria

Table 6.3.3.2.5-1: Interpretation of operation

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Create |  |
| 2 | Retrieve |  |
| 3 | Update |  |
| 4 | Delete |  |
| 5 | Notify |  |
| NOTE: See clause 6.4.1 “Request message parameter data types” |

Table 6.3.3.2.29-1: Interpretation of accessControlOperations

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | CREATE |  |
| 2 | RETRIEVE |  |
| 4 | UPDATE |  |
| 8 | DELETE |  |
| 16 | DISCOVERY |  |
| 32 | NOTIFY |  |
| NOTE: Combinations of these values are specified by adding them together. For example the value 5 is interpreted as “CREATE and UPDATE” |

### -----------------------Start of change 1-------------------------------------------

##### m2m:resourceOperations

Used for accessControlPolicys and eventNotificationCriteria.

Table 6.3.3.2.29-1: Interpretation of resourceOperations

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | CREATE |  |
| 2 | RETRIEVE |  |
| 4 | UPDATE |  |
| 8 | DELETE |  |
| 16 | NOTIFY |  |
| 32 | DISCOVERY |  |
| NOTE: Combinations of these values are specified by adding them together. For example the value 5 is interpreted as “CREATE and UPDATE” |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 1-------------------------------------------

##### m2m:resourceOperations

Used for accessControlPolicys and eventNotificationCriteria.

Table 6.3.3.2.29-1: Interpretation of resourceOperations

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | CREATE |  |
| 2 | RETRIEVE |  |
| 4 | UPDATE |  |
| 8 | DELETE |  |
| 16 | NOTIFY |  |
| 32 | DISCOVERY |  |
| NOTE: Combinations of these values are specified by adding them together. For example the value 5 is interpreted as “CREATE and UPDATE” |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

Table 6.3.3.2.19-1: Interpretation of resourceStatus

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | childCreated |  |
| 2 | childDeleted |  |
| 4 | updated |  |
| 8 | deleted |  |
| NOTE: See clause 7.4.1.1 “Definition of Notification” Note: Combinations of these values are specified by adding them together. For example the value 5 is interpreted as “childCreated and updated” |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

Table 6.3.4.26-1: Type Definition of m2m:accessControlRule

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| accesscControlOriginators | list of xs:anyURI | 1 |  |
| accessControlOperations | m2m:resourceOperations | 1 |  |
| accessControlContexts |  | 0..1 |  |
| accessControlContexts/accessControlWindow | m2m:scheduleEntry | 0..n |  |
| accessControlContexts/accessControlIpAddresses | list of m2m:ipv4 or list of m2m:ipv6 | 0..1 |  |
| accessControlContexts/accessControlLocationRegions | m2m:locationRegion | 0..n |  |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

Table 6.3.4.6-1:Type Definition of m2m:eventNotificationCriteria

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| createdBefore | m2m:timestamp | 0..1 |  |
| createdAfter | m2m:timestamp | 0..1 |  |
| modifiedSince | m2m:timestamp | 0..1 |  |
| unmodifiedSince | m2m:timestamp | 0..1 |  |
| stateTagSmaller | xs:positiveInteger | 0..1 |  |
| stateTagBigger | xs:nonNegativeInteger | 0..1 |  |
| expireBefore | m2m:timestamp | 0..1 |  |
| expireAfter | m2m:timestamp | 0..1 |  |
| sizeAbove | xs:nonNegativeInteger | 0..1 |  |
| sizeBelow | xs:positiveInteger | 0..1 |  |
| resourceStatus | m2m:resourceStatus | 0..1 |  |
| operationMonitor | m2m:resourceOperations | 0..1 | Note, Discover operation is not applicable to operationMonitor hence operationMonitor value shall be less than 32 |
| attribute | m2m:attribute | 0..n |  |

### -----------------------End of change 4 ---------------------------------------------

### -----------------------Start of change 5 ---------------------------------------------

<!-- resource operations -->

<xs:simpleType name="resourceOperations">

<xs:annotation>

<xs:documentation>Shall be considered for resource operations by the CSE</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:integer">

<!-- Create -->

<xs:enumeration value="1"/>

<!-- Retrieve -->

<xs:enumeration value="2"/>

<!-- Create + Retrieve -->

<xs:enumeration value="3"/>

<!-- Update -->

<xs:enumeration value="4"/>

<!-- Create + Update -->

<xs:enumeration value="5"/>

<!-- Retrieve + Update -->

<xs:enumeration value="6"/>

<!-- Create + Retrieve + Update -->

<xs:enumeration value="7"/>

<!-- Delete -->

<xs:enumeration value="8"/>

<!-- Create + Delete -->

<xs:enumeration value="9"/>

<!-- Retrieve + Delete -->

<xs:enumeration value="10"/>

<!-- Create + Retrieve + Delete -->

<xs:enumeration value="11"/>

<!-- Update + Delete -->

<xs:enumeration value="12"/>

<!-- Create + Update + Delete -->

<xs:enumeration value="13"/>

<!-- Retrieve + Update + Delete -->

<xs:enumeration value="14"/>

<!-- Create + Retrieve + Update + Delete -->

<xs:enumeration value="15"/>

<!-- Notify -->

<xs:enumeration value="16"/>

<!-- Create + Notify -->

<xs:enumeration value="17"/>

<!-- Retrieve + Notify -->

<xs:enumeration value="18"/>

<!-- Create + Retrieve + Notify -->

<xs:enumeration value="19"/>

<!-- Update + Notify -->

<xs:enumeration value="20"/>

<!-- Create + Update + Notify -->

<xs:enumeration value="21"/>

<!-- Retrieve + Update + Notify -->

<xs:enumeration value="22"/>

<!-- Create + Retrieve + Update -->

<xs:enumeration value="23"/>

<!-- Delete + Notify -->

<xs:enumeration value="24"/>

<!-- Create + Delete + Notify -->

<xs:enumeration value="25"/>

<!-- Retrieve + Delete + Notify -->

<xs:enumeration value="26"/>

<!-- Create + Retrieve + Delete + Notify -->

<xs:enumeration value="27"/>

<!-- Update + Delete + Notify -->

<xs:enumeration value="28"/>

<!-- Create + Update + Delete + Notify -->

<xs:enumeration value="29"/>

<!-- Retrieve + Update + Delete + Notify -->

<xs:enumeration value="30"/>

<!-- Create + Retrieve + Update + Delete + Notify -->

<xs:enumeration value="31"/>

<!-- Discover -->

<xs:enumeration value="32"/>

<!-- Create + Discover -->

<xs:enumeration value="33"/>

<!-- Retrieve + Discover -->

<xs:enumeration value="34"/>

<!-- Create + Retrieve + Discover -->

<xs:enumeration value="35"/>

<!-- Update + Discover -->

<xs:enumeration value="36"/>

<!-- Create + Update + Discover -->

<xs:enumeration value="37"/>

<!-- Retrieve + Update + Discover -->

<xs:enumeration value="38"/>

<!-- Create + Retrieve + Update + Discover -->

<xs:enumeration value="39"/>

<!-- Delete + Discover -->

<xs:enumeration value="40"/>

<!-- Create + Delete + Discover -->

<xs:enumeration value="41"/>

<!-- Retrieve + Delete + Discover -->

<xs:enumeration value="42"/>

<!-- Create + Retrieve + Delete + Discover -->

<xs:enumeration value="43"/>

<!-- Update + Delete + Discover -->

<xs:enumeration value="44"/>

<!-- Create + Update + Delete + Discover -->

<xs:enumeration value="45"/>

<!-- Retrieve + Update + Delete + Discover -->

<xs:enumeration value="46"/>

<!-- Create + Retrieve + Update + Delete + Discover -->

<xs:enumeration value="47"/>

<!-- Notify + Discover -->

<xs:enumeration value="48"/>

<!-- Create + Notify + Discover -->

<xs:enumeration value="49"/>

<!-- Retrieve + Notify + Discover -->

<xs:enumeration value="50"/>

<!-- Create + Retrieve + Notify + Discover -->

<xs:enumeration value="51"/>

<!-- Update + Notify + Discover -->

<xs:enumeration value="52"/>

<!-- Create + Update + Notify + Discover -->

<xs:enumeration value="53"/>

<!-- Retrieve + Update + Notify + Discover -->

<xs:enumeration value="54"/>

<!-- Create + Retrieve + Update + Discover -->

<xs:enumeration value="55"/>

<!-- Delete + Notify + Discover -->

<xs:enumeration value="56"/>

<!-- Create + Delete + Notify + Discover -->

<xs:enumeration value="57"/>

<!-- Retrieve + Delete + Notify + Discover -->

<xs:enumeration value="58"/>

<!-- Create + Retrieve + Delete + Notify + Discover -->

<xs:enumeration value="59"/>

<!-- Update + Delete + Notify + Discover -->

<xs:enumeration value="60"/>

<!-- Create + Update + Delete + Notify + Discover -->

<xs:enumeration value="61"/>

<!-- Retrieve + Update + Delete + Notify + Discover -->

<xs:enumeration value="62"/>

<!-- Create + Retrieve + Update + Delete + Notify + Discover -->

<xs:enumeration value="63"/>

</xs:restriction>

</xs:simpleType>

### -----------------------End of change 5 ---------------------------------------------

### -----------------------Start of change 6 ---------------------------------------------

<xs:complexType name="accessControlRule">

<xs:sequence>

<xs:element name="accessControlOriginators" type="m2m:listOfURIs" />

<!-- accessControlOperations defined as enumerated list 1 ... 63 -->

<xs:element name="accessControlOperations" type="m2m:resourceOperations" />

<!-- TODO: mismatch with TS-0004 where "accessControlContexts" has multiplicity 0..1 -->

<xs:element name="accessControlContexts" minOccurs="0" maxOccurs="unbounded">

<xs:complexType>

<xs:sequence>

<!-- TODO: mismatch with TS-0003 where element is called "accessControlTimeWindows" -->

<!-- TODO: mismatch with TS-0001 where element is called "accessControlTimeWindow" -->

<xs:element name="accessControlWindow" type="m2m:scheduleEntry" minOccurs="0" maxOccurs="unbounded" />

<!-- TODO: mismatch with TS-0001: element is called accessControlIpAddress in TS-0001" in TS-0003 -->

<xs:element name="accessControlIpAddresses" minOccurs="0">

<xs:complexType>

<xs:sequence>

<!-- TODO: it should be possible to include both IPv6 and IPv4 address. Present text in TS-0004 is ambiguous. Not

clear if "or" in TS-0001 is inclusive or exclusive. Below it is interpreted as inclusive. -->

<!-- TODO: the element names ipv4Addresses and ipv6Addresses are not explicitly mentioned in TS-0004 -->

<xs:element name="ipv4Addresses" minOccurs="0" maxOccurs="1">

<!-- space separated list of IPv4 addresses -->

<xs:simpleType>

<xs:list itemType="m2m:ipv4" />

</xs:simpleType>

</xs:element>

<xs:element name="ipv6Addresses" minOccurs="0" maxOccurs="1">

<!-- space separated list of IPv6 addresses -->

<xs:simpleType>

<xs:list itemType="m2m:ipv6" />

</xs:simpleType>

</xs:element>

</xs:sequence>

</xs:complexType>

</xs:element>

<!-- TODO: mismatch with TS-0003 and TS-0004 where element is called "accessControlLocationRegions" -->

<!-- TODO: mismatch with TS-0004 where element has multiplicity [0..n] -->

<xs:element name="accessControlLocationRegion" type="m2m:locationRegion" minOccurs="0" />

</xs:sequence>

</xs:complexType>

</xs:element>

</xs:sequence>

</xs:complexType>

### -----------------------End of change 6 ---------------------------------------------

### -----------------------Start of change 7 ---------------------------------------------

<xs:simpleType name="resourceStatus">

<xs:annotation>

<xs:documentation></xs:documentation>

</xs:annotation>

<xs:restriction base="xs:integer">

<!-- childCreated -->

<xs:enumeration value="1" />

<!-- childDeleted -->

<xs:enumeration value="2" />

<!-- childCreated + childDeleted -->

<xs:enumeration value="3" />

<!-- updated -->

<xs:enumeration value="4" />

<!-- childCreated + updated -->

<xs:enumeration value="5"/>

<!-- childDeleted + updated -->

<xs:enumeration value="6"/>

<!-- childCreated + childDeleted + updated -->

<xs:enumeration value="7"/>

<!-- deleted -->

<xs:enumeration value="8"/>

<!-- childCreated + deleted -->

<xs:enumeration value="9"/>

<!-- childDeleted + deleted -->

<xs:enumeration value="10"/>

<!-- childCreated + childDeleted + deleted -->

<xs:enumeration value="11"/>

<!-- updated + deleted -->

<xs:enumeration value="12"/>

<!-- childCreated + updated + deleted -->

<xs:enumeration value="13"/>

<!-- childDeleted + updated + deleted -->

<xs:enumeration value="14"/>

<!-- childCreated + childDeleted + updated + deleted -->

<xs:enumeration value="15"/>

</xs:restriction>

</xs:simpleType>

### -----------------------End of change 7 ---------------------------------------------

### -----------------------Start of change 8 ---------------------------------------------

<xs:complexType name="eventNotificationCriteria">

<xs:sequence>

<xs:element name="createdBefore" type="m2m:timestamp" minOccurs="0" />

<xs:element name="createdAfter" type="m2m:timestamp" minOccurs="0" />

<xs:element name="modifiedSince" type="m2m:timestamp" minOccurs="0" />

<xs:element name="unmodifiedSince" type="m2m:timestamp" minOccurs="0" />

<xs:element name="stateTagSmaller" type="xs:positiveInteger" minOccurs="0" />

<xs:element name="stateTagBigger" type="xs:nonNegativeInteger" minOccurs="0" />

<xs:element name="expireBefore" type="m2m:timestamp" minOccurs="0" />

<xs:element name="expireAfter" type="m2m:timestamp" minOccurs="0" />

<xs:element name="sizeAbove" type="xs:nonNegativeInteger" minOccurs="0" />

<xs:element name="sizeBelow" type="xs:positiveInteger" minOccurs="0" />

<xs:element name="resourceStatus" type="m2m:resourceStatus" minOccurs="0" />

<xs:element name="operationMonitor" type="m2m:resourceOperation" minOccurs="0" />

<xs:element name="attribute" type="m2m:attribute" minOccurs="0" maxOccurs="unbounded" />

</xs:sequence>

</xs:complexType>

### -----------------------End of change 8 ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?