| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#16 |
| Source:* | Qualcomm Inc. |
| Date:* | 2015-03-22 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Editorial and essential corrections of data types |
| CR against: Release* | Release-1 |
| CR against: WI* | Active WI-0009 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004v1.0.1 |
| Clauses/Sub Clauses* | 6.2.1, 6.3.2, 6.3.3.2.31 (new), 6.3.3.3.4, 6.3.4.8, 6.3.4.14, 6.3.4.22, 6.3.4.23, 6.3.4.28, 6.6.3, 7.3.10.1, 7.3.13, 7.4.1.1, D.12.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The review of XSD files after the PRO#15 meeting in Miami has discovered a number of inconsistencies between data type definitions in TS-0004 and in the XSD files. These issues are summarised in the Excel sheet attached to PRO-2015-0730. Some of these changes which are not just editorial could not be corrected by the rapporteurs in the published version of TS-0004v1.0.1.

This CR addresses some of the issues listed in PRO-2015-0730 and aims to align TS-0004 with the published XSD files version v1_0_0. If the proposed change to TS-0004 cannot be agreed, in most cases the corresponding XSD file(s) would need to be revised.

Note that issues on Access Control Policy related data types listed in PRO-2015-0730 are addressed in a separate CR, PRO-2015-0732.

change 1+2: Adding data type  m2m:triggerRecipientID missing in TS-0004, removing parentheses from list types

change 3:  data type m2m:attribute changed to sequence of name and value

change 4:  renaming element “type” of anyArgType to “value”

change 5:  removing “anyArg” element from m2m:execReqArgsListType

change 6: m2m:mgmtLinkRef, data type of @name change from xs:string to xs:NCName

change 7: m2m:childResourceRef, data type of @name change from xs:string to xs:NCName

change 8: spelling corrections to Response Status Code names

change 9: data type of locationStatus attribute of <locationPolicy> resource changed from xs:string to xs:status

change 10:  data types of currentNrOfMembers and maxNrOfMembers  attributes of <group> resource corrected from xs:long to xs:nonNegativeInteger

change 11: Clarifications on data types of notification data object

change 12: Correction of data type of requestContext and requestCharacteristics attributes of <cmdhLimits> resource from xs:string to xs:anyType. This change was agreed at discussion of agreed CR PRO-2014-0663R04, but it was forgotten to be implemented in the CR.

changes added in revision R01:

addition to change 2:  in Table 6.3.2-1, ‘m2m:labelsType’ replaced by ‘m2m:labels’ for alignment with the XSD

addition in change 12:  Data type of limitsDelAggregation attribute, ‘m2m:permittedBooleanValues’ replaced by  ‘list of xs:boolean’ and text on constraints added to the last column.

change 13: Addition of a new clause 6.3.3.2.31  which defines the enumeration data type ‘m2m:filterUsage’

change 14: Correction of data type ‘m2m:stdEventCats’ defined in clause 6.3.3.3.4

### -----------------------Start of change 1-------------------------------------------

### Summary of oneM2M Identifiers

Table 6.2.1-1 shows the summary of M2M Identifiers defined in oneM2M TS-0001 Functional Architecture [Error! Reference source not found.].

Table 6.2.1-1: M2M Identifiers

| Identifier | Data Type | Description |
| --- | --- | --- |
| M2M-SP-ID | m2m:ID (see clause 6.3) | A globally unique ID as specified in [Error! Reference source not found.] |
| App-ID | m2m:ID (see clause 6.3) | The identifier is specified in[Error! Reference source not found.] |
| AE-ID | m2m:ID (see clause 6.3) | A globally unique ID as specified in [Error! Reference source not found.] |
| CSE-ID | m2m:ID (see clause 6.3) | A globally unique ID as specified in [Error! Reference source not found.] |
| M2M-Node-ID | m2m:nodeID (see clause 6.3) | A globally unique ID as specified in[Error! Reference source not found.] |
| M2M-Sub-ID | m2m:ID (see clause 6.3) | A globally unique ID as specified in [Error! Reference source not found.] |
| M2M-Request-ID | m2m:requestID (see clause 6.3) | A unique ID as specified in [Error! Reference source not found.] |
| M2M-Ext-ID | m2m:externalID (see clause Error! Reference source not found.) | The identifier is specified in [Error! Reference source not found.] |
| UNetwork-ID | m2m:ID (see clause 6.3) | A unique ID as specified in [Error! Reference source not found.] |
| Trigger-Recipient-ID | m2m:triggerRecipientID | The identifier is specified in [Error! Reference source not found.] |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### oneM2M simple data types

Table 6.3.2-1 describes oneM2M-specific simple data type definitions. XML Schema data type definitions for these data types can be found in the XSD file called CDT-commonTypes-v1_0_0.xsd.

The types in table 6.3.2-1 are either:

- Atomic data types derived from XML Schema data types by restrictions other than enumeration

- List data types constructed from other XML Schema or oneM2M-defined atomic data types.

The oneM2M-defined enumeration data types are defined in clause Error! Reference source not found..

Table 6.3.2-1: oneM2M Simple Data Types

| XSD type name | Type Name | Examples | Description |
| --- | --- | --- | --- |
| m2m:ID | Generic ID | //globalm2m.org | Used to represent generic IDs generated and used within oneM2M (M2M-SP-ID) |
|  |  | //globalm2m.org/C190XX7T | (CSE-ID) |
|  |  | //globalm2m.org/CSE1/123A38ZZY | (AE-ID) |
| m2m:nodeID | Node ID | urn:gsma:imei:90420156-025763-0;svn=42 | Used for Node IDs. The constraints on this type are different from those on Generic IDs (IMEI as node ID) |
| m2m:deviceID | Device ID |  |  |
| m2m:externalID | M2M-EXT-ID | urn:gsma:imei:90420156-025763-0;vers=0 | The identifier of the node for the underlying network provider. In 3GPP case, the accessID is mapped to External Identifier as specified in TS 23.003 Error! Reference source not found.. Or (MSISDN) The identifier of the node as specified in TS 23.003 Error! Reference source not found., |
| m2m:requestID | Request ID | ab3f124a, CSE1/98821 | Used for Request IDs. This type may include the ID of the target CSE as well as a part that varies for each ID |
| m2m:nhURI | Non hierarchical Identifier | /CSE090112/ C190XX7T | Used where a resourceID is required to be non-hierarchical |
| m2m:acpType | List of ACP Types | //IN-CSEID.m2m.myoperator.org/93405 | Used to represent an AccessControlPolicy identifier. This can be either a URI or an opaque token |
| m2m:labels | Labels | printers networkwifi1 vendor1 | A list of tokens used as keys for discovering resources (searching wifi connected printer from vendor 1) |
| m2m:networkaccessID | Network Access Identifier | user@realm | The network access Identifier is a standard way of identifying users who request access to a network as specified at IETF RFC 4282 [Error! Reference source not found.]. |
| m2m:triggerRecipientID | Trigger Recipient Identifier | 4000 | Used when device triggering services are requested from the Underlying Network, to identify an instance of an ASN/MN-CSE on an execution environment, to which the trigger is routed. Defined as port number in the range 0 and 65535. |
| m2m:listOfM2MID | List of M2M identifiers |  | xs:list of elements of data type m2m:ID |
| m2m:listOfMinMax | List of Time Limits | 10 2560 | xs:list of two xs:long values defining min and max limits of time intervals in units of milliseconds (value -1 representing infinite time) |
| m2m:backOffParameters | List of Backoff Parameters | 100 100 2000 | Ordered sequence of 3 values of data type xs:nonNegativeInteger representing backoffTime, backoffTimeIncrement, maximumBackoffTime (in units of milliseconds) |
| m2m:ipv4 | IPv4 address string with optional CIDR suffix | 10.125.0.0/16, 122.77.12.1 | Required in m2m:acr |
| m2m:ipv6 | IPv6 address string with optional CIDR suffix | ::/0, Fadf:ddd0::/32, abcd:ffff:abb0:aaaa::/64 | Required in m2m:acr |
| m2m:countryCode | Country Code | KR | 2-character country code as defined by ISO-3166 |
| m2m:poaList | List of PointOfAccess strings | http://172.25.0.10:8080, coap://m2m.sp.com | list of xs:string. Each pointOfAccess entry in list is represented as a string containing the underlying transport protocol as well as the IP address and port (or an FQDN). |
| m2m:timestamp | Time stamp string | 20141003T112032 | DateTime string of ‘Basic Format’ specified in ISO8601 [27]. Time zone shall be interpreted as UTC timezone. |
| m2m:typeOfContent | Type of Content | application/xml | The media type shall be an IANA registered Media Types name, or an experimental Media Type (See [26]) ‘:’ |
| m2m:contentInfo | Content Information | application/xml:2 | A string consisting of a media type optionally followed by a m2m:encoding separated by ‘:’ character. If the encoding portion is omitted, value 0 (plain) shall be applied ‘:’.. |
| m2m:eventCat | Event Category | 2 | Either One of the values from m2m:stdEventCats or A user-defined category in the range 100-999 |
| m2m:eventCatWithDef | Event Category with default | 0 | Either A value from m2m:eventCat , or The value 0 which has the special meaning “default” |
| m2m:listOfEventCat | List of (applicable) Event Categories | 1 101 | xs:list of elements of data type m2m:eventCat |
| m2m:listOfEventCatWithDef | List of m2m:eventCatWithDef | 0 1 101 |  |
| m2m:scheduleEntry | Schedule Entry | * 0-5 2,6,10 * * * | The string is used to describe a duration of enablement. The string format is described in clause Error! Reference source not found. |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### m2m:attribute

Used in m2m:eventNotificationCriteria and m2m:filterCriteria.

Table 6.3.4.8-1: Type Definition of m2m:attribute

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| name | xs:NCName | 1 |  |
| value | xs:anyType | 1 |  |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

#### m2m:anyArgType

Table 6.3.4.14-1: Type Definition of m2m:anyArgType

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| name | xs:NCName |  |  |
| value | xs:anyType |  |  |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

#### m2m:execReqArgsListType

Table 6.3.4.22-1: Type Definition of m2m:execReqArgsListType

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| reset | m2m:resetArgsType | 0..n |  |
| reboot | m2m:rebootArgsType | 0..n |  |
| upload | m2m:downloadArgsType | 0..n |  |
| download | m2m:downloadArgsType | 0..n |  |
| softwareInstall | m2m:softwareInstallArgsType | 0..n |  |
| softwareUpdate | m2m:softwareUpdateType | 0..n |  |
| softwareUninstall | m2m:softwareUninstallArgsType | 0..n |  |

This type is an xs:choice.  It shall contain elements from no more than one row listed in the table above.

### -----------------------End of change 5-------------------------------------------

### -----------------------Start of change 6-------------------------------------------

#### m2m:mgmtLinkRef

Table 6.3.4.23-1: Type Definition of m2m:mgmtLinkRef

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| (base content) | xs:anyURI | 1 | URI (of type xs:anyURI) with name and type attributes. |
| @name | xs:NCName | 1 | The name attribute represents the name of the referenced resource instance. |
| @type | m2m:mgmtDefinition | 1 | The type attribute is restricted to the allowed specializations of resource type <mgmtObj> |

In the above table, names of XML schema attributes are prefixed with a “@” character to differentiate these from Resource attribute names. The “@” character is not part of the actual attribute name.

### -----------------------End of change 6-------------------------------------------

### -----------------------Start of change 7-------------------------------------------

#### m2m:childResourceRef

Table 6.3.4.24-1: Type Definition of m2m:childResourceRef

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| (base content) | xs:anyURI | 1 | URI of the child resource |
| @name | xs:NCName | 1 | Gives the name of the child resource pointed to by the URI |
| @type | m2m:resourceType | 1 | Gives the resourceType of the child resource pointed to by the URI |

In the above table, names of XML schema attributes are prefixed with a “@” character to differentiate these from Resource attribute names. The “@” character is not part of the actual attribute name.

### -----------------------End of change 7-------------------------------------------

### -----------------------Start of change 8-------------------------------------------

### Definition of Response Status Codes

#### Overview

The tables in the following clauses specify the RSCs for oneM2M releases. Each RSC includes: a response status represented as numeric code. The supplemental information may be returned when it is needed.

#### Informational response class

Table 6.6.3.2-1 specifies the RSCs for acknowledgement responses for each release.

Table 6.6.3.2-1: Informational Responses class

| Numeric Code | Description |
| --- | --- |
| 1000 | ACCEPTED |

#### Successful response class

Table 6.6.3.2-1 specifies the RSCs for Successful responses.

Table 6.6.3.3-1: RSCs for Successful response class

| Numeric Code | Description |
| --- | --- |
| 2000 | OK |
| 2001 | CREATED |
| 2002 | DELETED |
| 2004 | CHANGED |

#### Redirection response class

In this release, no values in this response class are defined.

Table 6.6.3.4-1: RSCs for Redirection response class

| Numeric Code | Description |
| --- | --- |

#### Originator Error response class

Table 6.6.3.5-1 specify the RSCs for Originator Error responses.

Table 6.6.3.5-1: RSCs for Originator Error response class

| Numeric Code | Description |
| --- | --- |
| 4000 | BAD_REQUEST |
| 4004 | NOT_FOUND |
| 4005 | OPERATION_NOT_ALLOWED |
| 4008 | REQUEST_TIMEOUT |
| 4101 | SUBSCRIPTION_CREATOR_HAS_NO_PRIVILEGE |
| 4102 | CONTENTS_UNACCEPTABLE |
| 4103 | ACCESS_DENIED |
| 4104 | GROUP_REQUEST_IDENTIFIER_EXISTS |
| 4105 | CONFLICT |

#### Receiver Error response class

Table 6.6.3.6-1 specifies the RSCs for Receiver Error responses.

Table 6.6.3.6-1: RSCs for Receiver Error response class

| Numeric Code | Description |
| --- | --- |
| 5000 | INTERNAL_SERVER_ERROR |
| 5001 | NOT_IMPLEMENTED |
| 5103 | TARGET_NOT_REACHABLE |
| 5105 | NO_PRIVILEGE |
| 5106 | ALREADY_EXISTS |
| 5203 | TARGET_NOT_SUBSCRIBABLE |
| 5204 | SUBSCRIPTION_VERIFICATION_INITIATION_FAILED |
| 5205 | SUBSCRIPTION_HOST_HAS_NO_PRIVILEGE |
| 5206 | NON_BLOCKING_REQUEST_NOT_SUPPORTED |

#### Network System Error response class

Table 6.6.3.7-1 specifies the RSCs for when the External System reported some errors.

Table 6.6.3.7-1: RSCs for Network Service Error response class

| Numeric Code | Description |
| --- | --- |
| 6003 | EXTENAL_OBJECT_NOT_REACHABLE |
| 6005 | EXTENAL_OBJECT_NOT_FOUND |
| 6010 | MAX_NUMBER_OF_MEMBER_EXCEEDED |
| 6011 | MEMBER_TYPE_INCONSISTENT |
| 6020 | MGMT_SESSION_CANNOT_BE_ESTABLISHED |
| 6021 | MGMT_SESSION_ESTABLISHMENT _TIMEOUT |
| 6022 | INVALID _CMDTYPE |
| 6023 | INVALID_ARGUMENTS |
| 6024 | INSUFFICIENT_ARGUMENTS |
| 6025 | MGMT_CONVERSION_ERROR |
| 6026 | MGMT_CANCELATION_FAILURE |
| 6028 | ALREADY_COMPLETE |
| 6029 | COMMAND_NOT_CANCELLABLE |

### -----------------------End of change 8-------------------------------------------

### -----------------------Start of change 9-------------------------------------------

#### Introduction

The <locationPolicy> resource represents the method for obtaining and managing geographical location information of an M2M Node. The detailed description can be found in the clause 9.6.10 in TS-0001 Functional Architecture [Error! Reference source not found.] .

Table 7.3.10.1-1: Data type definition of <locationPolicy> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| locationPolicy | CDT-locationPolicy-v1_0_0.xsd |  |

Table 7.3.10.1-2: Universal/Common Attributes of <locationPolicy> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| expirationTime | O | O |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| lastModifiedTime | NP | NP |
| labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |

Table 7.3.10.1-3: Resource Specific Attributes of <locationPolicy> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| locationSource | M | NP | m2m:locationSource | No default |
| locationUpdatePeriod | O | O | xs:duration | No default |
| locationTargetID | O | NP | m2m:nodeID | No default |
| locationServer | O | NP | xs:anyURI | No default |
| locationContainerID | NP | NP | xs:anyURI | No default |
| locationContainerName | O | O | xs:string | No default |
| locationStatus | NP | NP | xs:status | No default |

Table 7.3.10.1-4: Child resources of <locationPolicy> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause Error! Reference source not found. |

### -----------------------End of change 9-------------------------------------------

### -----------------------Start of change 10-------------------------------------------

### Resource Type <group>

#### Introduction

The <group> resource represents a group of resources of the same or mixed types. The <group> resource can be used to do bulk manipulations on the resources represented by the membersID attribute. The <group> resource contains an attribute that represents the members of the group and a virtual resource (the <fanOutPoint>) that allows operations to be applied to the resources represented by those members. The detailed description can be found in clause 9.6.13 in TS-0001 Functional Architecture [Error! Reference source not found.].

Table 7.3.13.1-1: Data type definition of <group> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| group | CDT-group-v1_0_0.xsd |  |

Table 7.3.13.1-2: Universal/Common Attributes of <group> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | O |
| resourceID | NP | O |
| parentID | NP | NP |
| accessControlPolicyIDs | O | NP |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| Labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |

Table 7.3.13.1-3: Resource Specific Attributes of <group> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| creator | O | NP | m2m:ID |  |
| memberType | M | O | m2m:memberType | Default value is set to ‘MIXED’ |
| currentNrOfMembers | NP | NP | xs:nonNegativeInteger | No default (This is generated by the hosting CSE and limited by the maxNrOfMembers attribute of the <group> resource) |
| maxNrOfMembers | M | O | xs:nonNegativeInteger | No default |
| memberID | M | O | list of xs:anyURI | No default |
| membersAccessControlPolicyIDs | O | O | xs:anyURI | No default |
| memberTypeValidated | NP | NP | xs:boolean | No default (This is generated by the hosting CSE) |
| consistencyStrategy | O | NP | m2m:consistencyStrategy | Default value is set to ‘ABANDON_MEMBER’ |
| groupName | O | O | xs:string | No default |

Table 7.3.13.1-4: Child resources of <group> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause Error! Reference source not found. |
| <fanOutPoint> | fanOut | 1 | Clause Error! Reference source not found. |

#### <group> resource specific procedure on CRUD operations

This clause describes <group> resource specific procedure on Resource Hosting CSE for CRUD operations.

##### Create

Primitive specific operation after Recv-C-6.4 "Check validity of resource representation for the given resource type" and before Recv-C-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed ". See clause Error! Reference source not found..

- Primitive specific operation: Validate the provided attributes. It shall also check whether the number of URIs present in the memberID attribute of the group resource representation does not exceed the maximum as specified by the attribute maxNrOfMembers. If the maximum is exceeded, the request shall be rejected with a Response Status Code indicating “MAX_NUMBER_OF_MEMBER_EXCEEDED” error.
If the memberType attribute of the <group> resource is not "MIXED", the hosting CSE shall also verify that all the member URIs including sub-groups in the attribute memberID of the <group> resource representation provided in the request shall conform to the memberType of the group resource.

In the case that the <group> resource contains sub-group member resources, the receiver shall retrieve the memberType of the sub-group member resources to validate the memberType. If the memberType cannot be retrieved due to lack of privilege, the request shall be rejected with a Response Status Code indicating “NO_PRIVILEGE” error. If the sub-group member resources are temporarily unreachable, the receiver shall set the memberTypeValidated attribute of the <group> resource to FALSE and return the result to the originator in the response of the request. As soon as any unreachable sub-group resource becomes reachable, the receiver shall perform the memberType validation procedure. The originator may get to know the validation result by subscribe to the created resource if the memberTypeValidated attribute is FALSE. Upon unsuccessful validation, the receiver shall delete the <group> resource if the consistencyStrategy of the <group> resource is ABANDON_GROUP, or remove the inconsistent members from the <group> resource if the consistencyStrategy attribute is ABANDON_MEMBER, or set the memberType attribute of the <group> resource to "MIXED" if the consistencyStrategy attribute is SET_MIXED.
The memberTypeValidated attribute shall be set to TRUE if all the members have been validated successfully.

##### Retrieve

No primitive specific operations.

##### Update

- Primitive specific operation after Recv-6.4 "Check validity of resource representation for the given resource type" and before Recv-6.5 “Create/Update/Retrieve/Delete/Notify operation is performed ". See clause Error! Reference source not found..Primitive specific operation: If the memberType attribute of the <group> resource is not "MIXED", the hosting CSE shall verify that all the member URIs including sub-groups in the attribute memberID of the <group> resource representation provided in the request shall conform to the memberType of the <group> resource.

In the case that the <group> resource contains sub-group member resources, the receiver shall retrieve the memberType of the sub-group member resource to validate the memberType. If the memberType cannot be retrieved due to lack of privilege, the request shall be rejected with a Response Status Code indicating “NO_PRIVILEGE” error. If the sub-group member resources are temporarily unreachable, the receiver shall set the memberTypeValidated attribute of the <group> resource to FALSE and return the result to the originator in the response of the request. As soon as any unreachable sub-group resource becomes reachable, the receiver shall perform the memberType validation procedure. The originator may get to know the validation result by subscribe to the created resource if the memberTypeValidated attribute is FALSE. Upon unsuccessful validation, the receiver shall delete the <group> resource if the consistencyStrategy of the <group> resource is ABANDON_GROUP, or remove the inconsistent members from the <group> resource if the consistencyStrategy attribute is ABANDON_MEMBER, or set the memberType attribute of the <group> resource to "MIXED" if the consistencyStrategy attribute is SET_MIXED.
The memberTypeValidated attribute shall be set to TRUE if all the members have been validated successfully.

Primitive specific operation: The hosting CSE shall check whether the number of provided memberID in the attribute members exceeds the limitation of maxNrOfMembers. If it exceeds, the hosting CSE shall reject the request with Response Status Code indicating “NOT_ALLOWED” error.

##### Delete

No primitive specific operations.

### -----------------------End of change 10-------------------------------------------

### -----------------------Start of change 11-------------------------------------------

#### Notification data object

Notification procedures represent a special case of the generic procedures defined in clause Error! Reference source not found., where the Operation parameter of the request primitive is set to value "N" (Notify). In this case, the request primitive is referred to as Notify request primitive, and the associated response primitive is denoted as Notify response primitive.

A Notify request primitive shall convey a special notification data object in its Content parameter. This notification data object has no resource type representation in the oneM2M TS-0001 Functional Architecture [Error! Reference source not found.], since it does not represent a resource accessible by any M2M entities. The data type of the notification data object is defined in the tables below. The first column of Table 7.4.1.1-2 defines the permitted names the root element the notification data object can take with the data type listed in the third column.

Table 7.4.1.1-1: Data Type Definition of notification data object

| Data Type ID | File Name | Note |
| --- | --- | --- |
| notification | CDT-notification-v1_0_0.xsd |  |

Table 0.1-2: Data Types for notification data objects

| Root ElementName | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | N |  |  |
| notification | O | m2m:notification |  |
| aggregatedNotification | O | m2m:aggregatedNotification |  |
| responsePrimitive | O | m2m:responsePrimitive |  |

### -----------------------End of change 11-------------------------------------------

### -----------------------Start of change 12-------------------------------------------

Resource [cmdhLimits]

The resource [cmdhLimits] represents limits for CMDH related parameter values. The detailed description can be found in clause D.12.5 of TS-0001 Functional Architecture [Error! Reference source not found.].

Table D.12.5-1: Data Type Definition of [cmdhLimits]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhLimits | CDT-cmdhLimits-v1_0_0.xsd |  |

Table D.12.5-2: Resource specific attributes of [cmdhLimits]

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| mgmtDefinition | M | NP | See clause Error! Reference source not found. | 1016 (cmdhLimits) |
| objectID | O | NP | See clause Error! Reference source not found. |  |
| objectPaths | O | NP | See clause Error! Reference source not found. |  |
| description | O | O | See clause Error! Reference source not found. |  |
| order | M | O | xs:positiveInteger | None |
| requestOrigin | M | O | m2m:listOfM2MID | None |
| requestContext | O | O | xs:anyType | None |
| requestContextNotification | O | O | xs:boolean | None |
| requestCharacteristics | O | O | xs:anyType | None |
| limitsEventCategory | M | O | list of m2m:eventCat | None |
| limitsRequestExpTime | M | O | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsResultExpTime | M | O | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsOpExecTime | M | O | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsRespPersistence | M | O | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsDelAggregation | M | O | list of xs:boolean | Permitted value settings of this data type are the following: ‘0’, ‘1’ or ‘0 1’ |

### -----------------------End of change 12-------------------------------------------

### -----------------------Start of change 13-------------------------------------------

##### m2m:filterUsage

Used in m2m:filterCriteria.

Table 6.3.3.2.31-1: Interpretation of filterUsage

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Discovery Criteria |  |
| 2 | Event Notification Criteria |  |

### -----------------------End of change 13-------------------------------------------

### -----------------------Start of change 14-------------------------------------------

##### m2m:stdEventCats

Used for ec parameter in request and eventCat attribute of <delivery> resource and cmdh policy resource types.

Table 6.3.3.3.4-1: Interpretation of stdEventCats

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Immediate |  |
| 2 | BestEffort |  |
| 3 | Latest |  |
| NOTE: See clause Error! Reference source not found. “Resource Type delivery” and Annex Error! Reference source not found. “Resource cmdhPolicy” |

### -----------------------End of change 14-------------------------------------------