| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#16 |
| Source:* | Qualcomm Inc. |
| Date:* | 2015-03-22 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Editorial and essential corrections |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0009v1.0.1 |
| Clauses/Sub Clauses* | 2.2, 3, 5, 6, 7 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Proposed changes address the following

- General editorial improvements of text, especially clarifying that the mapping between HTTP messages and primitives is bi-directional, i.e. from HTTP message to primitive and vice versa. Also this CR tries to differentiate in the description whether a mapping applies to request or response messages, or to both.

- Clarification of Figure 5.1-1: insufficient descriptive text was given previously, added text and thereby updated the figure for alignment with the new text.

- Included text about resourceType (ty) parameter into clause 6.4.3 (Content-Type).

- It is presently not clearly specified how the complex type ‘attribute’ parameter of filterCriteria shall be included into the query-string. It is also not specified how multiple instances of ‘attribute’ and ‘contentType’ parameters are included. In this version this issue is not resolved yet, just comments which need to be discussed and addressed are given instead.

Changes in R01:

- corrected the template to show correct CR footer and line numbering

- clause 5.1:  ‘shall provide’ ( ‘provides’

- removed ‘oneM2M’ when referring to primitive parameter names (consistently throughout this specification)

- clause 5.3:  ‘shall be omitted’ ( ‘is omitted’

- clause 6.1: clarified that the 4  use cases appear not only at originator and receiver, but also at transit CSEs

- clause 6.2.2: Description of To parameter applies to request only? How shall To parameter of response primitives be handled?

- clause 6.2.2:  Filter Criteria ( Filter Criteria

- clause 6.2.2 example 1): removed “(notificationURI shall not be present)”

- Example 2:  to be added

- Table 6.2.2-1: clarified Note on responseType. Do we need to define short query field name for notificationURI part?

- clause 6.3.2: ‘verbose’ ( ‘with more detailed information’

- Table 6.3.2-1: correction for “Conflict” Response Status Code

- clause 6.3.3:  clarification on omission of reason phrase

- clause 6.4.1: clarification of Receiver CSE in multi-hop scenario

- clause 6.4.7: ‘composer’ ( ‘originator’

Two issues are still open and need to be discussed and addressed in a revision of this change request:

- mapping of the To parameter  of response primitives

- clarification of the representation of multiple instances of the attribute and content elements of Filter Criteria parameter in the HTTP query string.

changes in R02 relative to R01:

- new header X-M2M-TO defined in HTTP response messages which carries to To parameter of request primitives

- specification how elements of Filter Criteria with multiplicity 0..n shall be handled. Added a column to Table 6.2.2-1 which shows multiplicity of the elements.

- added RSC 2000 (OK) to the Status Code Mapping Table 6.3.2-1

- editorial corrections in the Header descriptions

### -----------------------Start of change 1-------------------------------------------

# 2	References

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]	IETF RFC 7230 (June 2014): "Hypertext Transfer Protocol (HTTP/1.1): Message Syntax and Routing".

[2]	oneM2M TS-0003: Security Solutions.

[3]	oneM2M TS-0004: "Service Layer Core Protocol Specification".

[4]	RFC7235: “Hypertext Transfer Protocol (HTTP/1.1): Authentication”, IETF, June 2014.

[5]	RFC6750: “The OAuth 2.0 Authorization Framework: Bearer Token Usage”, October 2012.

[6]	oneM2M TS-0011: Common Terminology.

[7]	oneM2M TS-0001: Functional Architecture.

[x]		IETF RFC 7232 (June 2014): "Hypertext Transfer Protocol (HTTP/1.1): “Conditional Requests".

## 2.2	Informative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules.

NOTE:	Available at http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc.

[i.2]	IETF RFC 2617 (June 1999): "HTTP Authentication: Basic and Digest Access Authentication".

[i.3]	IETF RFC 6750 (October 2012): "The OAuth 2.0 Authorization Framework: Bearer Token Usage".

[i.4]	IETF RFC 6455 (December 2011):"The WebSocket Protocol".

[i.5]	oneM2M TS-0003: "Security Solutions".

# 3	Abbreviations

For the purposes of the present document, the following abbreviations those given in TS-0011-Common Terminology [6] apply:

CSE-ID	Common Service Entity Identifier

HTTP	Hyper Text Transfer Protocol

TLS	Transport Layer Security

URI	Uniform Resource Identifier

# 4	Conventions

The keywords "Shall", "Shall not", "May", "Need not", "Should", "Should not" in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1].

# 5	Overview on HTTP Binding

HTTP binding specifies the equivalence between oneM2M request and response primitives and HTTP request and response messages, respectively. This clause provides a brief overview on the mapping relationship between oneM2M and HTTP message parameters.

This clause describes how oneM2M request/response primitives can be mapped to HTTP request/response messages and vice versa.

## 5.1	Introduction

Figure 5.1-1 illustrates an example oneM2M system configuration and its correspondence to an HTTP-based information system if HTTP binding as defined in this specification is applied. The upper diagram in Figure 5.1-1 shows with solid line arrows the flow of a request primitive originating from an AE which is registered to an MN-CSE (Registrar of AE). The request primitive is assumed to address a resource which is hosted by another MN-CSE (Host of Resource). Both MN-CSEs are registered to the same IN-CSE.

When applying HTTP binding, the oneM2M entities of the upper diagram take the roles outlined in the lower diagram of a corresponding HTTP information system as defined in [1]. The AE takes the role of an HTTP client, the MN-CSE (Registrar of AE) takes the role of a HTTP Proxy Server, and both the IN-CSE and MN-CSE (Host of Resource) take the role of a HTTP server for this particular request message.

CSEs may also issue unsolicited request messages, shown with dashed line arrows in Figure 5.1-1, and receive associated response messages. Therefore, for HTTP protocol binding, CSEs generally provides capability of both HTTP Server and HTTP Client.  AEs may provide HTTP Server capability optionally in order to be able to serve Notification request messages (see TS-0004 [3] and TS-0001 [7]).

Figure 5.1-1: Correspondence between oneM2M entities and HTTP Client and Server

Each individual request primitive will be mapped to single HTTP request message, and each individual response primitive will be mapped to a single HTTP response message, and vice-versa.

An HTTP request message consists of Request-Line, headers and message-body. An HTTP response message consists of Status-Line, headers and message-body [1]. This clause describes how oneM2M request/response primitives are mapped to HTTP messages at a high level. Corresponding details are specified in clause 6.

## 5.2	Request-Line

The HTTP method of a request message is mapped to the Operation parameter, and vice-versa.

At the message originator side the HTTP Request-Target is derived from the To parameter of the request primitive, including a query string which carries other specific primitive parameters.

HTTP-Version is specified in clause 6.

## 5.3	Status-Line

HTTP Version is specified in clause 6.

The Status-Code of HTTP response messages is derived from the Response Status Code parameter of the response primitive. The Reason-Phrase is not applicable to oneM2M systems and is omitted.

# 6	HTTP Message Mapping

## 6.1	Introduction

Mapping between oneM2M primitives and HTTP messages shall be applied in the following four use cases:

- Mapping of request primitive to HTTP request message at the request originator (HTTP client)

- Mapping of HTTP request message to request primitive at the request receiver (HTTP server)

- Mapping of response primitive to HTTP response message at the request receiver (HTTP server)

- Mapping of HTTP response message to response primitive at the request originator (HTTP client)

All four use cases also appear at transit CSEs.

The following clauses specify the mapping between each oneM2M primitive parameter and a corresponding HTTP message field to compose HTTP request/response message.

## 6.2	Parameter Mappings on Request-Line

### 6.2.1	Method

The HTTP 'Method' shall be derived from the Operation request primitive parameter of the request primitive.

Table 6.2.1-1: HTTP Method Mapping

| oneM2M Operation | HTTP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT (full update) or POST (partial update) |
| Delete | DELETE |
| Notify | POST |

At the Receiver, an HTTP request message with POST method shall be mapped to a oneM2M Create or Notify request primitive in accordance with the value of the Operation parameter.

### 6.2.2	Request-Target

The path component of HTTP Request-Target shall be interpreted as the mapping of the To parameter. The query component (e.g. query-string) shall include other primitive parameters compliant with [1].

The To request primitive parameter shall be mapped to Request-Target. Only SP-Relative-Resource-ID and Absolute-Resource-ID forms (see clause 7.2 [7]) shall be applicable for the To parameter.

If the To request primitive parameter is in the SP-Relative-Resource-ID form, then the ‘origin-form’ representation shall be mapped to Request-Target. If the To parameter has Absolute-Resource-ID form, then ‘absolute-form’ shall be used for Request-Target (see clause 6.2.3 [3]).

The prefix string "http:" shall be added to the ‘absolute-form’ when the address is used in the ‘absolute-form’ in the Request-Target.

Each applicable request primitive parameter and element of the Filter Criteria parameter shown in Table 6.2.2-1 shall be represented as pair of field-name and value in query-string.  Multiple such pairs shall be concatenated with an ampersand ‘&’ character used as separator between two pairs.

Table 6.2.2-1 also shows the permitted multiplicity of occurrence of field names in the query-string. Multiplicity ‘0..1’ means that a  parameter  is optional and can occur at most once. Parameters with multiplicity ‘0..n’, may occur multiple times in the query-string in the form of  <query field name> = value.  For example, if the resourceType element of the Filter Criteria parameter is represented by a list of 3 values ‘2 3 4’ (see clause 6.3.4.7 in TS-0004 [3]), it would be mapped to rty=2&rty=3&rty=4 in the query-string. At the receiver side, this query string can be reverted back into the list type of representation.

The ‘attribute’ element of the Filter Criteria request primitive parameter consists of two elements, name and value, which in XML notation would look for example as follows in case of multiplicity 2 (see clause 6.2.4.8 in TS-0004 [3]):

<attribute>

<name>attname1</name>

<value>attvalue1</value>

</attribute>

<attribute>

<name>attname2</name>

<value>attvalue2</value>

</attribute>

attname1 and attname2 shall represent valid resource attribute names included in one of the resource types indicated in the rty field of the query-string. The sequence of attributes elements as shown in the above example shall be mapped into the query-string as  attname1=attvalue1&attname2=attvalue2. The attribute names shall be expressed in the form of short names as defined in clause 8.2.3 of TS-0004 [3].

Examples of valid Request-Target representations are the following:

Example 1): Request-Target for ‘nonBlockingRequestSynch’

Primitive parameters: 	To:						/CSE1234/RCSE78/container234        (SP-Relative-Resource-ID)

Response Type:	      responseType = 1     						(nonBlockingRequestSynch)

Result Persistence:	P1Y2M3DT10H1M0S	Request-Target:			/CSE1234/RCSE78/container234?rt=1&rp=P1Y2M3DT10H1M0S

Example 2):  Request-Target for Discovery

When the entity wants to discover container resources where the creator attribute has the value ‘Sam’:

Primitive parameters:	To:						/CSE1234/RCSE78

Filter Criteria:		resourceType = 3           (container)

attribute name:  creator

attribute value: Sam

filterUsage = discovery

Request-Target:			/CSE1234/RCSE78?rty=3&creator=Sam&fu=1

Table 6.2.2-1: oneM2M request parameters mapped as query-string field

| Request Primitive Parameter | Query Field Name | multiplicity | Note |
| --- | --- | --- | --- |
| Response Type | rt | 0..1 | responseType element of data type responseTypeInfo (cf. clause 6.3.4.29 of TS-0004 [3] |
| Result Persistence | rp | 0..1 |  |
| Result Content | rc | 0..1 |  |
| Delivery Aggregation | da | 0..1 |  |
| createdBefore | crb | 0..1 | filterCriteria condition |
| createdAfter | cra | 0..1 | filterCriteria condition |
| modifiedSince | ms | 0..1 | filterCriteria condition |
| unmodifiedSince | us | 0..1 | filterCriteria condition |
| stateTagSmaller | sts | 0..1 | filterCriteria condition |
| stateTagBigger | stb | 0..1 | filterCriteria condition |
| expireBefore | exb | 0..1 | filterCriteria condition |
| expireAfter | exa | 0..1 | filterCriteria condition |
| labels | lbl | 0..n | filterCriteria condition |
| resourceType | rty | 0..n | filterCriteria condition |
| sizeAbove | sza | 0..1 | filterCriteria condition |
| sizeBelow | szb | 0..1 | filterCriteria condition |
| contentType | cty | 0..n | filterCriteria condition |
| limit | lim | 0..1 | filterCriteria condition |
| attribute | atr | 0..n | filterCriteria condition |
| filterUsage | fu | 0..1 | filterCriteria condition |
| Discovery Result Type | drt | 0..1 |  |

### 6.2.3	HTTP-Version

This specification defines binding compliant with HTTP 1.1 [1] The HTTP version field in HTTP request messages shall be set to "HTTP/1.1".

## 6.3	Status-Line

### 6.3.1	HTTP-Version

The HTTP version field in HTTP response messages shall be set to "HTTP/1.1".

### 6.3.2	Status-Code

The Response Status Code parameter of response primitives shall be mapped to the HTTP Status-Code. Since the Response Status Code parameter values have been defined with more detailed information than HTTP status codes, one or more Response Status Code values may be mapped to the same HTTP Status-Code. The original Response Status Code parameter value shall be carried in the X-M2M-RSC Header (see clause 6.4.14).

The mapping of Response Status Code parameter values of oneM2M request primitive to Status-Code of  HTTP request messages is specified in Table 6.3.2-1.

Table 6.3.2-1: Status Code Mapping

| oneM2M Response Status Codes | HTTP Status Codes |
| --- | --- |
| 1000 (ACCEPTED) | 202 (Accepted) |
| 2000 (OK) | 200 (OK) |
| 2001 (CREATED) | 201 (Created) |
| 4000 (BAD_REQUEST) | 400 (Bad Request) |
| 4004 (NOT_FOUND) | 404 (Not Found) |
| 4005 (OPERATION_NOT_ALLOWED) | 405 (Method Not Allowed) |
| 4008 (REQUEST_TIMEOUT) | 408 (Request Timeout) |
| 4101 (SUBSCRIPTION_CREATOR_HAS_NO_PRIVILEGE) | 403 (Forbidden) |
| 4102 (CONTENTS_UNACCEPTABLE) | 400 (Bad Request) |
| 4103 (ACCESS_DENIED) | 403 (Forbidden) |
| 4104 (GROUP_REQUEST_IDENTIFIER_EXISTS) | 409 (Conflict) |
| 4105 (CONFLICT) | 409 (Conflict) |
| 5000 (INTERNAL_SERVER_ERROR) | 500 (Internal Server Error) |
| 5001 (NOT_IMPLEMENTED) | 501 (Not Implemented) |
| 5103 (TARGET_NOT_REACHABLE) | 404 (Not Found) |
| 5105 (NO_PRIVILEGE) | 403 (Forbidden) |
| 5106 (ALREADY_EXISTS) | 403 (Forbidden) |
| 5203 (TARGET_NOT_SUBSCRIBABLE) | 403 (Forbidden) |
| 5204 (SUBSCRIPTION_VERIFICATION_INITIATION_FAILED) | 500 (Internal Server Error) |
| 5205 (SUBSCRIPTION_HOST_HAS_NO_PRIVILEGE) | 403 (Forbidden) |
| 5206 (NON_BLOCKING_REQUEST_NOT_SUPPORTED) | 501 (Not Implemented) |
| 6003 (EXTERNAL_OBJECT_NOT_REACHABLE) | 404 (Not Found) |
| 6005 (EXTERNAL_OBJECT_NOT_FOUND) | 404 (Not Found) |
| 6010 (MAX_NUMBER_OF_MEMBER_EXCEEDED) | 400 (Bad Request) |
| 6011 (MEMBER_TYPE_INCONSISTENT) | 400 (Bad Request) |
| 6020 (MANAGEMENT_SESSION_CANNOT_BE_ESTABLISHED) | 500 (Internal Server Error) |
| 6021 (MANAGEMENT_SESSION_ESTABLISHMENT_TIMEOUT) | 500 (Internal Server Error) |
| 6022 (INVALID_CMDTYPE) | 400 (Bad Request) |
| 6023 (INVALID_ARGUMENTS) | 400 (Bad Request) |
| 6024 (INSUFFICIENT_ARGUMENT) | 400 (Bad Request) |
| 6025 (MGMT_CONVERSION_ERROR) | 500 (Internal Server Error) |
| 6026 (CANCELLATION_FAILED) | 500 (Internal Server Error) |
| 6028 (ALREADY_COMPLETE) | 400 (Bad Request) |
| 6029 (COMMAND_NOT_CANCELLABLE) | 400 (Bad Request) |

### 6.3.3	Reason-Phrase

The Reason-Phrase shall be omitted in HTTP response messages.

## 6.4	Header Fields

### 6.4.1	Host

The Host header shall be present in each HTTP request message.

While the Request-Target indicates a target resource on the Hosting CSE, the Host header indicates the Receiver CSE of the next hop in multi-hop communication scenarios. Therefore, the Request-Target is not changed but the Host header is changed each time when a request is forwarded to the next hop CSE.

The Host header shall be set as one of pointOfAccess attribute values of the Receiver (i.e. pointOfAccess attribute of the corresponding <remoteCSE> resource). Selection of the appropriate Receiver is described in oneM2M TS-0004 [3].

### 6.4.2	Accept

The Originator may use the Accept header to indicate which content-type it supports. The Accept header shall be mapped to a set of media types among ”application/xml”, “application/json”, ”application/vnd.onem2m-prsp+xml”, “application/vnd.onem2m-prsp+json”. Note that this information is not included in a request primitive.

### 6.4.3	Content-Type

Any HTTP request or response containing message-body shall include the Content-type header set to one of ”application/xml”, “application/json”, ”application/vnd.onem2m-res+xml”, “application/vnd.onem2m-res+json”, “application/vnd.onem2m-ntfy+xml” , “application/vnd.onem2m-ntfy+json”, “application/vnd.onem2m-attrs+xml” , “application/vnd.onem2m-attrs+json”.

Content-Type of the HTTP response should be chosen by the Hosting CSE considering Accept header given in the HTTP request. For example, if the Accept header in a request is set to “application/vnd.onem2m-prsp+xml”, then the response should use one of the oneM2M defined media types in XML serialization (see clause 6.7 [3]).

The value of the Resource Type primitive parameter, which is present in Create request primitives only, shall be appended to the Content-type of the corresponding HTTP request message in the form ty=value, separated by a semicolon character. A valid Content-Type header in this case looks e.g. as follows:

Content-Type: application/vnd.onem2m-res+xml; ty=3

### 6.4.4	Content-Location

The Content-Location header of HTTP response messages shall be set to the URI of the created resource, when responding to a Create request primitive. The URI shall be retrieved from the Content parameter of the response primitive. See clause 7.2.3.11 “Create a success response” in [3].

### 6.4.5	Content-Length

If message-body is included into HTTP request or response messages, the Content-Length header shall be included indicating the length of the message-body in octets (8-bit bytes).

### 6.4.6	Etag

A response primitive sent in reply to a resource retrieval request primitive should include an Etag header [x] in combination with the resource representation in the HTTP message body.

Etag facilitates the use of conditional requests (i.e. using the if-match and if-none-match HTTP headers) [x].

If a CSE supports the Etag header, then the CSE shall support conditional requests compliant with [x].

### 6.4.7	X-M2M-Origin

The X-M2M-Origin header shall be mapped to the From parameter of request and response primitives and vice versa, if applicable.

The X-M2M-Origin header value shall be assigned by the originator of the request (e.g. AE or CSE).

### 6.4.8	X-M2M-RI

The X-M2M-RI header shall be mapped to the Request Identifier parameter of request and response primitives and vice versa.

### 6.4.9	X-M2M-NM

The X-M2M-NM header shall be mapped to the Name parameter of request primitives and vice versa, if applicable.

### 6.4.10	X-M2M-GID

The X-M2M-GID header shall be mapped to the Group Request Identifier parameter of request primitives and vice versa, if applicable.

### 6.4.11	X-M2M-RTU

The X-M2M-RTU header shall be mapped to the notificationURI element of the Response Type parameter of request primitives and vice versa, if applicable. If there are more than one value in the element, then the values shall be combined with “&” character.

### 6.4.12	X-M2M-OT

The X-M2M-OT header shall be mapped to the Originating Timestamp parameter of request and response primitives, and vice versa, if applicable.

### 6.4.13	X-M2M-RST

The X-M2M-RST header shall be mapped to the Result Expiration Timestamp parameter of request and response primitives, and vice versa, if applicable.

### 6.4.14	X-M2M-RET

The X-M2M-RET header shall be mapped to the Request Expiration Timestamp parameter of request primitives and vice versa, if applicable.

### 6.4.15	X-M2M-OET

The X-M2M-OET header shall be mapped to the Operation Execution Time parameter of request primitives and vice versa, if applicable.

### 6.4.16	X-M2M-EC

The X-M2M-EC header shall be mapped to the Event Category parameter of request and response primitives, and vice versa, if applicable.

### 6.4.17	X-M2M-RSC

The X-M2M-RSC header in a HTTP response message shall be mapped to the Response Status Code parameter of response primitives and vice versa.

### 6.4.18	X-M2M-TO

The X-M2M-TO header in a HTTP response message shall be mapped to the To parameter of response primitives and vice versa.

## 6.5	Message-body

Message-body shall be mapped to the Content parameter of request and response primitives, and vice versa, if applicable.

## 6.6	Message Routing

HTTP request and response message routing shall be performed as described in HTTP/1.1 [1].

# 7	Security Consideration

## 7.1	Authentication on HTTP Request Message

When sending the credential to be checked by the Registrar CSE, Proxy-Authorization header should be used as specified in HTTP/1.1 (see [4]).

When sending the credential to be checked by Hosting CSE, Authorization header should be used as specified in HTTP/1.1 [4].

When the credential to be checked by Hosting CSE is an Access Token which is compatible with OAuth 2.0 framework (see [5]), the Bearer authentication scheme shall be used as specified in OAuth 2.0 framework.

NOTE:	The oneM2M Security Solutions [2] does not provide any details on usage or provisioning of the token.

## 7.2	Transport Layer Security

oneM2M primitive parameters contained in HTTP messages may be protected by TLS in a hop-by-hop manner. For the details, see the oneM2M Security Solutions specification [2].

NOTE:	Some provisioning schemes of oneM2M TS-0003 [2] enable the provisioning of end-to-end credentials, but protocols to establish security associations between non-adjacent nodes are not addressed.by oneM2M in the present release.

Annex A (informative):
Example Procedures

# A.1	<container> resource creation

Figure A.1-1 is HTTP mapping of procedure described in clause 7.3.7.2.1.

Figure A.1-1: oneM2M HTTP Binding Example - container creation

Annex B (informative):
WebSocket

# B.1	Notification using WebSocket

WebSocket [i.4] can be used for transporting notifications to an AE/CSE. This can be useful for an AE/CSE which is not server-capable or cannot be reachable for delivery of unsolicited requests.

For example, when an AE needs to receive a notification message from the CSE, the AE establishes a WebSocket connection to a CSE. When a new notification message is generated, the notification will be sent to the AE as the data frame of the WebSocket.

### -----------------------End of change 1-------------------------------------------