| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | KT Corp. |
| Format:* | Face-to-Face Meeting |
| Date:* | 2015-03-15 |
| Contact:* | Francisco Sang-Eon Kim (kim.sangeon@kt.com) |
| Reason for Change/s:* | This contribution is proposed to primitive naming about API. |
| CR against: Release* | Release 1 & Release 2 |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* | 5.3.X |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Review of Release 1 TS of architecture and protocol

The functional architecture, TS-0001-V1.6.1, specifies including resource structure, resource type and information flows.

The resource types are defined in section 9.6.1.1 of which title is ‘Resource Type Summary’. The resource types are accessControlPolicy, AE, container, contentInstance, CSEBase, delivery, eventConfig, execInstance, fanOutPoint (V), group, , latest (V), locationPolicy, mgmtCmd, mgmtObj, m2mServiceSubscriptionProfile, node, oldest(V), pollingChannel, pollingChannelURI(V), remoteCSE, request, schedule, serviceSubscribedNode, statsCollect, StatsConfig, subscription, serviceSubscribedAppRule.

The information flow is specified in section 10.1. It is about such procedures as create (C), retrieve (R), update (U), delete (D), notify (N) for resource types.

The service layer core protocol specification, TS-0004-V1.0.1, specifies including protocol design principles, API and primitive formats.

Problem of primitive naming

A developers are hard to find a rule for primitive naming. The primitive naming is described implicitly. Developers can assume naming rule of primitives which is ‘ <resource>PROCRDURES’ from section 10.2 in TS-0001. The results of an example from this assumption is ‘homeapplicationCREATE’, ‘homeapplicationRETRIEVE’, ‘homeapplicationUPDATE’, ‘homeapplicationDELETE’ and so on. In this case ‘homeapplicationCREATE’ is for application registration.

A developers can assume primitive naming such as <resource>Procedures’ from section 7.3 in TS-0004. The results of an example from this assumption is ‘homeapplicationCreate’, ‘homeapplicationRetrieve’, ‘homeapplicationUpdate’, ‘homeapplicationDelete’ and so on.

In this contribution, I use ‘Procedures’ instead of ‘Methods’ or ‘Verbs’ for Create/Retrive/Update/Delete/Notify. The method is generally accepted term for software development. However, TS-0001 is used for method as similar meaning of resource at section 9.6.10 which state that “The <locationPolicy> resource represents the method for obtaining and managing geographical location information of an M2M Node.” 9.6.11, 9.6.16 has stated that method is similar meaning of resource. TS-0004 uses procedures instead of methods, That’s why I use term of procedure.

When manufacturer of field domain uses different primitive name from infrastructure domain for same functionality, it is not working between CES of device and CSE of infrastructure at Mcc reference point. Because developers for CSE of device and infrastructures are different.

Discussion on Components of primitive naming

A component of primitive naming can be considered resource, procedure and communication flow.

The TS-0001 is specified resource at section 9 and procedure at section 10 as reviewed above.A communicatuion flow is ‘Request’ and ‘Response’ as specified at section 8 in TS-0001.

It is possible to primitive name with combination of resource, procedure and communication flow.

For example, originator that use nodeCreateRequest primitive is difficult to communicate receiver that use ResponseNodeCreate or nodeResponseCreate primitive

## ----------------------- Start of change 1 -----------------------

### 5.3.X Naming of primitives

Primitive name consists of information of resource, procedure and communication flow. Resources are specified at section 9 and procedure at section 10 in [6]. Communicatuion flow is ‘Request’ and ‘Response’ as specified at section 8 in [6].

Primitive name is a concatenation of resource name, procedure and communication flows. It starts with lower case of resource. Procrdure and communication flow start with a capital letter; e.g. accessControlPolicyCreateRequest, accessControlPolicyCreateResponse, groupCreateRequest, groupRetriveResponse

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?