| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 16.0 |
| Source:* | FUJITSU |
| Date:* | 2015-03-16 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | The specification to receive Notification request over WebSocket was imcompleted on Release 1. |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0009 |
| Clauses/Sub Clauses* | Annex. B |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

WebSocket is popular mechanism to use HTTP infrastructure as bidirectional communication channel.

Annex. B of TS-0009 is mentioning sending Notfication message over WebSocket, but it is imcompleted for developpers.

This CR aims providing supplemental information to implement WebSocket based Notification.

### -----------------------Start of change 1-------------------------------------------

Annex B (normative):
WebSocket

# B.1	Notification using WebSocket

WebSocket [i.4] can be used for transporting notifications to an AE/CSE. This can be useful for an AE/CSE which is not server-capable or cannot be reachable for delivery of unsolicited requests.

When an AE needs to receive a notification message from the registrar CSE and the AE decided to use WebSocket based communication channel to receive notification message, the AE shall establishes a WebSocket connection to a CSE for accessing reserved URI "/wschannel". The pointOfAccess attribute of <AE> resource shall be set with the string value "wschannel" to indicate WebSocket channel shall be used to retarget notification message.

When a new notification message is delivered to registrar CSE and the pointOfAccess attribute of <AE> resource, the notification shall be sent to the AE as the data frame of the WebSocket. The opcode of the data frame shall be "0x1(Text)". The payload data shall be m2m:primitiveContent serialized as JSON Object. Note that re-targeted primitive request shall not be generate response.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?