| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#16 |
| Source:* | Sung-Chan Choi, Yong-Suk Park, Jaeho Kim, Peter Niblett |
| Date:* | 2015-03-24 |
| Contact:* | Sung-Chan Choi (csc@keti.re.kr) |
| Reason for Change/s:* | The section 6.4.5 needs to have description aligned with 6.4.2, 6.4.3, and 6.4.4 |
| CR against: Release* | Rel-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0010-v1.0.1 |
| Clauses/Sub Clauses* | 6.4.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Section 6.4.5 (Reqeuset/Response Message Flow) is not align with 6.4.2, 6.4.3, and 6.4.4. Therefore, in section 6.4.5, the description about topic name when MQTT clients start initial process and the description about Request/Response message delivery over MQTT need to be changed.

Changes in R02.

- Replace <from> and <to> with <originator> and <receiver throughout clause 6.4

- Introduce escaping  rules for Topic strings to accommodate AE-IDs and CSE_IDs that contain  “/” characters

### -----------------------Start of change 1-------------------------------------------

### 6.4.2	Sending a Request

A request is transmitted by sending it as an MQTT PUBLISH protocol packet to the MQTT Server. It uses a Topic that identifies both the Originator and the Receiver of the request as follows:

/oneM2M/req/<originator>/<receiver>

"oneM2M" is a literal string identifying the topic as being used by oneM2M.

<originator> is the SP-relative-AE-ID or SP-relative-CSE-ID of the entity that sent the request on this hop, omitting any leading /. In the AE-ID case, any / characters embedded in the ID shall be replaced with : characters.

<receiver> is the SP-relative-CSE-ID of the Receiver  (Transit or Hosting CSE), omitting any leading /

"req" is a literal string identifying this as a request.

The payload of the MQTT PUBLISH packet is used to carry the request primitive, as described in clause 6.5.

### 6.4.3	Listening for and responding to a Request

A Receiver listens for requests arriving via MQTT by subscribing to its Topics using a wildcarded topic filter of the following form

- /oneM2M/req/+/<receiver>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- + is a wildcard which matches any Originator

- <receiver> is the  SP-relative-CSE-ID of the Receiver  (Transit or Hosting CSE), omitting any leading /

- “req” is a literal string identifying this as a request.

When it receives a request, the Receiver shall perform the Core Transport operations associated with the request, including any access control policy checks. In particular it shall check the request expiration timestamp (if any) contained in the request, since it is possible that that time might have passed while the message was being stored by MQTT.

It transmits a response by sending an MQTT PUBLISH packet to a response topic. This takes the form:

/oneM2M/resp/<originator>/<receiver>

"oneM2M" is a literal string identifying the topic as being used by oneM2M.

<receiver> is the SP-relative-CSE-ID of the Receiver  (Transit or Hosting CSE) of the original request, omitting any leading /

<originator> is the SP-relative-AE-ID or SP-relative-CSE-ID of the entity that sent the original request on the current hop, omitting any leading /. In the AE-ID case, any / characters embedded in the ID shall be replaced with : characters.

"resp" is a literal string identifying this as a response.

The Originator shall subscribe to this Topic (either explicitly or using a wildcarded filter) in order to see the response.

The payload of the MQTT PUBLISH packet is used to carry the response primitive, as described in clause 6.5.

### Initial Registration

In some security scenarios, an Originator might not initially know its AE-ID or CSE-ID. Initial registration exchanges can use the communication pattern described in clauses 6.4.1 and 6.4.2 except that they use Topics containing a credential ID rather than an AE-ID or CSE-ID, as follows:

- /oneM2M/reg_req/<originator>/<receiver>

and

- /oneM2M/reg_resp/<originator>/<receiver>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- <originator> is Credential-ID. Any / characters embedded in the ID shall be replaced with : characters.

- <receiver> is the  SP-relative-CSE-ID of the Receiver  (Transit or Hosting CSE), omitting any leading /

- “reg_req” and “reg_resp” are literal strings identifying them as registration requests and responses.

### 6.4.5	Request/Response Message Flow

Figure 6.4.5-1: Initiating Process in MQTT binding

In the MQTT protocol, each client shall subscribe to the MQTT server to receive messages. As shown in figure 6.4.5.1-1, the AE or CSE initiates the MQTT binding process by trying to connect to the MQTT server, as described in clause 6.3..

After each MQTT client successfully connects to the server, it shall subscribe to the MQTT server. The topic names which each MQTT client subscribes to are “/oneM2M/req/+/<receiver>” (to receive requests) and “/oneM2M/resp/<originator>/+” (to receive replies) where <receiver> and <originator> are both set equal to the ID (SP-relative-AE-ID or SP-relative-CSE-ID as appropriate).

Accordingly, the plus sign (‘+' U+002B) wildcard with the SP-relative-AE-ID or SP-relative-CSE-ID is used as the topic name within the MQTT SUBSCRIBE packet. This enables MQTT client to receive the PUBLISH packets whose target it is. Through this process, therefore, AE or CSE receives messages if the request/response messages are published to oneM2M/req/<originator>/<receiver> or oneM2M/resp/<originator>/<receiver>.

Figure 6.4.5-2: Request/Response message delivery over MQTT

As an example, figure 6.4.5-2 illustrates the request/response message delivery over MQTT protocol between AE and CSE via Mca reference point in oneM2M. The message flow is as follows.

In this scenario, the AE wants to send a Request message to the registered CSE. After that, the AE's MQTT client library sends an MQTT PUBLISH packet to the MQTT server with "oneM2M/req/SP-relative-AE-ID/SP-relative-CSE-ID" as the topic name. The MQTT PUBLISH packet can include {"op", "fr", "to", "ri", "pc", "ty"} and any other optional message parameters described in clause 8 of [3] in its payload.

After the MQTT server receives the MQTT PUBLISH packet from the MQTT client, the server refers to the topic name and delivers the message to the intended MQTT client. Finally, the MQTT client library delivers the message to the CSE.

Regarding the Response message, the MQTT messages are sent using “oneM2M/resp/<originator>/<receiver>” as topic. In order to send a Response message to the requestor, the CSE can use the "fr" information from the received request message or topic name of the MQTT PUBLISH packet related with the received request message. After that, the CSE sends an MQTT PUBLISH packet to the MQTT server with "oneM2M/resp/SP-relative-AE-ID/ SP-relative-CSE-ID " as the topic name in this scenario. In addition, the MQTT PUBLISH packet can include {"rsc", “fr”, “to”, "ri", "pc"} and any other optional message parameters described in clause 8 of [3] in its payload.

Similar to the request message delivery from AE to CSE, the MQTT server delivers the published packet to the intended MQTT client by referring to the topic name. Finally, AE receives the response message from the MQTT client.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?