| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#16 |
| Source:* | Qualcomm Inc. |
| Date:* | 2015-03-22 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Corrections to Filter Criteria usage and related data types |
| CR against: Release* | Release-1 |
| CR against: WI* | Active < Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004v1.0.1 |
| Clauses/Sub Clauses* | 6.3.6, |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The review of XSD files after the PRO#15 meeting in Miami has discovered a number of inconsistencies between data type definitions in TS-0004 and in the XSD files. These issues are summarised in the Excel sheet attached to PRO-2015-0730.

This CR aims to add missing data type definitions related to the Filter Criteria primitive parameter and thereby to correct the text in clause 6.3.6 which specifies the usage of these parameters and the matching conditions .

Note: this revision is an incomplete CR version present for discussion how to proceed with remaining issues.

### -----------------------Start of change 1-------------------------------------------

    - Filter criteria

The request primitive parameter Filter Criteria is represented as a sequence of elements as defined in the m2m:filterCriteria data type in clause 6.2.4.8. The Filter Criteria primitive parameter applies to retrieve request primitives only. It defines a set of conditions which are compared with the actual values of resource attributes. If the  attribute value matches any of the search condition given in the Filter Criteria parameter, the resource shall be retrieved and returned to the originator in the format defined in the Response Type and/or Discovery Result Type primitive parameters, provided access control policies associated with those resources permit access to the originator of the request primitive. Search conditions are defined either by an individual element given in the Filter Criteria parameter, or by a combination of two or more of such elements. The applicable conditions are defined in the following subsections.

If multiple conditions are provided in the Filter Criteria parameter, these shall be matched all to pass the criterion.

#### creationTime condition

The creationTime condition defines a time interval which is tested against the creationTime attribute of the resource instances. The creationTime condition is defined by two Filter Criteria elements, createdBefore and createdAfter. The data type of creationTime, createdBefore and createdAfter is m2m:timestamp.

The creationTime condition is satisfied if any of the following three conditions is fulfilled:

- createdBefore only given in Filter Criteria:

condition:   if (creationTime <  createdBefore)

- createdAfter only given in Filter Criteria:

condition:   if (createdAfter < creationTime)

- both, createdBefore and createdAfter given in Filter Criteria:

condition:   if ((createdAfter < creationTime) AND (creationTime <  createdBefore))

NOTE:  Case 3) requires createdAfter < createdBefore to derive a matching condition.

#### lastModifiedTime condition

The lastModifiedTime condition defines a time interval which is tested against the lastModifiedTime attribute of the resource instances. The lastModifiedTime condition is defined by two Filter Criteria elements, lastModifiedBefore and lastModifiedAfter. The data type of lastModifiedTime, lastModifiedBefore and lastModifiedAfter is m2m:timestamp.

The lastModifiedTime condition is satisfied if any of the following three conditions is fulfilled:

- lastModifiedBefore only given in Filter Criteria:

condition:   if (lastModifiedTime <  lastModifiedBefore)

- lastModifiedAfter only given in Filter Criteria:

condition:   if (lastModifiedAfter < lastModifiedTime)

- both, lastModifiedBefore and lastModifiedAfter given in Filter Criteria:

condition: if ((lastModifiedAfter < lastModifiedTime) AND (lastModifiedTime <  lastModifiedBefore))

NOTE:  Case 3) requires lastModifiedAfter < lastModifiedBefore to derive a matching condition

#### stateTag condition

The stateTag condition defines a number range which is tested against the value of the stateTag attribute given in the resource instances. The stateTag condition is defined by two Filter Criteria elements, stateTagSmaller and stateTagBigger. The data type of stateTag and stateTagBigger is xs:nonNegativeInteger. The data type of stateTagSmaller is xs:positiveInteger.

The stateTag condition is satisfied if any of the following three conditions is fulfilled:

- stateTagSmaller only given in Filter Criteria:

condition:   if (stateTag <  stateTagSmaller)

- stateTagBigger only given in Filter Criteria:

condition:   if (stateTagBigger < stateTag)

- both, stateTagSmaller and stateTagBigger given in Filter Criteria:

condition: if ((stateTagBigger < stateTag) AND (stateTag <  stateTagSmaller))

NOTE:  Case 3) requires stateTagBigger < stateTagSmaller to derive a matching condition.

#### expirationTime condition

The expirationTime condition defines a number range which is tested against the value of the expirationTime attribute given in the resource instances. The expirationTime condition is defined by two Filter Criteria elements, expiredBefore and expiredAfter. The data type of expirationTime and expiredBefore and expiredAfter is m2m:timestamp.

The expirationTime condition is satisfied if any of the following three conditions is fulfilled:

- expiredBefore only given in Filter Criteria:

condition:   if (expirationTime <  expiredBefore)

- expiredAfter only given in Filter Criteria:

condition:   if (expiredAfter < expirationTime)

- both, expiredBefore and expiredAfter given in Filter Criteria:

condition: if ((expiredAfter < expirationTime) AND (expirationTime <  expiredBefore))

NOTE:  Case 3) requires expiredAfter < expiredBefore to derive a matching condition.

#### labels condition

The labels condition is defined by a list of labels which is tested against the labels attribute of the resource instances. The list of lables shall be provided in the labels element of Filter Criteria parameter. The data type of both, labels in Filter Criteria and the labels resource attribute, is m2m:labels, which represents a list of xs:token (see clause 6.3.2).

The labels condition is satisfied if any of the labels in Filter Criteria matches any of the labels in the resource attribute.

#### resourceType condition

The resourceType condition is defined by a list of resource types which is tested against the resourceType attribute of the resource instances. The list of resource types shall be provided in the resourceType element of the Filter Criteria parameter. The data type of resourceType in Filter Criteria is a list of m2m:resourceType and the resourceType attribute, is m2m:labels, which represents a list of xs:token (see clause 6.3.2).

The labels condition is satisfied if any of the labels in Filter Criteria matches any of the labels in the resource attribute.

The condition matches with the resource which resourceType attribute value is specified value.

Table 6.3.6.6-1: Definition of Resource Type Match condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| single type | m2m:resourceType |  |
| multiple types | list of m2m:resourceType | separator of list elements shall be specified in protocol bindings. |
| NOTE: |

#### contentSize condtion

The condition matches with the contentSize attribute of the <contentInstance> resources is in range of specified numerica value range.

Table 6.3.6.7-1: Definition of Content Size Match condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| sizeBelow | xs:nonNegativeInteger |  |
| sizeAbove | xs:nonNegativeInteger |  |
| NOTE: |

#### typeOfContent condition

The condition matches with the typeOfContent attribute of the <contentInstance> resource is the specified value.

Table 6.3.6.8-1: Definition of Content Type Match condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| content type | xs:token | The one of the Content-Type string shall be specified |
| content sub-types | xs:token after ‘:’ character. | The one of the Content sub-type strings shall be specified. |
| NOTE: |

#### attribute Match condition

The condition matches with the resources which all attribute/value pairs are specified combination.

Table 6.3.6.9-1: Definition of Attribute Match condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| single pair | concatenation of xs:token with ‘:’ character. | first token shall be shortname of attribute and second token shall be its value. |
| multiple pairs | list of single pairs. | separator of list elements shall be specified in protocol bindings. |
| NOTE: |

#### Limit results request parameter

Limitation the number of matching resources to the specified value.

Table 6.3.6.10-1: Definition of Limit conditions

| Format Variants | Definition | Note |
| --- | --- | --- |
| limits | xs:nonNegativeInteger |  |
| NOTE: |

#### Filter Usage request parameter

Indicates how the Filter Criteria parameter shall be used. E.g. if this parameter is not provided, the Retrieve operation is for generic retrieve operation.

Table 6.3.6.11-1: Definition of Filter Usage

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Discovery Criteria |  |
| 2 | Event Notification Criteria |  |
| NOTE: |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

##### m2m:filterUsage

Used in m2m:filterCriteria.

Table 6.3.3.2.31-1: Interpretation of filterUsage

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Discovery Criteria |  |
| 2 | Event Notification Criteria |  |

### -----------------------End of change 2-------------------------------------------