| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#16 |
| Source:* | Qualcomm Inc. |
| Date:* | 2015-03-27 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Corrections to Filter Criteria usage and related data types |
| CR against: Release* | Release-1 |
| CR against: WI* | Active < Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004v1.0.1 |
| Clauses/Sub Clauses* | 6.3.6, |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The review of XSD files after the PRO#15 meeting in Miami has discovered a number of inconsistencies between data type definitions in TS-0004 and in the XSD files. These issues are summarised in the Excel sheet attached to PRO-2015-0730.

This CR aims to add missing data type definitions related to the Filter Criteria primitive parameter and thereby to correct the text in clause 6.3.6 which specifies the usage of these parameters and the matching conditions.

Note: this revision is an incomplete CR version present for discussion how to proceed with remaining issues.

Changes in R02 relative to initial version:

- removed all proposed changes on clarification of the filter conditions. This will be addressed in a separate CR which will be presented after TP#16.

- the changes addressed in this version only address the issue of the filterUsage parameter.

### -----------------------Start of change 1-------------------------------------------

#### Filter Usage request parameter

The filterUsage element of the Filter Criteria parameter does not represent a filter condition. It indicates how the Filter Criteria parameter shall be used. If this parameter is not provided, the Retrieve request primitive which includes this element  triggers a generic retrieve operation. The data type of filterUsage is defined in clause 6.3.3.2.31.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

##### m2m:filterUsage

Used in m2m:filterCriteria.

Table 6.3.3.2.31-1: Interpretation of filterUsage

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Discovery Criteria |  |
| 2 | Event Notification Criteria |  |

### -----------------------End of change 2-------------------------------------------