| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#17.1 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2015-06-08 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | XSD name for Content primitive parameter |
| CR against: Release* | R1 |
| CR against: WI* | Active – WI-0009 (PRO) MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TS-0004-v1.1.0 |
| Clauses/Sub Clauses* | 7.1.1, 7.4.2, 8.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

At TP#17, PRO-2015-0758R03-CR_for_TS-0004_ShortNames was agreed which has reassigned some names of resource attributes, request parameters and of elements of complex data types in order to allow a one-to-one mapping correspondence between short and long names.

PRO-2015-0758R03 proposed to change the XML element name used for the Content primitive parameter, from ‘content’ to ‘primitiveContent’.

However, when implementing this name change in CDT-requestPrimitive-v1_2_0.xsd and CDT-responsePrimitive-v1_2_0.xsd the question came up whether or not the changes shown in PRO-2015-0758R03 really justify this name change since none of the data types given that this change is not reflected in a change of any data type shown in clause 6.3 of TS-0004.

The reason is that data types for resources and primitives are defined anonymously and therefore do not appear in clause 6.3 of TS-0004 but instead show up in tables of clauses 7.1 (primitives) and 7.3 (resource types) that specify the data types to be used for the primitive parameters and resource attributes.

However in order to clarify the relation between primitive parameters and their corresponding names in the XML  representations, especially for the Content primitive parameter,  this CR proposes some additional text changes to clauses 7.1.1 (Primitive format) and 7.4.2 (Elements contained in the primitive Content), and 8 (Representation of primitives in data transfer)

### -----------------------Start of change 1-------------------------------------------

### Primitive format

#### Request primitive format

Table 7.1.1.1-1 summarizes the primitive parameters of  the Request primitive, indicating their presence depending on the C, R, U, D or N operations. "M" indicates mandatory, "O" indicates optional, "NP" indicates not present. The Table also shows the (long) name used in XML representations of request primitives (see clauses 7.4.2 and 8).

Refer to clause 8.1.2 of the oneM2M TS-0001 [6] for additional information on the request primitive parameters.

Table 7.1.1.1-1: Request Primitive Parameters

| Primitive Parameter | XML name | CREATE | RETRIEVE | UPDATE | DELETE | NOTIFY |
| --- | --- | --- | --- | --- | --- | --- |
| Operation | operation | M | M | M | M | M |
| To | to | M | M | M | M | M |
| From | from | M | M | M | M | M |
| Request Identifier | requestIdentifier | M | M | M | M | M |
| Resource Type | resourceType | M | NP | NP | NP | NP |
| Name | name | O | NP | NP | NP | NP |
| Content | primitiveContent | M | O | M | NP | M |
| Originating Timestamp | originating imestamp | O | O | O | O | O |
| Request Expiration Timestamp | requestExpirationTimestamp | O | O | O | O | O |
| Result Expiration Time | resultExpirationTime | O | O | O | O | O |
| Operation Execution Time | operationExecutionTime | O | O | O | O | O |
| Response Type | responseType | O | O | O | O | O |
| Result Persistence | resultPersistence | O | O | O | O | NP |
| Result Content | resultContent | O | O | O | O | NP |
| Event Category | eventCategory | O | O | O | O | O |
| Delivery Aggregation | deliveryAggregation | O | O | O | O | O |
| Group Request Identifier | groupRequest Identifier | O | O | O | O | O |
| Filter Criteria | filterCriteria | NP | O | O | O | NP |
| Discovery Result Type | discoveryResultType | NP | O | NP | NP | NP |

The Content parameter in a Request shall contain one of the following:

- A complete or partial Resource. In this case the Content shall contain a single element whose name is the name of the Resource and whose content consists of one or more attributes, child Resources or childResource references. In this case the resource type is as defined in clause 7.3, however if a partial resource is being transferred, it is not required to be valid according to the XSD for that resource.

A Notification Data Object. This is named <m2m:notification> and is described in Clause 7.4.1

An Aggregated Notification. This is named <m2m:aggregatedNotification> and contains multiple <m2m:notification> objects. This is described in clause 7.4.1.

An AttributeList element, as described in clause 7.4.2. This is used in the partial retrieval case to pass a set of attribute Names  (by leaving the attribute values blank). In the partial update case it is used to pass a set of attribute Name/Value pairs.

A ResponsePrimitive object as described in clause 7.4.1.  This is used in Asynchronous non-blocking case.

#### Response primitive format

Table7.1.1.2-1 summarizes the primitive parameters for Response primitive, indicating their presence depending on the C, R, U, D or N operations of the associated Request primitive and whether this operation was successful or caused an error. "M" indicates mandatory, "O" indicates optional, "NP" indicates not present. The Table also shows the (long) name used in XML representations of response primitives (see clauses 7.4.2 and 8).

Refer to clause 8.1.3 of TS-0001 [6] for additional information on the request primitive parameters.

NOTE: Response Code and Status Code parameters are merged into the Response Status Code parameter.

Table7.1.1.2-1 : Response Primitive Parameters

| Primitive parameter | XML name | Ack | CREATE Success | RETRIEVE Success | UPDATE Success | DELETE Success | NOTIFY Success | Error |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Response Status Code | responseStatusCode | M | M | M | M | M | M | M |
| Request Identifier | requestIdentifier | M | M | M | M | M | M | M |
| Content | primitiveContent | O | O | M | O | O | O | O |
| To | to | O | O | O | O | O | O | O |
| From | from | O | O | O | O | O | O | O |
| Originating Timestamp | originatingTimestamp | O | O | O | O | O | O | O |
| Result Expiration Timestamp | resultExpirationTimestamp | O | O | O | O | O | O | O |
| Event Category | eventCategory | O | O | O | O | O | O | O |

The Content parameter in a Response shall contain one of the following:

- A complete or partial Resource. In this case the Content shall contain a single element whose name is the name of the Resource and whose content consists of one or more attributes, child Resources or childResource references. In this case the resource type is as defined in clause 7.3, however if a partial resource is being transferred, it is not required to be valid according to the XSD for that resource.

The URI of a resource. This is included directly as the content of the Content parameter (like in case 6)

A partial resource and its hierarchical URI. These are included in an element called m2m:resource defined in clause 7.4.2. The URI is included as an attribute of m2m:resource.

A list of URIs. This can  be used for transferring the childResource URIs only or in a Discovery response. These are included in an element called m2m:URIList defined in clause 7.4.2.

An Aggregated Response. This is sent as a result of a Group operation. This uses the element m2m:aggregatedResponse defined in clause 7.4.2.

Raw data. This could be a simple data value, or structured data (an XML complex type or JSON object)

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### Elements contained in the Content primitive  parameter

Clauses 7.1.1.1 and 7.1.1.2 enumerate the forms that the Content primitive parameter takes in various Request and Response cases. Note that the Content primitive parameter is denoted as primitiveContent in both, CDT-requestPrimitive-v1_2_0.xsd and CDT-responsePrimitive-v1_2_0.xsd.

This clause details the Objects (elements) used in some of these cases. in the tables below.

The following elements are defined for use in the content parameter of a request:

Table 7.4.2-1: Elements used for request content

| Element Name | Applicable Operations | Data Type | Defined in |
| --- | --- | --- | --- |
| m2m:notification | N | m2m:notification | CDT-notification-v1_0_0.xsd |
| m2m:aggregatedNotification | N | m2m:aggregatedNotification | CDT-notification-v1_0_0.xsd |
| m2m:attributeList | R | m2m:attributeList | CDT-requestPrimitive-v1_0_0.xsd |
| m2m:responsePrimitive | N | m2m:responsePrimitive | CDT-responsePrimitive-v1_0_0.xsd |

The following elements are defined for use in the content parameter of a response:

Table 7.4.2-2: Elements used for response content

| Element Name | Applicable Operations | Data Type | Element is Defined in |
| --- | --- | --- | --- |
| m2m:resource | C R U | m2m:resourceWrapper | CDT-responsePrimitive-v1_0_0.xsd |
| m2m:URIList | R | m2m:listOfURIs | CDT-responsePrimitive-v1_0_0.xsd |
| m2m:aggregatedResponse | C R U D | m2m:aggregatedResponse | CDT-responsePrimitive-v1_0_0.xsd |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3---------------------------------------------

## XML serialization

### Method

XML serialization of request or response primitives refers to the process of representing the primitive as an XML document.

The XML document shall be a well-formed XML document compliant with W3C XML 1.0 [1]. It shall be restricted to Unicode characters and encoded using UTF-8 as described in RFC 3629 [21].

The structure and data types of XML serialized request and response primitives shall be consistent with the XSD defined in CDT-requestPrimitive-v1_0_0.xsd and CDT-responsePrimitive-v1_0_0.xsd, respectively. The data types used in these XSD files comply with the definitions in clause 6 and clause 7 of this specification.

Note that the XSD files included in the present release employ the long names for primitive parameters and other XML elements and attributes, but the primitive serialization is required to use the corresponding short names (as defined clause 8.2 of this specification).

NOTE: XML Schema files that use short names might be made available at a future date.

The Content primitive parameter (denoted primitiveContent in CDT-requestPrimitive-v1_0_0.xsd) is serialized just like any other element of complex type. Generally, the Content parameter may include only a partial set of attributes specified for the resource type as indicated in the Resource Type parameter, e.g. for partial Update or Retrieve Request procedures. For Notification Request primitives, the Content parameter includes a Notification data object as defined in clause 7.4.1.1 and the datatype definition given in CDT-notification-v1_0_0.xsd.

### Examples

An example that shows a request primitive serialized into an XML document is shown below. This example shows the create request for an instance of a <contentInstance> resource. Only mandatory primitive parameters and resource attributes are shown.

<?xml version="1.0" encoding="UTF-8"?>
<m2m:rqp xmlns:m2m="http://www.onem2m.org/xml/protocols"
 xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"
 xsi:schemaLocation="http://www.onem2m.org/xml/protocols CDT-requestPrimitive-v1_0_0.xsd">
    <op>1</op>
    <to>//cse1.mym2msp.org/</to>
    <fr>//cse1234/app567</fr>
    <ri>0002bf63</ri>
    <ty>4</ty>
    <pc>
        <cin rn="temp754">
            <cnf>application/xml:1</cnf>
            <con>PHRpbWU+MTc4ODkzMDk8L3RpbWU+PHRlbXA+MjA8L3RlbXA+DQo=</con>
        </cin>
    </pc>
</m2m:req>

The XML elements have the following meaning:

- rpq:  Root element of the Request primitive, which includes a reference to an XSD file which defines its datatype.

- op: 	Operation parameter of datatype m2m:operation:  in this example value = 1 indicates a “Create” operation.

- to: 	To parameter of type m2m:anyURI: URI of the target resource.

- fr: 	From parameter of type m2m:ID: ID of the Originator (either AE-ID or CSE-ID).

- ri: 	Request Identifier parameter of type m2m:requestID: this could e.g. represent a counter number.

- ty: 	Resource Type parameter of datatype m2m:resourceType: indicating type of the resource to be created (value = 4 indicates that a <contentInstance> resource shall be created).

- pc: 	Content parameter of datatype m2m:primitiveContent: the attributes of the resource to be provided by the Originator.

- cin:  Root element of the <contentInstance> resource of datatype m2m:contentInstance: this includes the mandatory attributes  (and optional attributes not shown in this example) supplied by the request Originator. The instance name is given in the XML name attribute, here rn="temp754". In this example, the cn parameter includes an instance of a <contentInstance> resource which consists of two attributes: contentInfo (cnf) – which specifies base64 encoding - and the content (con) itself.

## JSON serialization

### Terminology

The following conventions are used in the clause that follows.

- The italicized terms object, member, name, array, number, string, boolean and null are to be interpreted as in RFC 7159 [19]

- The italicized term element is to be interpreted to encompass oneM2M Primitive Parameters, Resource Attributes and other elements or attributes used inside oneM2M complex type definitions

### Method

The primitive shall be encoded as a JSON object, conforming to the requirements of RFC 7159 [19]. This JSON object shall be restricted to Unicode characters defined in The Unicode Standard and encoded using UTF-8 as described in RFC 3629 [21].  The names in each object in the JSON shall be unique.

The structure of the top-level primitive object shall be determined by the data type definitions in clause 6 and clause 7 of this specification, as follows:

- All member’s names shall be the short name defined in clause 8.2.

- If an element is defined in this specification as having a complex type, then it is serialized in the JSON member as an object and its children are recursively serialized as members of that object, using short names as defined in clause 8.2.

- The membership of each nested object shall respect the cardinality constraints from the corresponding XSD complex type definition,

- If an element is defined in this specification as having an atomic data type that is numeric in nature (e.g. xs:integer or a type derived from it) then its value is serialized into the JSON member as a number.

- If an element is defined as having an atomic data type that is non-numeric then its value is serialized into the JSON member as a string.

- If an element is defined as xs:boolean (or a type derived from xs:boolean) then it is serialized in the JSON member as a boolean.

- If an element is defined as having an xs:list type in the corresponding XSD then it is serialized in the JSON member as an array.

- If an element instance has a null value then it is serialized into the JSON member as a null, regardless of the data type that it has in the corresponding XSD.

- If an element is defined as having maxOccurs > 1 in the corresponding XSD then its parent JSON member is serialized as an array.

- If an element has an XSD data type that is a simple type with XML attributes, then it is serialized in the JSON member as an object. The XML attributes appear as members of that object (using their short names) and the value of the element is serialized as a member of that object with the special name “val”.

- The members (at each level) may be serialized in any order. The order in which they appear in the corresponding XSD file is immaterial.

The Content parameter is treated just like any other parameter of complex type. It is serialized as an object and its members are the attributes and/or child resource references of the Resource that is being transferred. The Content parameter is not required to contain all the attributes of the Resource.

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?