| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 19.0 |
| Source:* | KT Corp. (TTA) |
| Date:* | 2015-09-10 |
| Contact:* | Francisco Sang-Eon Kim, KT, kim.sangeon@kt.com Seongyoon Kim (seongyoon.kim@lge.com) |
| Reason for Change/s:* | Request primitive is not consistent with TS-0001 and TS-0004. |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / WI-0038 STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0010-V1.2.0 |
| Clauses/Sub Clauses* | 6.5.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

TS-0001 is specified to mandatory parameters for Request message at clause 8.1.2.

TS-0004 is also specified mandatory for Request primitive parameters 7.1.1.1

A proposed figure takes into account sequence of parameter and option.

An example is introduced based on PRO-2015-0913 and Table 8.2.2-1 which is about short name of primitive parameters in TS-0004.

Note1: I realize that ri (request identifier) is widely used. It is not consistent with XSD file and Table 8.2.2-1 in TS-0004 that specifies rqi.

Note2: m2m:scheduleEntry has 6 in TS-0004 fields at the time. This is not consistent with TS-0001.

### -----------------------Start of change 1-------------------------------------------

### 6.5.1	Request primitives

A oneM2M request primitive is made up of a number of control parameters and (optionally) a content part. All the parameters in these parts are serialized into the payload of an MQTT Publish Packet, using the rules given in clause 8 of [3] using m2m:requestPrimitive defined in clause 6.4.1 [3].

All the parameters that are present in the primitive shall be serialized, in particular the request shall contain the mandatory parameters such as Operation, To, From, Request Identifier parameters as specified in clause 8.1.2 of [2] and 7.1.1.1 of [3]..

Figure 6.5.1-1: MQTT Request example

An example of a MQTT Request message serialized using JSON is:

{“op”: 1, “to”: “//xxxxx/2345”, “fr”: “//xxxxx/99”, “rqi”: “A1234”, “ty”: 18, “nm”: schedule1, “pc”: {“m2m:sch”:{“se”: “* 0-5 2,6,10 * * * *”}}, “ot”: 20150910T062032}

- op: short name of Operation parameter specified as m2m:operation in [3].

- to: short name of To parameter specified either xs:anyURI [3] or m2m:nhURI [3]. It is an URI of the target resource.

- fr: short name of From parameter which is an ID of the Originator e.g. either the AE or CSE

- rqi: short name of Request Identifier specified as m2m:requestID [3].

- ty: short name of Resource Type parameter specified as m2m:resourceType [3]

- nm: short name of Name parameter specified as xs:NCName [3]. It is a name of the resource to be created

- pc: short name of Content parameter specified in [3].

- ot: short name of Originating Timestamp parameter specified as m2m:timestamp [3].

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?