| CHANGE REQUEST |
| --- |
| Meeting:* | ARC 19.0 |
| Source:* | InterDigital |
| Date:* | 2015-08-28 |
| Contact:* | Catalina Mladin, InterDigital, Catalina.Mladin@InterDigital.com |
| Reason for Change/s:* | Correcting error introduced with notation change of lists |
| CR against: Release* | Release-2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2.1.0 |
| Clauses/Sub Clauses* | 7.3.16 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

When changing notations for lists of sub-resources, an error has been introduced and the <execInstances> list has been changed to <execInstance> resource with no multiplicity.

In TS-0001 V. 0.3.2 contained <execInstances> as a child of mgmtCmd, with the following description (see text in green)

### 9.6.13	Resource Type execInstances

The <execInstances> resource contains all execution instances of the same management command <mgmtCmd>. Each <execInstance> is a sub-resource of <execInstances>. When <mgmtCmd> is successfully triggered by an M2M network application using UPDATE method, a corresponding <execInstance> sub-resource shall be generated.

Figure 9.6.13-1: Structure of <execInstances> resource 
(only resource specific attributes are shown)

The clean up in the following version (V0.4.2) removed lists of resources such as <execInstances>, but the multiplicity was carried incorrectly in this instance, with only on <execInstance> child being specified for the <mgmtCmd> resources.

This error was carried into TS-004, although both TS-0001 and TS-0004 clearly indicate the multiplicity in functional descriptions.

“For multiple requests of the same management command, <mgmtCmd> may use the child-resource (i.e. <execInstance>) to contain all execution instances.” (TS-0001 V0.4.2)

“The Receiver shall automatically create an <execInstance> based on the <mgmtCmd> resource. If the execTarget attribute addresses a <group> resource, the Receiver shall create multiple <execInstance> sub-resources based on the value of currentNrOfMembers attribute.” (TS-0004 V.1.3.0)

The corresponding Rel-1 CDT-mgmtCmd-v1_2_0.xsd also indicates correctly (text in green):

<!-- Child Resources -->

<xs:choice minOccurs="1" maxOccurs="1">

<xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" />

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:execInstance" />

<xs:element ref="m2m:subscription" />

</xs:choice>

</xs:choice>

This CR restores the correct multiplicity for <execInstance> child of <mgmtCmd>.

### -----------------------Start of change 1-------------------------------------------

### Resource Type <mgmtCmd>

#### Introduction

The <mgmtCmd> resource shall contain the following attributes and child resource as illustrated in Table 7.3.16.1-2, Table 7.3.16.1-3, and Table 7.3.16.1-4. The data type and default value of these attributes and child resources are included in the tables.

Table 7.3.16.1-1: Data type definition of <mgmtCmd> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| mgmtCmd | CDT-mgmtCmd-v1_0_0.xsd |  |

Table 7.3.16.1-2: Universal/Common Attributes of <mgmtCmd> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | NP |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| labels | O | O |

Table 7.3.16.1-3: Resource Specific Attributes of <mgmtCmd> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| description | O | O | xs:string | size: 256 No default |
| cmdType | M | O | m2m:cmdType | RESET, REBOOT, UPLOAD, DOWNLOAD, SOFTWAREINSTALL, SOFTWAREUPDATE, SOFTWAREUNINSTALL No default |
| execReqArgs | O | O | m2m:execReqArgsListType | A list of entries which are dependent on cmdType: If cmdType=RESET, execReqArgsList=resetArgsType. If cmdType=REBOOT, execReqArgsList=rebootArgsType. If cmdType=UPLOAD, execReqArgsList=uploadArgsType. If cmdType=DOWNLOAD, execReqArgsList=downloadArgsType. If cmdType=SOFTWAREINSTALL, execReqArgsList=softwareInstallArgsType. If cmdType=SOFTWAREUPDATE, execReqArgsList=softwareUpdateArgsType. If cmdType= SOFTWAREUNINSTALL, execReqArgsList=softwareUninstallArgsType. No default |
| execEnable | O | O | xs:boolean | No default |
| execTarget | M | O | m2m:nodeID | No default |
| execMode | M | O | m2m:execModeType | IMMEDIATEONCE, IMMEDIATEREPEAT, RANDOMONCE, RANDOMREPEAT Default=IMMEDIATEONCE |
| execFrequency | O | O | xs:duration | No default |
| execDelay | O | O | xs:duration | Default=0 |
| execNumber | O | O | xs:nonNegativeInteger | Default=1 |

Table 7.3.16.1-4: Child resources of <mgmtCmd> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | clause 7.3.8 |
| <execInstance> | [variable] | 0..n | clause 7.3.17 |

The <mgmtCmd> shall be executed for the following modes:

- If execMode is IMMEDIATEONCE, <mgmtCmd> shall be executed immediately and only once. In this mode, execFrequency, execDelay, and execNumber shall not be used.

- If execMode is IMMEDIATEREPEAT, <mgmtCmd> shall be executed immediately and repeated multiple times as determined by execNumber and the time interval between each execution is specified by execFrequency. In this mode, execDelay shall not be used.

- If execMode is RANDOMONCE, <mgmtCmd> shall be executed only once at a delayed time which is specified by execDelay. In this mode, execFrequency and execNumber shall not be used.

- If execMode is RANDOMREPEAT, <mgmtCmd> shall be executed multiple times as specified by execNumber but the first execution shall be executed at a delayed time. execDelay specifies the delayed time. The time interval between each execution is specified by execFrequency.

### -----------------------End of change 1 ---------------------------------------------