| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#19 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2015-09-09 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Reason for Change/s:* | Corrections on HTTP Request-Target representations |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0009v1.2.0 |
| Clauses/Sub Clauses* | 6.2.2.1, 6.4.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes a correction to the mapping between To request primitive parameter and the HTTP Request-Target parameter, and a clarification on the HTTP Host header. The detailed justification for the proposed changes is given in the attached slide deck.

### -----------------------Start of change 1-------------------------------------------

#### 6.2.2.1  Path component

The path component of the origin-form HTTP Request-Target shall be interpreted as the mapping of the resource identifier part of the To request primitive parameter. If the HTTP message is sent directly to the next hop CSE, the origin-form of Request-Target shall be employed (see clause 5.3.1 of [1]).

The resource identifier part of the To parameter can be represented in three different formats (see clause 6.2.3 [3] and clause 7.2 [7]):

- CSE-Relative-Resource-ID,

- SP-Relative-Resource-ID,

- Absolute-Resource-ID.

Each of the above three formats may include either a structured Resource ID (used for hierarchical addressing) or an unstructured Resource ID (used for non-hierarchical addressing) as defined in clause 7.2 [7].

For CSE-relative Resource ID representation, the path component of the HTTP request message shall be constructed as the concatenation of the literal “/” and the To request primitive parameter. For SP-relative Resource ID representation, the path component of the HTTP request message shall be constructed as the concatenation of the literal “/~” and the To request primitive parameter. For Absolute Resource ID representation, the path component of the HTTP request message shall be constructed by replacing the first “/” character of the To request primitive parameter with “/_”.

The Table below shows valid mappings between the To request primitive parameter and the path component of the origin-form HTTP request target. In the shown examples, /myCSEID and /CSE178 represent applicable CSI-IDs, CSEBase represents the resource name of a <CSEBase> resource, CSEBase/ae12/cont27/contInst696 represents a structured CSE-relative resource ID, and cin00856 an unstructured CSE-relative resource ID.

Table 6.2.2.1-1: Mapping examples between To parameter and path component of request-line

| Resource-ID Type | To parameter value | path component (origin-form) |
| --- | --- | --- |
| structured CSE-Relative | CSEBase/ae12/cont27/contInst696 | /CSEBase/ae12/cont27/contInst696/ |
| unstructured CSE-Relative | cin00856 | /cin00856 |
| structured SP-Relative | /CSE178/CSEBase/ae12/cont27/contInst696 | /~/CSE178/CSEBase/ae12/cont27/contInst696 |
| unstructured SP-Relative | /CSE178/cin00856 | /~/CSE178/cin00856 |
| structured Absolute | //mym2msp.org/CSE178/CSEBase/ ae12/cont27/contInst696 | /_/mym2msp.org/CSE178/CSEBase/ ae12/cont27/contInst696 |
| unstructured Absolute | //mym2msp.org/CSE178/cin00856 | /_/mym2msp.org/CSE178/cin00856 |

At the HTTP server side, the reverse operations shall be applied to the path component of request-line to derive a replica of the original To request primitive parameter.

If the HTTP message is sent to a HTTP proxy instead directly to the next hop CSE, the absolute-form of Request-Target shall be employed (see clause 5.3.2 of [1]). The absolute-form is derived by prefixing the origin-form with the schema and the host address of the next hop CSE:

http://{host address of next hop CSE}{origin-form path-component}

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 6.4.1	Host

The Host header shall be present in each HTTP request message.

While the Request-Target indicates a target resource on the Hosting CSE, the Host header indicates the FQDN or IP address of the Receiver CSE of the next hop in multi-hop communication scenarios. Therefore, the Request-Target is not changed but the Host header is changed each time when a request is forwarded to the next hop CSE.

When no HTTP proxy is used, the Host header shall be set as one of the pointOfAccess attribute values of the Receiver (i.e. pointOfAccess attribute of the corresponding <remoteCSE> resource). Selection of the appropriate Receiver is described in oneM2M TS-0004 [3]. In this case the origin-form of target URI shall be used (see clause 6.2.2).

If the HTTP request message is sent to a HTTP proxy rather than to the next hop CSE, the Host header shall be set to the FQDN or IP address of the proxy.  In this case the absolute-form of target URI shall be used (see clause 6.2.2).

### -----------------------End of change 2-------------------------------------------