| CHANGE REQUEST |
| --- |
| Meeting:* | TP#19 |
| Source:* | InterDigital |
| Date:* | 2015-08-28 |
| Contact:* | Dale.Seed@InterDigital.com |
| Reason for Change/s:* | Enhancements to ‘attribute’ criterion of the eventNotificationCriteria attribute to support sending notifications when the value of a particular attribute under the subscribed resource changes. This can also be viewed as partial subscription feature. |
| CR against: Release* | Rel-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v1.4.0 |
| Clauses/Sub Clauses* | See description |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

As per the current specification TS 0001 v2.2.0 and TS 004 v1.2.0, the attribute criterion of the eventNotificationCriteria is a name and value pair where the subscriber specifies that a notification needs to be triggered if the particular attribute has the specified value. Also the attribute criterion can be a list so that multiple attributes and their values could also be specified as a filtering criteria. But if a subscriber wants to receive notifications if only a particular attribute’s value gets changed, then there is no support with the current attribute criterion. i.e, if a subscriber is interested in the changes of only a single attribute (or a set of attributes) and no other of the particular resource, there should be means of specifying a criteria where the notification needs to be triggered if and only if those attribute(s) gets modified.

As an example, a subscriber subscribes under <container> resource and wants to monitor any change in the maxNrOfInstances attribute, then currently the subscriber has to subscribe for the full <container> resource and upon receiving notifications, himself identify whether the particular attribute changed or not.

The proposal here is that the attribute criterion could be enhanced to take an empty value. Currently both the name and value sub-attributes of the attribute criterion are mandatory and by making value as optional, it can be indicated to the CSE that the subscriber is interested just in the change of the attribute alone. Further the notification content can have only the attribute value since the subscriber is not interested in other attributes of the resource.

The changes are spread across TS0004 and the XSD files and specific changes is documented below.

### -----------------------Start of change 1 in TS 0004--------------------------------------

#### m2m:attribute

Used in m2m:eventNotificationCriteria and m2m:filterCriteria.

Table 6.3.4.8-1: Type Definition of m2m:attribute

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| name | xs:NCName | 1 |  |
| value | xs:anyType | 0..1 | To subscribe to an individual attribute of a resource and receive notifications for operations performed on this attribute, an eventNotificationCriteria can be configured having only a name and no value. |

### -----------------------End of change 1 in TS 0004 -----------------------------------------

### -----------------------Start of change 2 in XSD v2_0_0 --------------------------------

The CDT-commmonTypes-v2_0_0.xsd needs the below enhancement for the definition of the ‘attribute’ attribute.

<xs:complexType name="attribute">

<xs:sequence>

<xs:element name="name" type="xs:NCName" />

<xs:element name="value" type="xs:anyType" minOccurs=”0” />

</xs:sequence>

</xs:complexType>

### -----------------------End of change 2 in XSD v2_0_0 --------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?