| CHANGE REQUEST |
| --- |
| Meeting:* | TP#19 |
| Source:* | InterDigital |
| Date:* | 2015-08-28 |
| Contact:* | Dale.Seed@InterDigital.com |
| Reason for Change/s:* | MemberType attribute RequestOptionaity should be changed to Optional from Mandatory during Create and NotPresent in update as it has a default value of MIXED and is a WO attribute. |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V2.1.0 |
| Clauses/Sub Clauses* | Table 7.3.13.1-3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: PRO-2015-0930-CR-Group_MemberTypeReqOptionality_R1 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This STE CR proposes to correct request optionality of memberType attribute for Group resource.

memberType attribute is a WriteOnce attribute based on its description available in clause 9.6.13 of TS0001 v1.10.0 and has a default value of “mixed”. So, correcting its request optionality to Optional during Create and NotPresent during update.

A corresponding change to the XSD is also proposed.

## ----------------------- Start of change 1 -----------------------

Table 7.3.13.1-3: Resource Specific Attributes of <group> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| Creator | NP | NP | m2m:ID |  |
| memberType | O | NP | m2m:memberType | Default value is set to ‘MIXED’ |
| currentNrOfMembers | NP | NP | xs:nonNegativeInteger | No default (This is generated by the hosting CSE and limited by the maxNrOfMembers attribute of the <group> resource) |
| maxNrOfMembers | M | O | xs:nonNegativeInteger | No default |
| memberIDs | M | O | list of xs:anyURI | No default |
| membersAccessControlPolicyIDs | O | O | list of xs:anyURI | No default |
| memberTypeValidated | NP | NP | xs:Boolean | No default (This is generated by the hosting CSE) |
| consistencyStrategy | O | NP | m2m:consistencyStrategy | Default value is set to ‘ABANDON_MEMBER’ |
| groupName | O | O | xs:string | No default |

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

<xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.onem2m.org/xml/protocols"

27 	xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

28 	elementFormDefault="unqualified" xmlns:xs="http://www.w3.org/2001/XMLSchema">

29

30 	<xs:include schemaLocation="CDT-commonTypes-v1_3_0.xsd" />

31 	<xs:include schemaLocation="CDT-subscription-v1_3_0.xsd" />

32

33 	<xs:element name="group">

34 		<xs:complexType>

35 			<xs:complexContent>

36 				<!-- Inherit common attributes for announceable Resources -->

37 				<xs:extension base="m2m:announceableResource">

38 					<!-- Resource Specific Attributes -->

39 					<xs:sequence>

40                         <xs:element name="creator" type="m2m:ID" minOccurs="0" />

41 						<xs:element name="memberType" type="m2m:memberType" minOccurs=”0” />

42 						<xs:element name="currentNrOfMembers" type="xs:nonNegativeInteger" />

43 						<xs:element name="maxNrOfMembers" type="xs:nonNegativeInteger" />

44 						<xs:element name="memberIDs" type="m2m:listOfURIs" />

45 						<xs:element name="membersAccessControlPolicyIDs" type="m2m:listOfURIs" minOccurs="0" />

46 						<xs:element name="memberTypeValidated" type="xs:boolean" />

47 						<xs:element name="consistencyStrategy" type="m2m:consistencyStrategy" minOccurs="0" />

48 						<xs:element name="groupName" type="xs:string" minOccurs="0" />

49

50 						<!-- Child Resources -->

51 						<xs:element name="fanOutPoint" type="xs:anyURI" />

52

53 						<xs:choice minOccurs="0" maxOccurs="1">

54 							<xs:element name="childResource" type="m2m:childResourceRef" maxOccurs="unbounded" />

55 							<xs:element ref="m2m:subscription" maxOccurs="unbounded" />

56 						</xs:choice>

57 					</xs:sequence>

58 				</xs:extension>

59 			</xs:complexContent>

60 		</xs:complexType>

61 	</xs:element>

62

## ----------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?