| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#19 |
| Source:* | Qualcomm Inc. |
| Date:* | 2015-09-01 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Reason for Change/s:* | Remaining issues with formats of the Content primitive parameter |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004v1.3 |
| Clauses/Sub Clauses* | 6.2.3, 6.3.4.24, 7.1.1, 7.4.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

At TP#18, CR 2015-0844R03 was agreed, which was intended to clarify the permitted representation of the Content primitive parameter and their use cases. However, a number of issues still remained open. These are addressed in this contribution:

Use of the m2m:attributesList root element in retrieve request primitives:  in the discussions of  CR 2015-0844R03 the question was raised if this form of representation could not simply be replaced by m2m:<resourceType>, i.e. the same format as used for the primitive parameter of Create request.

We think it is possible to apply m2m:<resourceType> for this use case when imposing the same restriction regarding XSD validation is already stated in the text for both Create request and partial retrieve operations:  “Since a partial resource is being transferred with a Create request primitive, it is not required to be valid according to the XSD for that resource in terms of the presence of resource attributes. Any attribute that is present, however, shall comply to the data type defined in the XSD of that resource.

If it is agreed to replace m2m:attributeList by m2m:<resourceType>  the next revision of this CR will need to include changes to some other sections not currently covered (complete removal of attributeList where it occurs).

Usage of  “raw data” in the Content parameter of response primitives:   CR 2015-0844R03 has clarified that this representation  is used either

  - to indicate the URI of a <request> resource  in the response (“acknowledgement”) to non-blocking requests in asynchronous mode for any CRUD operation

  - to indicate the URI in response to Create requests for Result Content  “Hierarchical Address”

Since in both cases, a single URI is included, it is proposed to define another permitted root element m2m:URI for this purpose and replace the “raw data” option with it.

Applicability of CSE-relative, SP-relative and Absolute Resource ID scope:  it is currently not clearly specified which of these URI representation applies. Some text is proposed here for clause 6.2.3 to fix this issue.

Use of root element m2m:resource with data type m2m:resourceWrapper. This is applicable only to responses to Create requests with rcn = 3 (hierarchical address and attributes).  The data type definition of m2m:resourceWrapper adds a @URI attribute to the base data type m2m:resource (note that this is a data type which only incidentally has the same name as the root element mentioned above).  This data type m2m:resource however has been defined as one of the base resource data types employed to build the inheritance model as described in clause 6.5.1. It is obviously incorrect to use this data type as basis for the resourceWrapper data type. Supposedly, here the intention was to add the @URI attribute to any of the potential <resourceType> root elements.

Options to resolve this:

  - Add @URI as an optional attribute to all XSD definitions to all applicable <resourceType> root elements.

  - Redefine root element m2m:resource as sequence of  a <resourceType> element and a URI-element as follows:

<xs:complexType  type="resourceWrapper">
			<xs:sequence>
				<xs:choice minOccurs="1" >

<xs:element ref="m2m:AE" />

<xs:element ref="m2m:accessControlPolicy" />
				      <xs:element ref="m2m:container" />

(all applicable resource types to be added)

<xs:element ref="m2m:subscription" />
   			        </xs:choice>
				 <xs:element name="URI" type="xs:anyURI" />		
			</xs:sequence>	
	    </xs:complexType>

The above suggested definition of m2m:resourceWrapper  would be suitable also for the rcn = 5 (“attributes and child resource references”) use cases. The current definition of using m2m:<resourceType> results in somewhat more verbose representation of the child resource references, based on the m2m:childResourceref data type. When using an XML representation with short names this leads to a representation like        <m2m:ch nm={resourceName}   typ={resourceType}>{address of child resource}</m2m:ch> .

“Address of child resource”, however,  presently is not mandated to represent a hierarchical resource address. The value of the m2m:childResourceref data type may also employ the non-hierarchical address format. When using hierarchical resource addresses, the nm = {resourceName} would become actually redundant information since it is already included in the last segment of the hierarchical resource address as can be seen from the following example:

<m2m:ch nm=ContentInstance1 typ=4> /CSE-ID1/CSEBase22/AE1//Container2/ContentInstance1</m2m:ch>

It should be discussed whether this format is acceptable or if the formats used for rcn=5 and rcn =6 should be aligned with each other. The alignment can be achieved by using the m2m:resource datatype and changing the m2m:resourceWrapper datatype as suggested above by replacing the  URI element just needs to be replaced by a URIList element.

<xs:element name="URIList" type="m2m:listOfURIs" />

This would also make the format more consistent with the other rcn formats which include hierarchical resource addresses.

Case rcn = 7 applies to Retrieve operation only (R/7). It retrieves the original resource in case the To parameter points to an announced resource. This is clarified in a new note. The case C/7 is removed (this is covered by C/1)

It is currently not clearly defined what happens when an operation/rcn combination is selected which is not defined by Table 7.4.2-2. A statement is added that in this case an error response with Response Status Code “BAD_REQUEST” shall be returned.

……………………………………………………………………………………………………………………………

This contribution intends to clarify the formats the Content primitive parameter is permitted to take. This is currently defined in clauses 7.1.1 and 7.4.2. However, there is to some extent a mismatch between these two clauses.

This contribution aims to align these two clauses, and also to supply uses case as well as more detailed information on conditions with respect to primitive parameters which have impact on selection of the appropriate format of the Content primitive parameter.

- The relation between the format of Content parameter and media types defined in clause 6.7 is not completely clear. Which media type(s) shall be used when it includes an element m2m:<resourceType> or raw data?

### -----------------------Start of change 1-------------------------------------------

### oneM2M Resource Addressing

Authorized oneM2M entities can operate on an oneM2M Resource by specifying the Resource Identifier as the target address.

- Structured Resource ID (used in Hierarchical Addressing): the ID is constructed as a relative path from the CSEBase resource via parent resources.

- Unstructured Resource ID (used in Non-hierarchical Addressing): the ID uniquely identifies the resource in the domain of its Hosting CSE.

Furthermore each of these forms can be expressed either

- Relative to the Hosting CSE, or

- Relative to the M2M Service Provider, or

- In absolute form

A single attribute of the targeted oneM2M resource shall be addressable adding the sub-address (targeted-attribute-name) following a "#" character after the resource address.

The address appearing in 'ChildResourceRef' may be used as in M2M-SP relative form, if it is obvious which M2M-SP or CSE-ID should be added.

The syntax of the oneM2M Resource Identifier (resource-ID) in ABNF notion [20] is as follows:

resource-identifier = (hierarchical-resource-address / non-hierarchical-resource-address) [ "#" targeted-attribute-name ]

hierarchical-resource-address = [ CSE-ID] 1*("/" resource-name)

non-hierarchical-resource-address = [ CSE-ID] "/" unstructured-ID

unstructured-ID = 1*unreserved

resource-name = 1*unreserved

When including hierarchical resource IDs into the Content parameter of response primitives (cf. clause 7.4.2), the resource hosting CSE shall select the appropriate format of the ID depending on the location of the originator. If the originator of the request primitive is registered to the hosting CSE, the CSE-relative format of hierarchical resource ID applies. If the originator of the request primitive is not registered to the hosting CSE but belongs to the same M2M-SP domain, the CSE-relative format applies. If the originator of the request primitive belongs to a different M2M-SP domain, the Absolute format of hierarchical resource ID applies.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### oneM2M simple data types

Table 6.3.2-1 describes oneM2M-specific simple data type definitions. XML Schema data type definitions for these data types can be found in the XSD file called CDT-commonTypes-v1_0_0.xsd.

The types in table 6.3.2-1 are either:

- Atomic data types derived from XML Schema data types by restrictions other than enumeration

- List data types constructed from other XML Schema or oneM2M-defined atomic data types.

The oneM2M-defined enumeration data types are defined in clause 6.3.3.

Table 6.3.2-1: oneM2M Simple Data Types

| XSD type name | Type Name | Examples | Description |
| --- | --- | --- | --- |
| m2m:ID | Generic ID | //globalm2m.org | Used to represent generic IDs generated and used within oneM2M (M2M-SP-ID) |
|  |  | //globalm2m.org/C190XX7T | (CSE-ID) |
|  |  | //globalm2m.org/CSE1/123A38ZZY | (AE-ID) |
| m2m:nodeID | Node ID | urn:gsma:imei:90420156-025763-0;svn=42 | Used for Node IDs. The constraints on this type are different from those on Generic IDs (IMEI as node ID) |
| m2m:deviceID | Device ID | urn:dev:ops:012345-Set%2DTop%2DBox-0123456789 | A Device ID identifies a device using a Universally Unique IDentifier (UUID). A valid hex digit character string of UUID and the format of the URN is one of OPS URN, OS URN, IMEI URN, ESN URN, or MEID URN. |
| m2m:externalID | M2M-EXT-ID | urn:gsma:imei:90420156-025763-0;vers=0 | The External Identifier allows the Underlying Network to identify the M2M Device (e.g. ASN, MN) associated with the CSE-ID.In 3GPP case, the accessID is mapped to External Identifier as specified in TS 23.003 [17]. |
| m2m:requestID | Request ID | ab3f124a, CSE1/98821 | Used for Request IDs. This type may include the ID of the target CSE as well as a part that varies for each ID |
| m2m:nhURI | Non Hierarchical Identifier | /CSE090112/ C190XX7T | Used where a resourceID is required to be non-hierarchical |
| m2m:acpType | List of ACP Resource IDs | //IN-CSEID.m2m.myoperator.org/93405 | Used to represent a list of AccessControlPolicy identifiers. |
| m2m:labels | list of xs:token | printers networkwifi1 home_energy | A list of tokens used as keys for discovering resources (searching wifi connected printer from vendor 1) |
| m2m:triggerRecipientID | Trigger Recipient Identifier | 3010 | Used when device triggering services are requested from the Underlying Network, to identify an instance of an ASN/MN-CSE on an execution environment, to which the trigger is routed. Defined as port number in the range 0 to 65535. |
| m2m:listOfM2MID | List of M2M identifiers |  | xs:list of elements of data type m2m:ID |
| m2m:listOfMinMax | List of Time Limits | 10 2560 | xs:list of two xs:long values defining min and max limits of time intervals in units of milliseconds (value -1 representing infinite time) |
| m2m:backOffParameters | List of Backoff Parameters | 100 100 2000 | Ordered sequence of 3 values of data type xs:nonNegativeInteger representing backoffTime, backoffTimeIncrement, maximumBackoffTime (in units of milliseconds) |
| m2m:ipv4 | IPv4 address string with optional CIDR suffix | 10.125.0.0/16,122.77.12.1 | Used in m2m:accessControlRules specified in the section 6.3.4.26 |
| m2m:ipv6 | IPv6 address string with optional CIDR suffix | ::/0, Fadf:ddd0::/32, abcd:ffff:abb0:aaaa::/64 | Used in m2m:accessControlRules specified in the section 6.3.4.26 |
| m2m:countryCode | Country Code | KR | 2-character country code as defined by ISO-3166 |
| m2m:poaList | List of PointOfAccess strings | http://172.25.0.10:8080, coap://m2m.sp.com | list of xs:string. Each pointOfAccess entry in list is represented as a string containing the underlying transport protocol as well as the IP address and port (or an FQDN). |
| m2m:timestamp | Time stamp string | 20141003T112032 | DateTime string of ‘Basic Format’ specified in ISO8601 [27]. Time zone shall be interpreted as UTC timezone. |
| m2m:absRelTimestamp | absolute or relative time stamp string | 20141003T112032 (absolute time),or 3600000 (relative time) | defined as xs:union of m2m:timestamp and xs:duration data types |
| m2m:typeOfContent | Type of Content | application/xml | The media type shall be an IANA registered Media Types name, or an experimental Media Type (See [26]) ‘:’ |
| m2m:contentInfo | Content Information | application/xml:2 | A string consisting of a media type optionally followed by a m2m:encoding separated by ‘:’ character. See Note-1. |
| m2m:eventCat | Event Category | 2 | Either One of the values from m2m:stdEventCats or A user-defined category in the range 100-999 |
| m2m:eventCatWithDef | Event Category with default | 0 | Either A value from m2m:eventCat , or The value 0 which has the special meaning “default” |
| m2m:listOfEventCat | List of (applicable) Event Categories | 1 101 | xs:list of elements of data type m2m:eventCat |
| m2m:listOfEventCatWithDef | List of m2m:eventCatWithDef | 0 1 101 |  |
| m2m:scheduleEntry | Schedule Entry | * 0-5 2,6,10 * * * * | The string is used to describe a duration of enablement. The string format is described in clause 7.3.9.1 |
| m2m:attributeList | List of xs:NCName | poa rr | Used for the Content parameter of Retrieve request primitives |
| Note-1: the encoding in m2m:contentInfo may be omitted when the value was ''0 (plain)". But since default value of encoding is not allowed in future releases, it is recommended not to omit the encoding. |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### (void)

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

## oneM2M specific MIME media types

The present sub-clause defines oneM2M specific MIME media types which may be used by protocol bindings.

The oneM2M specific MIME media types are defined under the vendor tree of "application" mediate type which is prefixed with ‘application/vnd.onem2m-‘.

Table 6.7-1: oneM2M specific MIME media types

| oneM2M specific MIME subtype | mapped oneM2M data type | Note |
| --- | --- | --- |
| vnd.onem2m-res+xml | m2m:resource | For oneM2M resource operation.The type of oneM2M resource in content shall be indicated by "ty" parameter. XML serialization rule is applied. (See clause 7.4.2) |
| vnd.onem2m-res+json | m2m:resource | Same information of above. JSON serialization rule is applied. (See clause 7.4.2) |
| vnd.onem2m-ntfy+xml | m2m:notification or m2m:aggregatedNotification | For Notify operation for resource subscription. XML serialization rule is applied. (See clause 7.4.1) |
| vnd.onem2m-ntfy+json | m2m: notification or m2m:aggregatedNotification | Same information of above. JSON serialization rule is applied. (See clause 7.4.1) |
| vnd.onem2m-preq+xml | m2m:requestPrimitive | For exchanging serialized oneM2M request primitive. XML serialization rule is applied. (See clause 6.4.1 and 7.1.1.1) |
| vnd.onem2m-preq+json | m2m:requestPrimitive | Same information of above. JSON serialization rule is applied. (See clause 6.4.1 and 7.1.1.1) |
| vnd.onem2m-prsp+xml | m2m:responsePrimitive | For exchanging Response parameters. XML serialization rules is applied. (See clause 6.4.2 and 7.1.1.2) |
| vnd.onem2m-prsp+json | m2m:responsePrimitive | Same information of above. JSON serialization rule is applied. (See clause 6.4.2 and 7.1.1.2) |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

#### m2m:resourceWrapper

This data type is used for the m2m:resource root element of the Content parameter of response primitives as defined in clause 7.4.2

Table 6.3.4.24-1: Type Definition of m2m:resourceWrapper

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| m2m:<resourceType> | (anonymous) | 1 | A representation of a Resource with specific type as described in clause 7.3 |
| URI | xs:anyURI | 1 | Hierarchical URI of the resource |

### -----------------------End of change 5-------------------------------------------

### -----------------------Start of change 6-------------------------------------------

## Primitive format and generic procedure

### Primitive format

#### Request primitive format

Table 7.1.1.1-1 summarizes the primitive parameters of the Request primitive, indicating their presence depending on the C, R, U, D or N operations. "M" indicates mandatory, "O" indicates optional, "NP" indicates not present.

Refer to clause 8.1.2 of the oneM2M TS-0001 [6] for additional information on the request primitive parameters.

Table 7.1.1.1-1: Request Primitive Parameters

| Primitive Parameter | CREATE | RETRIEVE | UPDATE | DELETE | NOTIFY |
| --- | --- | --- | --- | --- | --- |
| Operation | M | M | M | M | M |
| To | M | M | M | M | M |
| From | M | M | M | M | M |
| Request Identifier | M | M | M | M | M |
| Resource Type | M | NP | NP | NP | NP |
| Name | O | NP | NP | NP | NP |
| Content | M | O | M | NP | M |
| Role | O | O | O | O | O |
| Originating Timestamp | O | O | O | O | O |
| Request Expiration Timestamp | O | O | O | O | O |
| Result Expiration Time | O | O | O | O | O |
| Operation Execution Time | O | O | O | O | O |
| Response Type | O | O | O | O | O |
| Result Persistence | O | O | O | O | NP |
| Result Content | O | O | O | O | NP |
| Event Category | O | O | O | O | O |
| Delivery Aggregation | O | O | O | O | O |
| Group Request Identifier | O | O | O | O | O |
| Filter Criteria | NP | O | O | O | NP |
| Discovery Result Type | NP | O | NP | NP | NP |

The Content parameter in a Request shall contain one of the following:

- A partial Resource. This applies to Create and Updaterequest primitives. In the case of a Create request the Content parameter shall contain a single root element whose name is the name of the Resource and whose content consists of one or more attributes, child Resources or childResource references. In the case of an Update request primitive, the Content parameter shall contain the attributes and their new values. Attributes to be deleted from the resource shall be indicated without a value. In both cases, the resource type is as defined in clause 7.3, however since a partial resource is being it is not required to be valid according to the XSD for that resource.  If an attribute is present with a value, however, that value shall comply to the data type defined in the XSD of that resource.

- A Notification Data Object. This applies to Notification request primitives. The data type of the data object is named <m2m:notification> and is described in Clause 7.4.1

- An Aggregated Notification. This applies to Notification request primitives. The data type of the data object is named <m2m:aggregatedNotification> and contains multiple <m2m:notification> objects. This is described in clause 7.4.1.

- An AttributeList element, as described in clause 7.4.2. This is used in partial retrieve request primitives to indicate a list of attribute names whose values shall be retrieved in the response. l. In the case of an Retrieve request primitive, the Content parameter shall contain the attributes to be retrieved without any values.

- A ResponsePrimitive object as described in clause 7.4.1. This applies to Notification request primitives which are sent when accessing resources in asynchronous non-blocking mode.

#### Response primitive format

Table 7.1.1.2-1 summarizes the primitive parameters for Response primitive, indicating their presence depending on the C, R, U, D or N operations of the associated Request primitive and whether this operation was successful or caused an error. "M" indicates mandatory, "O" indicates optional, "NP" indicates not present.

Refer to clause 8.1.3 of TS-0001 [6] for additional information on the request primitive parameters.

NOTE: Response Code and Status Code parameters are merged into the Response Status Code parameter.

Table 7.1.1.2-1 : Response Primitive Parameters

| Primitive parameter | Ack | CREATE Success | RETRIEVE Success | UPDATE Success | DELETE Success | NOTIFY Success | Error |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Response Status Code | M | M | M | M | M | M | M |
| Request Identifier | M | M | M | M | M | M | M |
| Content | O | O | M | O | O | O | O |
| To | O | O | O | O | O | O | O |
| From | O | O | O | O | O | O | O |
| Originating Timestamp | O | O | O | O | O | O | O |
| Result Expiration Timestamp | O | O | O | O | O | O | O |
| Event Category | O | O | O | O | O | O | O |

The Content parameter in a Response shall contain one of the following:

- A complete or partial Resource. This applies to a response primitive sent in reply to create and retrieve request message. In this case the Content parameter shall contain a single root element whose name is the name of the resource and whose content consists of one or more attributes, child resources or childResource references. In this case the resource type is as defined in clause 7.3. However, if a partial resource is being transferred, it is not required to be valid according to the XSD for that resource, in terms of the presence of resource attributes. Any attribute that is present, however, shall comply to the data type defined in the XSD of that resource.

- The URI of a resource.  These are included in an element called m2m:URI defined in clause 7.4.2.

- A partial resource and its hierarchical URI. These are included in a root element called m2m:resource defined in clause 7.4.2 as a sequence consisting of one  m2m:<resourceType> element and a m2m:URI element.

- A list of URIs. This can  be used for transferring the childResource URIs only or in a Discovery response. These are included in an element called m2m:URIList defined in clause 7.4.2.

- An Aggregated Response. This is sent as a result of a Group operation. This uses the root element m2m:aggregatedResponse defined in clause 7.4.2.

- Raw data may be included in the Content primitive parameter of error response primitives e.g. to indicate debugging information.

### -----------------------End of change 6-------------------------------------------

### -----------------------Start of change 7-------------------------------------------

### Elements contained in the Content primitive parameter

Clauses 7.1.1.1 and 7.1.1.2 enumerate the forms that the Content primitive parameter takes in various Request and Response cases. Note that the Content primitive parameter is denoted as primitiveContent in both, CDT-requestPrimitive-v1_2_0.xsd and CDT-responsePrimitive-v1_2_0.xsd.

This clause details the Objects (elements) used in some of these cases in the tables below.

The following elements are defined for use in the Content parameter of a request:

Table 7.4.2-1: Elements used for request content

| Element Name | Applicable Operations | Data Type | Defined in |
| --- | --- | --- | --- |
| m2m:<resourceType> | C R U | m2m:<resourceType> | CDT-<resourceType>-v1_0_0.xsd |
| m2m:notification | N | m2m:notification | CDT-notification-v1_0_0.xsd |
| m2m:aggregatedNotification | N | m2m:aggregatedNotification | CDT-notification-v1_0_0.xsd |
| m2m:responsePrimitive | N | m2m:responsePrimitive | CDT-responsePrimitive-v1_0_0.xsd |

The following elements are defined for use in the Content parameter of a response sent in reply to a request message with Operation and Result Content (rcn) parameters as given in the column “Applicable Operations” (the settings of the Result Content parameters are defined in clause 6.3.3.2.7; NP means the rcn parameter is not present)::

Table 7.4.2-2: Elements used for response content

| Element Name | Applicable Operations/rcn | Data Type | Element is Defined in |
| --- | --- | --- | --- |
| m2m:<resourceType> | C/1, NP R/1,4,5,6,7,NP U/1,NP D/1,NP Note 1 | m2m:<resourceType> | CDT-<resourceType>-v1_0_0.xsd |
| m2m:resource | C/3 | m2m:resourceWrapper | CDT-responsePrimitive-v1_0_0.xsd |
| m2m:URIList | R/NP Note 2 | m2m:listOfURIs | CDT-responsePrimitive-v1_0_0.xsd |
| m2m:aggregatedResponse | C R U D Note 3 | m2m:aggregatedResponse | CDT-responsePrimitive-v1_0_0.xsd |
| m2m:URI | C/2 Note 4 | xs:anyURI | CDT-responsePrimitive-v1_0_0.xsd |
| Raw data | Note 5 |  |  |
| Note 1: The case rcn = 7 applies to Retrieve operation only (R/7). It retrieves the original resource in case the To parameter points to an announced resource. Note 2: This applies to ordinary retrieve operation when the Result Content parameter is not present and for discovery operation. For discovery, the format of the URIList elements (structured, unstructured) depends on the Discovery Result Type parameter setting (see clause 6.3.3.2.8). Note 3: This applies to CRUD operations on a <fanOut> child resource of a <group> parent resource. The Content parameter of each response primitive included in aggregatedResponse is set as given in one of the other rows of this table. Note 4: This also applies to the response (“acknowledgement”) to non-blocking requests in asynchronous mode for any CRUD operation Note 5: Raw data could e.g. be included as debugging information into error responses |

### Request messages indicating a combination of operation/rcn not listed in Table 7.4.2-2 should cause an error response message with Response Status Code  RSC= 4000 (“BAD_REQUEST”).

### -----------------------End of change 7-------------------------------------------