| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#19 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2015-09-10 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Removing Use of Fragments from HTTP Request-Target |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0009v2.0.0 |
| Clauses/Sub Clauses* | 6.2.2.2, 6.2.2.3 (merged into 6.2.2.2) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: PRO-2015-0964R01<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to remove use of fragments in the HTTP Request-Target parameter for retrieve requests which are mapped to HTTP GET request messages. Some widely used http client implementations apparently do not support fragments (e.g. HTTP clients under Android OS).

This proposal assumes that a (partial) retrieve request primitive, either

- includes a single attribute to be retrieved in the To parameter separated by ‘#’ character from the path identifying the addressed resource, or

- includes a  list of attributes with root element m2m:attributeList in the Content primitive parameter (not including any attribute values.

For the second use case the most appropriate data type would be “xs:list of xs:NCName”, as proposed in PRO-2015-0946R01. However, this proposal would also be feasible if the present data type of m2m:attributeList remains in place.

Essentially the proposal is to just replace the fragment separator ‘#’ of the HTTP request target by the short name of the attributeList element, which is “atrl”, and thus append this to the query string. This approach is feasible because an element attributeList/atrl does not occur in the Filter Conditions parameter. So the presence of the attributeList can be identified unambiguously by the receiver.

Example

Current solution:

/CSEbase1/AE01?rcn=1#lbl+rr+rid

Proposed solution:

/CSEbase1/AE01?rcn=1&atrl=lbl+rr+rid

For Release-2, it is proposed to consider removal of the option of appending the attribute to the To parameter from TS-0001, TS-0004 and TS-0009, and to mandate use of the attributeList in the Content parameter. Removal of this option just simplifies implementation. These CRs could however be prepared and discussed at a future meeting. The changes proposed here should still be mirrored into the Rel-2 version of TS-0009 for now.

### -----------------------Start of change 1-------------------------------------------

#### 6.2.2.2  Query component

The query component (e.g. query-string) may include  the optional primitive parameters listed in Table 6.2.2-1 compliant with RFC 7230 [1]. Each applicable request primitive parameters and elements of Filter Criteria parameter shown in Table 6.2.2-1 shall be represented as pair of field-name and value in query-string. Multiple such pairs shall be concatenated with an ampersand ‘&’ character used as separator between two pairs.

Table 6.2.2-1 also shows the permitted multiplicity of occurrence of field names in the query-string. Multiplicity ‘0..1’ means that a  parameter  is optional and can occur at most once. Parameters with multiplicity ‘0..n’, may occur multiple times in the query-string in the form of  <query field name> = value.  For example, if the resourceType element of the Filter Criteria parameter is represented by a list of 3 values ‘2 3 4’ (see clause 6.3.4.7 in TS-0004 [3]), it would be mapped to ty=2+3+4 in the query-string. At the receiver side, this query string can be reverted back into the list type of representation. The same representation shall be applied for multiple occurrences of contentType and labels elements.

The ‘attribute’ element of the Filter Criteria request primitive parameter consists of two elements, name and value, which in XML notation would look for example as follows in case of multiplicity 2 (see clause 6.2.4.8 in TS-0004 [3]):

<attribute>

<name>attname1</name>

<value>attvalue1</value>

</attribute>

<attribute>

<name>attname2</name>

<value>attvalue2</value>

</attribute>

Each name (e.g. attname1 and attname2) shall represent a valid resource attribute name of the resource types indicated in the ty field of the query-string. The sequence of attribute elements as shown in the above example will be mapped into the query-string as attname1=attvalue1&attname2=attvalue2. The attribute names (i.e. attname1 and attname2 in the above example) shall be expressed in the form of short names as defined in clause 8.2.3 of TS-0004 [3].  Note that the <attribute> tag of the XML representation is omitted in the HTTP binding.

Examples of valid Request-Target representations are the following:

Example 1): Request-Target for ‘nonBlockingRequestSynch’

Primitive parameters: 	To:						/CSE1234/RCSE78/container234        (SP-Relative-Resource-ID)

Response Type:	      responseType = 1     						(nonBlockingRequestSynch)

Result Persistence:	P1Y2M3DT10H1M0S	Request-Target:			/CSE1234/RCSE78/container234?rt=1&rp=P1Y2M3DT10H1M0S

Example 2):  Request-Target for Discovery

When the entity wants to discover container resources where the creator attribute has the value ‘Sam’:

Primitive parameters:	To:						/CSE1234/RCSE78

Filter Criteria:		resourceType = 3           (container)

attribute name:  creator

attribute value: Sam

filterUsage = discovery

Request-Target:			/CSE1234/RCSE78?ty=3&cr=Sam&fu=1

Any of the short names listed in Table 6.2.2-1, with the exception of ‘atr’, may be used in the query-string. The short name ‘atr’ itself is not used. Instead, any of the resource attribute short names as listed in Tables 8.2.3-1 to 8.2.3-5 may be used in the query-string in representations of  attname=attvalue expressions, except those that shall be omitted (see clause 7.2.3.16.9 in [3]).

Table 6.2.2-1: oneM2M request parameters mapped as query-string field

| Request Primitive Parameter | Query Field Name | Multiplicity | Note |
| --- | --- | --- | --- |
| Response Type | rt | 0..1 | responseType element of data type m2m:responseTypeInfo (cf. clause 6.3.4.29 of TS-0004 [3]) |
| Result Persistence | rp | 0..1 |  |
| Result Content | rc | 0..1 |  |
| Delivery Aggregation | da | 0..1 |  |
| createdBefore | crb | 0..1 | filterCriteria condition |
| createdAfter | cra | 0..1 | filterCriteria condition |
| modifiedSince | ms | 0..1 | filterCriteria condition |
| unmodifiedSince | us | 0..1 | filterCriteria condition |
| stateTagSmaller | sts | 0..1 | filterCriteria condition |
| stateTagBigger | stb | 0..1 | filterCriteria condition |
| expireBefore | exb | 0..1 | filterCriteria condition |
| expireAfter | exa | 0..1 | filterCriteria condition |
| Labels | lbl | 0..n | filterCriteria condition |
| resourceType | ty | 0..n | filterCriteria condition |
| sizeAbove | sza | 0..1 | filterCriteria condition |
| sizeBelow | szb | 0..1 | filterCriteria condition |
| contentType | cty | 0..n | filterCriteria condition |
| Limit | lim | 0..1 | filterCriteria condition |
| Attribute | atr | 0..n | filterCriteria condition |
| filterUsage | fu | 0..1 | filterCriteria condition |
| Discovery Result Type | drt | 0..1 |  |

For partial Retrieve request primitives, the To parameter may include the name of a single attribute separated by a ‘#’ character from the resource ID. If multiple resource attributes are to be retrieved with a partial retrieve request primitive, these attributes are included in form of an attributeList object (as specified in clause 6.3.4.9 of TS-0004 [] with empty values) in the Content parameter.

In both cases, the short resource attribute name(s) shall be included into the query component of request-target using “atrl’ (i.e. short name of attributeList) as <query field name>. If more than a single attribute name is included into the query component, these shall be separated by a ‘+’ character.

For example, if three resource attributes with long names resourceID, labels and requestReachability are indicated in the Content primitive parameter, the query component atrl=ri+lbl+rr is attached to the request-target. In case just a single attribute “rr” is indicated in the To parameter separated by ‘#’ character, the query component atrl=rr is attached to the request-target. The ‘#’ character and following attribute name shall be omitted from the path component of the request line.

At the HTTP server side, the reverse operation shall take place, when constructing the retrieve request primitive from the receive HTTP request message. Single attribute names in the query component may either be mapped back into the To parameter following a ‘#’ character, or included into the Content parameter using the attributeList format with just a single list element included. Multiple attributes shall be included into the Content parameter as specified in [3].

### -----------------------End of change 1-------------------------------------------