| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#20 |
| Source:* | Qualcomm Inc. |
| Date:* | 2015-11-10 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Minor correction to Notification for Asynchronous Non-blocking Request procedure |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004v2.2.0 |
| Clauses/Sub Clauses* | 7.4.1.2.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

There is an error in Section 7.4.1.2.4. According to ARC TS-0001, it says;

nonBlockingRequestAsynch {optional list of notification targets}: In case the request is accepted by the Receiver CSE, the Receiver CSE shall respond, after acceptance, with an Acknowledgement confirming that the Receiver CSE will further process the request. The result of the requested operation needs to be sent as notification(s) to the notification target(s) provided optionally within this parameter as a list of entities or to the Originator when no notification target list is provided. When an empty notification target list is provided by the Originator, no notification with the result of the requested operation shall be sent at all. Processing of Non-Blocking Requests is defined in clause 8.2.2 and in particular for the asynchronous case in clause 8.2.2.3.

There are three possibilities.

- Notification target is not included ( Notification back to the Originator.

- Notification target is included ( Notification(s) back to the list of notification targets.

- Notification target is included, but empty ( No notification at all.

The current text in Section 7.4.1.2.4 doesn’t specify the case 3 correctly. This CR propose a correction to this section.

### -----------------------Start of change 1-------------------------------------------

##### Notification for Asynchronous Non-blocking Request

Originator:

When the requested operation for a nonBlockingAsynch request is completed, the Originator (=hosting CSE of the resource) shall send a Notify request primitive to inform the final result of requested operation against the oneM2M resource. When the notificationURI was present and empty in the Response Type parameter in the previously received nonBlockingAsync request, no notification with the result of the requested operation shall be sent at all by the Originator.

- The Originator shall compose a Request primitive with following parameter settings:

  - The From parameter shall be set to the ID of the Originator (i.e. hosting CSE which hosts the targeted resource in the previously received nonBlockingAsynch request).

  - If the notificationURI was not present in the Response Type parameter in the previously received nonBlockingAsync request, then the To parameter shall be set to the Originator of the previously received nonBlockingAsynch request.
If the notificationURI was present and not empty in the Response Type parameter in the previously received nonBlockingAsync request, then the To parameter shall be set to the notificationURI.

  - The Response Type : If the Originator selects to send the Notification in nonBlockingAsynch mode, the Originator shall include empty notification target.

  - The Content parameter shall be set to the response to the previously received nonBlockingAsynch request as m2m:responsePrimitive.

- The Originator shall send the Request primitive. See clause 7.2.1.2 for detail.

Receiver:

No change from the generic procedure in clause 7.1.2.2.

### -----------------------End of change 1-------------------------------------------