| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#21 |
| Source:* | InterDigital |
| Date:* | 2016-01-18 |
| Contact:* | Dale Seed (dale.seed@InterDigital.com ) |
| Reason for Change/s:* | CR proposes to correct the Node XSD |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v2.2.0 |
| Clauses/Sub Clauses* | Node XSD |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: PRO-2016-0001-CR-CorrectionInNodeXSD_R1 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to correct the node resource XSD. The “<xs:extension base=” for nodeAnnc should be announcedResource and not announceableResource.

## ----------------------- Start of change 1 -----------------------

<xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.onem2m.org/xml/protocols"

xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

elementFormDefault="unqualified" xmlns:xs="http://www.w3.org/2001/XMLSchema">

<xs:include schemaLocation="CDT-commonTypes-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-memory-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-battery-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-areaNwkInfo-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-areaNwkDeviceInfo-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-firmware-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-software-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-deviceInfo-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-deviceCapability-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-reboot-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-eventLog-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-cmdhPolicy-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-activeCmdhPolicy-v2_2_0.xsd" />

<xs:include schemaLocation="CDT-subscription-v2_2_0.xsd" />

<xs:element name="node">

<xs:complexType>

<xs:complexContent>

<!-- Inherit common attributes for announceable Resources -->

<xs:extension base="m2m:announceableResource">

<!-- Resource Specific Attributes -->

<xs:sequence>

<xs:element name="nodeID" type="m2m:nodeID" />

<xs:element name="hostedCSELink" type="m2m:ID" minOccurs="0" />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" />

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:memory" />

<xs:element ref="m2m:battery" />

<xs:element ref="m2m:areaNwkInfo" />

<xs:element ref="m2m:areaNwkDeviceInfo" />

<xs:element ref="m2m:firmware" />

<xs:element ref="m2m:software" />

<xs:element ref="m2m:deviceInfo" />

<xs:element ref="m2m:deviceCapability" />

<xs:element ref="m2m:reboot" />

<xs:element ref="m2m:eventLog" />

<xs:element ref="m2m:cmdhPolicy" />

<xs:element ref="m2m:activeCmdhPolicy" />

<xs:element ref="m2m:subscription" />

</xs:choice>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

<xs:element name="nodeAnnc">

<xs:complexType>

<xs:complexContent>

<!-- Inherit common attributes for announceable Resources -->

<xs:extension base="m2m:announcedResource">

<!-- Resource Specific Attributes -->

<xs:sequence>

<xs:element name="nodeID" type="m2m:nodeID" />

<xs:element name="hostedCSELink" type="m2m:ID" minOccurs="0" />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded" />

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:memoryAnnc" />

<xs:element ref="m2m:batteryAnnc" />

<xs:element ref="m2m:areaNwkInfoAnnc" />

<xs:element ref="m2m:areaNwkDeviceInfoAnnc" />

<xs:element ref="m2m:firmwareAnnc" />

<xs:element ref="m2m:softwareAnnc" />

<xs:element ref="m2m:deviceInfoAnnc" />

<xs:element ref="m2m:deviceCapabilityAnnc" />

<xs:element ref="m2m:rebootAnnc" />

<xs:element ref="m2m:eventLogAnnc" />

<xs:element ref="m2m:subscription" />

</xs:choice>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

</xs:schema>

## ----------------------- Endof change 1 -----------------------

- 1, end of change 1, start of new clause, end of new clause.?