| CHANGE REQUEST |
| --- |
| Meeting:* | PRO #TP21 |
| Source:* | KETI, NEC |
| Date:* | 2016-01-18 |
| Contact:* | Minwoo Ryu, Jaeho Kim, SungChan Choi, KETI, minu@keti.re.kr Martin Bauer, NEC, martin.bauer@neclab.eu |
| Reason for Change/s:* | Revision of adding specific procedure of <semanticDescriptor> resource |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active WI-0005 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V2 |
| Clauses/Sub Clauses* | 7.3.30 |
| Type of change: * | Active WI-0005 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

## This CR adds specific procedures and definitions regarding a <semanticDescriptor> resource including CREATE, RETRIEVE, UPDATE, and, DELETE.

### -----------------------Start of change 1-------------------------------------------

### 7.3.30 Resource Type <semanticDescriptor>

#### 7.3.30.1 Introduction

The <semanticDescriptor> resource is used to store a semantic description pertaining to a resource and potentially sub-resources. Such a description shall be according to subject-predicate-object triples as defined in the RDF graph-based data model [4]. The detailed description can be found in the clause 9.6.30 in TS-0001 Functional Architecture [6].

Table 7.3.30.1-1: Data type definition of <semanticDescriptor> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| semanticDescriptor | TBD |  |

Table 7.3.30.1-2: Universal/Common Attributes of <semanticDescriptor> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| labels | O | O |

Table 7.3.30.1-3: Resource Specific Attributes of <semanticDescriptor> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| creator | O | NP | m2m:ID | No default |
| descriptor | M | O | xs:string | No default |
| ontologyRef | O | O | xs:anyURI | No default |

Table 7.3.30.1-4: Child resources of <semanticDescriptor> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause 7.3.8 |

#### 7.3.30.2 <semanticDescriptor> resource specific procedure on CRUD operations

This clause describes <semanticDescriptor> resource specific primitive behaviour for CRUD operations.

##### 7.3.30.2.1 Create

Originator:

No change from the generic procedures in clause 7.1.2.1

Receiver:

No change from the generic procedures in clause 7.1.2.2

##### 7.3.30.2.2 Retrieve

Originator:

No change from the generic procedures in clause 7.1.2.1

Receiver:

No change from the generic procedures in clause 7.1.2.2

##### 7.3.30.2.3 Update

Originator:

If the Originator updates semantic triples (e.g., RDF) in <semanticDescriptor> resource, it shall be execute the following steps in order:

- Complete update: No change from the generic procedures in clause 7.1.2.1

- Selective update of specific semantic triples: :

- Targeted <semanticDescriptor> resource shall be addressed with “#” character and descriptor attribute after <semanticDescriptor> resource address.

- Primitive specific operation on Orig-1.0 “Compose Request primitive”:
Content parameter shall  include semantic triples with SPARQL update statements as defined in the SPARQL query language [x].

Receiver:

- Complete update: No change from the generic procedures in clause 7.1.2.2.

- Selective update of specific semantic triples:

Primitive specific operation on Recv-6.5 “Create/Update/Retrieve/Delete/Notify operation is performed”:

- If the semantic description in Request exists in the targeted <semanticDescriptior> resource, the hosting CSE shall update the semantic description according to the meaning of the SPARQL statements in Request.

- If the semantic description in Request does not exists in the targeted <semanticDescriptor> resource, the hosting CSE shall return failure information with additional error information as defined in clause 7.1.1.2

##### 7.3.30.2.4 Delete

Originator:

No change from the generic procedures in clause 7.1.2.1.

Receiver:

No change from the generic procedures in clause 7.1.2.2

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## Normative references

The following referenced documents are necessary for the application of the present document.

[1]	W3C, Extensible Markup Language (XML) 1.0 (Fifth Edition), W3C Recommendation 26 November 2008.

[2]	IETF RFC 3986: "Uniform Resource Identifier (URI): Generic Syntax".

[3]	W3C XMLSchemaP2: "W3C Recommendation (2004), XML Schema Part 2:Datatypes Second Edition.".

[4]	oneM2M TS-0005 “Management Enablement (OMA)”

[5]	oneM2M TS-0006 “Management Enablement (BBF)”

[6]	oneM2M TS-0001 "Functional Architecture"

[7]	oneM2M TS-0003 “Security Solutions”

[8]	IEEE 754-2008: IEEE. IEEE Standard for Floating-Point Arithmetic. 29 August 2008. http://ieeexplore.ieee.org/servlet/opac?punumber=4610933

[9]	IETF RFC 3548: "The Base16, Base32, and Base64 Data Encodings". 2003.

[10]	IETF RFC 2045: "Multipurpose Internet Mail Extensions (MIME) Part One: Format of Internet Message Bodies". 1996.

[11]	IETF RFC 3987:" Internationalized Resource Identifiers (IRIs)" . January 2005.

[12]	IETF BCP 47: "Best Current Practices 47". Concatenation of RFC 4646:" Tags for Identifying Languages"(2006) and RFC 4647: "Matching of Language Tags"( 2006).

[13]	IETF RFC 3588: "Diameter Base Protocol". September 2003.

[14]	IETF RFC 6733: "Diameter Base Protocol". October 2012.

[15]	3GPP TS 23.682: "Architecture enhancements to facilitate communications with packet data networks and applications" Release 11.

[16]	3GPP TS 29.368: "Tsp interface protocol between the MTC Interworking Function (MTC-IWF) and Service Capability Server (SCS)" Release 11.

[17]	3GPP TS 23.003: "Numbering, addressing and identification".

[18]	(void)

[19]	IETF RFC 7159: "The JavaScript Object Notation (JSON) Data Interchange Format".

[20]	IETF RFC 4234: "Augmented BNF for Syntax Specifications: ABNF"

[21]	IETF RFC 3629: " UTF-8, a transformation format of ISO 10646".

[22]	oneM2M TS-0008 CoAP Protocol Binding

[23]	oneM2M TS-0009 HTTP Protocol Binding

[24]	oneM2M TS-0010 MQTT Protocol Binding

[25]	oneM2M TS-0011 Common Terminology

[26]	IETF RFC 6837: " Media Type Specifications and Registration Procedures".

[27]	ISO 3601:2004; "Data elements and interchange formats -- Information interchange -- Representation of dates and times".

[28]	OMA-TS-REST-NetAPI_TerminalLocation-V1_0-20130924-A: "RESTful Network API for Terminal Location", Version 1.0.

[29]	IETF RFC 4632: " Classless Inter-domain Routing (CIDR): The Internet Address Assignment and Aggregation Plan".

[30]	IETF RFC 5952: "A Recommendation for IPv6 Address Text Representation".

[31]	3GPP TS 32.299: " Telecommunication management;Charging management;Diameter charging applications" Release 11.

[32]	IETF RFC 4006: " Diameter Credit-Control Application". Auguest 2005.

[x]	W3C SPARQL 1.1 Query Language

### -----------------------End of Changes to References  -------------