| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#21 |
| Source:* | IBM |
| Date:* | 2016-01-19 |
| Contact:* | Peter Niblett ( peter_niblett@uk.ibm.com ) |
| Reason for Change/s:* | Align terminology better with TS-0004 and add some clarifications |
| CR against: Release* | Rel 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TS-0004 Service Layer Core Protocol v2.2.1 |
| Clauses/Sub Clauses* | 6.5.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: PRO-2016-0026 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Clause 6.5.3 of TS-0010 introduces a new primitive parameter, called xM2M-Accept, used just for the MQTT binding. This is needed because MQTT doesn’t have the equivalent of the HTTP Accept header or CoAP Accept option.

This change request proposes some tidying up of the wording of the clause.

- Use the term “serialization” rather than “content format” since TS-0004 talks about “serialization”

- Be consistent about calling it xM2M-Accept

- Add a sentence about what happens if there is no xM2M-Accept in the request message

- Limit the number of occurences of xM2M-Accept to be 0 or 1.

We might also consider whether the new parameter should in fact be defined in TS-0004, and whether it should be given a short name.

## ----------------------- Start of change 1 -----------------------

### 6.5.3	Serialization format

The request primitive can contain an additional parameter called xM2M-Accept which indicates the serialization format  that the Originator is prepared to accept in a Response.

If the Receiver supports the kind of serialization specified in the request’s xM2M-Accept parameter, the Receiver shall respond using that serialization. If the Receiver does not support the serialization specified in the request’s xM2M-Accept parameter, "Not Acceptable" shall be sent as the ResponseStatusCode unless another error code takes precedence for this response.

If the request does not contain the xM2M-Accept parameter, the Receiver is free to choose to use any oneM2M-supported serialization, since the requestor has not indicated a preference.

Possible values for the xM2M-Accept parameter are listed below:

- application/xml

- application/json

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?