| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#22 |
| Source:* | InterDigital |
| Date:* | 2016-3-2 |
| Contact:* | Dale Seed, InterDigital - Dale.Seed@InterDigital.com Chitra Vaidyanathan, InterDigital - Chitra.Vaidyanathan@InterDigital.com |
| Reason for Change/s:* | Add optional values and operators to eventNotificationCriteria |
| CR against: Release* | Rel2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2_4_0 |
| Clauses/Sub Clauses* | CommonTypes XSD file & oneM2M-TS-0004 Core Protocol Specification |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

One of the attributes of <subscription> is eventNotificationCriteria which contains conditions that indicate when a notification shall be generated.

One of the defined “conditions” of eventNOtificationCriteria is attribute. The current definition of this condition requires that on any update to any of the attributes specified in the attribute list, a notification shall be generated.  However, the definition currently supported in TS-0004 is slightly different.  In TS-0004, attribute has a type definition of m2m:attribute which has two elements name and value, both of which have multiplicity of 1 making them mandatory.  Therefore an entry in the attribute list must consist of a name and value pair, implying that a notification shall only be generated on an update to any of the attributes mentioned in this list in which the updated value equals the value specified in that attribute’s value element.

This contribution as well as the corresponding contribution to TS-0001, propose to align TS-0001 and TS-0004 on the definition of the eventNOtificationCriteria attribute condition as well as introduce one small enhancement by proposing the following:

- In TS-0004, update the multiplicity of the value element in the m2m:attribute type definition to 0..1 to make it optional rather than mandatory.  When a value is not present, this will allow a notification to be generated when any change is made to a specified attribute.

- In TS-0004 introduce a new operator element in the m2m:attribute type definition with a multiplicity of 0..1 to make it optional.

- In TS-00001, update the description of the attribute eventNOtificationCriteria condition to mention the missing  value element (which is optional).

- In TS-0001 introduce a new operator element in the attribute eventNOtificationCriteria condition.  The proposed values are equalTo, greaterThan, lessThan, notEqual.   This will enable the attribute condition to have a name, operator and value triple for each entry in the attribute list.

The above changes will enable more flexible and powerful subscription / notification functionality.   This is useful for subscriptions to resource types such as <flexContainer>, <mgmtObj>, <container>, etc.  The following is a <flexContainer> example, showing the benefits of this proposed enhancement.

For example, a <flexContainer> is defined for a smart parking garage.  The garage keeps track of the number of available spaces via a <flexContainer> resource having a custom attribute named availSpaces.  A subscription is created to the <flexContainer> resource to generate a notification when the number of available space is less than a value 50.  This is accomplished by configuring the eventNOtificationCriteria of the subscription with an eventType condition of ‘A - Update to attributes of the subscribed-to resource’ and configuring the attribute condition elements name to ‘availSpaces’, operation to ‘lessThan’ and value to ‘50’.   Thereafter, as updates are made to the <flexContainer> the CSE monitors the value of the availSpaces custom attribute to detect if the value drops below 50.  If/when this occurs, the CSE generates a notification.

### -----------------------Start of change 1-------------------------------------------

#### 6.3.4.2.32 m2m:operator

Used in m2m:attribute.

Table 6.3.4.2.32-1: Interpretation of operator

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | equalTo | This is the default value when the operator is not present |
| 2 | greaterThan |  |
| 3 | lessThan |  |
| 4 | equalTo |  |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 6.3.5.9 m2m:attribute

Used in m2m:eventNotificationCriteria and m2m:filterCriteria.

Table 6.3.4.8-1: Type Definition of m2m:attribute

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| name | xs:NCName | 1 |  |
| value | xs:anyType | 0..1 |  |
| operator | m2m:operator | 0..1 |  |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### Changes in the CDT-commonTypes-v2_4_0.xsd:

<xs:complexType name="attribute">

<xs:sequence>

<xs:element name="name" type="xs:NCName" />

<xs:element name="value" type="xs:anyType" minOccurs=0/>

<xs:element name="operator" type="m2m:operator" minOccurs=0/>

</xs:sequence>

</xs:complexType>

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### Changes in the CDT-enumerationTypes-v2_4_0.xsd:

<xs:simpleType name="operator">

<xs:annotation>

<xs:documentation>Used for eventNotificationCriteria attribute of &lt;subscription&gt; resource.</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:integer">

<!-- equalTo -->

<xs:enumeration value="1" />

<!—greaterThan -->

<xs:enumeration value="2" />

<!-- lessThan -->

<xs:enumeration value="3" />

<!-- equalTo -->

<xs:enumeration value="4" />

</xs:restriction>

</xs:simpleType>

### -----------------------End of change 4---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?