| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 22 |
| Source:* | Catalina Mladin, InterDigital |
| Date:* | 2015-03-06 |
| Contact:* | Catalina Mladin, Catalina.Mladin@InterDigital.com Martin Bauer, NEC, martin.bauer@neclab.eu |
| Reason for Change/s:* | Introduces procedures for Semantic Discovery using semanticFanOutPoint |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | Active WI -5 MNT maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v2.4.0 |
| Clauses/Sub Clauses* | 6.3.5.8, 7.3.3.17, (new) 7.3.3.18, 7.4.13, (new)7.4.14a |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Introduces stage 3 for semantic discovery using <semanticFanOutPoint>. This is a first draft for discussion only, there are several issues for discussion

### -----------------------Start  of change 1---------------------------------------------

#### m2m:filterCriteria

Used indirectly in the <request> resource and for the  Filter Criteria parameter in a request.

Table 6.3.5.8-1: Type Definition of m2m:filterCriteria

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| createdBefore | m2m:timestamp | 0..1 |  |
| createdAfter | m2m:timestamp | 0..1 |  |
| modifiedSince | m2m:timestamp | 0..1 |  |
| unmodifiedSince | m2m:timestamp | 0..1 |  |
| stateTagSmaller | xs:positiveInteger | 0..1 |  |
| stateTagBigger | xs:nonNegativeInteger | 0..1 |  |
| expireBefore | m2m:timestamp | 0..1 |  |
| expireAfter | m2m:timestamp | 0..1 |  |
| labels | m2m:labels | 0..1 |  |
| resourceType | list of m2m:resourceType | 0..1 |  |
| sizeAbove | xs:nonNegativeInteger | 0..1 |  |
| sizeBelow | xs:positiveInteger | 0..1 |  |
| contentType | m2m:typeOfContent | 0..n |  |
| attribute | m2m:attribute | 0..n |  |
| filterUsage | m2m:filterUsage | 0..1 |  |
| limit | xs:nonNegativeInteger | 0..1 |  |
| semanticsFilter | xs: string | 0..n |  |

### -----------------------End  of change 1---------------------------------------------

### -----------------------Start  of change 2---------------------------------------------

#### Using Filter Criteria for identification of target resources

When the Filter Criteria primitive parameter is present in a request primitive, it shall be applied for identification of the applicable target resources of the respective operation. This may apply to Retrieve, Delete, Discovery and Semantic Resource Discovery operations as specified in clauses 7.3.3.6, 7.3.3.8, 7.3.3.14 and 7.3.3.18 respectively.

The Filter Criteria primitive parameter defines conditions on resource attributes. Resources matching the conditions shall be selected as target of the operation. Table 7.3.3.17-1 summarizes the various filter criteria and conditions. Each row in the table represents a different filter condition type.

If multiple conditions of different type (i.e. different condition tags) are present in the Filter Criteria parameter, these shall be satisfied all to pass the overall combined filter condition, i.e. the combined condition shall be derived by applying Boolean AND operation across each individual condition.

If multiple conditions of the same type (i.e. same condition tag) are present in the Filter Criteria parameter, these shall be combined by applying Boolean OR operation. This applies to condition tags labels, resourceType, contentType or attribute for multiplicity n > 1.

Table 7.3.3.17-1: Summary on Filter conditions

| Condition Tag | Multiplicity | Targeted Resource Attribute | Matching Condition |
| --- | --- | --- | --- |
| createdBefore, | 0..1 | creationTime | creationTime < createdBefore, see clause 7.3.3.17.1 |
| createdAfter | 0..1 |  | createdAfter ≤ creationTime , see clause 7.3.3.17.1 |
| lastModifiedBefore | 0..1 | lastModifiedTime | lastModifiedTime < lastModifiedBefore, see clause 7.3.3.17.2 |
| lastModifiedAfter | 0..1 |  | lastModifiedAfter ≤ lastModifiedTime, see clause 7.3.3.17.2 |
| stateTagSmaller | 0..1 | stateTag | stateTagSmaller < stateTag, see clause 7.3.3.17.3 |
| stateTagBigger | 0..1 |  | stateTag ≤ stateTagBigger, see clause 7.3.3.17.3 |
| expireBefore | 0..1 | expirationTime | expirationTime < expireBefore, see clause 7.3.3.17.4 |
| expireAfter | 0..1 |  | expireAfter ≤ expirationTime , see clause 7.3.3.17.4 |
| labels | 0..n | labels | see clause 7.3.3.17.5 |
| resourceType | 0..n | resourceType | see clause 7.3.3.17.6 |
| sizeBelow | 0..1 | contentSize | contentSize < sizeBelow, see clause 7.3.3.17.7 |
| sizeAbove | 0..1 |  | sizeAbove ≤ contentSize, see clause 7.3.3.17.7 |
| typeOfContent | 0..n | contentInfo | matched with typeOfContent component in contentInfo, see clause 7.3.3.17.8 |
| attribute | 0..n | (variable) | name and value of Filter Criteria attribute matches resource attribute, see clause 7.3.3.17.9 |
| limits | 0..1 | (not applicable) | Constraint on maximum number of targeted resources, see clause 7.3.3.17.10 |
| filterUsage | 0..1 | (not applicable) | Indicator specifying the use case of Filter Criteria parameters |
| semanticsFilter | 0..n | (not applicable) | Semantic filter in SPARQL. |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 7.3.3.18	Semantic resource discovery

Semantic resource discovery is used to find resources in a CSE based on the semantic descriptions contained in the content attribute of <semanticDescriptor> resources.  Since an overall semantic description (logical tree) may be distributed across a set of <semanticDescriptor> resources,the semantic descriptions have to be retrieved before or as needed during the execution of the discovery request.

When using <semanticFanOutPoint>, the logical tree is distributed across the descriptors of the members of the parent <group> resource. The Group Hosting CSE indicates support and availability of semantic functionality by setting the semanticSupportIndicator attribute of the <group> resource to TRUE.

There are two alternatives for initiating semantic resource discovery:

- By sending a Retrieve request to the <semanticFanOutPoint> virtual resource, see section 7.4.14a

- By sending a Retrieve request with semanticsFilter and targeting a resource other than <semanticFanOutPoint>. In this alternative the semantic resource discovery request procedure shall be comprised of the following actions:

Originator:

The Originator shall follow the steps from Orig-1.0 to Orig-6.0 specified in clause 7.2.2.1 Generic Resource Request Procedure for Originator.

In addition to Orig-1.0, the following steps shall be performed.

The To parameter in the Retrieve Request indicates the root of where the semantic discovery begins.

The Retrieve Request shall include the SPARQL request in thesemanticsFilter parameter

Receiver:

The Receiver shall follow the steps from Recv-1.0 to Recv-7.0 specified in clause 7.2.2.2 Generic Resource Request Procedure for Receiver.

The following primitive specific operations shall be performed by the Hosting CSE after Recv-6.2 "Check existence of the addressed resource"

Hosting CSE shall not perform steps from Recv-6.3 to Recv-6.6 and perform the following steps instead.

- The Receiver shall find the <semanticDescriptor> resource(s) to which the Originator has "Discover" access right, under the addressed resource.

If the relatedSemantics attribute is empty or does not exist, the “Annotation-based method” (using resourceDescriptorLink) detailed in clause 7.3.3.18.1 shall be used.

If the relatedSemantics attribute is not empty the “Resource link-based method” (using relatedSemantics) detailed in clause 7.3.3.18.2 shall be used.

- Perform Recv-6.7 “Create a success response" where the Response shall include the resources matched based on the SPARQL engine result...

##### Annotation-based method

In the annotation-based method,  related <semanticDescriptor> resources are identified in the semantic description itself using a special annotation property called onem2m:resourceDescriptorLink, which refers to another <semanticDescriptor> resource whose descriptor attribute  may contain relevant information for matching the semantic filter. Whenever, during the execution of the SPARQL request on the semantic description in the descriptor attribute of the <semanticDescriptor>, such an annotation property for a matched semantic element is found, the execution is halted, the content of the descriptor attribute of the referred to <semanticDescriptor> is retrieved and the execution is continued on the combined content of the already present and the just retrieved semantic information.

For retrieving the semantic information from additional  <semanticDescriptor> resources as described in the paragraph above, the steps from Recv-1.0 to Recv-7.0 specified in clause 7.2.2.2 Generic Resource Request Procedure for Receiver shall be followed.

##### Resource link-based method

In this option, the relatedSemantics attribute contains the list of <semanticDescriptor> resources which shall be retrieved for the purpose of creating the logical tree

The receiver retrieves the <semanticDescriptor> resource of the request target and the addresses provided in the relatedSemantics attribute

For each <semanticDescriptor> resource addressed in the relatedSematics attribute, the Receiver shall follow the steps from Recv-1.0 to Recv-7.0 specified in clause 7.2.2.2 Generic Resource Request Procedure for Receiver.

The Hosting CSE shall find all the <semanticDescriptor> resources based on the, which match all the configured filterCriteria and which the Originator has "Discover" access right, under the addressed resource".

The Receiver shall aggregate the descriptors of all the found and deliver the content to the SPARQL engine.

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 7.4.13 Resource Type <group>

#### 7.4.13.1 Introduction

The <group> resource represents a group of resources of the same or mixed types. The <group> resource can be used to do bulk manipulations on the resources represented by the memberIDs attribute. The <group> resource contains an attribute that represents the members of the group and a virtual resource (the <fanOutPoint>) that allows operations to be applied to the resources represented by those members. The detailed description can be found in clause 9.6.13 in TS-0001 [6].

Table 7.4.13.1-1: Data type definition of <group> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| group | CDT-group-v2_4_0.xsd |  |

Table 7.4.13.1-2: Universal/Common Attributes of <group> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |

Table 7.4.13.1-3: Resource Specific Attributes of <group> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| creator | O | NP | m2m:ID |  |
| memberType | O | NP | m2m:memberType | Default value is set to 'MIXED' |
| currentNrOfMembers | NP | NP | xs:positiveInteger | No default (This is generated by the hosting CSE and limited by the maxNrOfMembers attribute of the <group> resource) |
| maxNrOfMembers | M | O | xs:positiveInteger | No default |
| memberIDs | M | O | list of xs:anyURI | No default |
| membersAccessControlPolicyIDs | O | O | list of xs:anyURI | No default |
| memberTypeValidated | NP | NP | xs:boolean | No default (This is generated by the hosting CSE) |
| consistencyStrategy | O | NP | m2m:consistencyStrategy | Default value is set to 'ABANDON_MEMBER' |
| groupName | O | O | xs:string | No default |

Table 7.4.13.1-4: Child resources of <group> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause 7.4.8 |
| <fanOutPoint> | fanOutPoint | 1 | Clause 7.4.14 |
| <semanticFanOutPoint> | semanticFanOutPoint | 1 | Clause 7.4.14a |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### 7.4.14a  Resource Type <semanticFanOutPoint>

### 7.4.14a.1  Introduction

The <semanticFanOutPoint> resource is a virtual resource because it does not have a representation. It is the child resource of a <group> resource. Only Retrieve requests to the <semanticFanOutPoint> resource are valid, the other operations are not allowed based on the syntax check step at the Receiver. When a Retrieve request is received by the <semanticFanOutPoint> it triggers a semantic discovery procedure. The detailed description can be found in clause 10.2.35 in TS-0001 [6].

There are no common attributes, resource specific attributes or xsd file to <semanticFanOutPoint> resource because it is a virtual resource.

A <semanticFanOutPoint> can be addressed in one of two ways:

- Using the URI retrieved from its parent <group> resource;  or

- Using a hierarchical URI formed by taking the hierarchical URI of the parent <group> and appending the string /semanticFanOutPoint to that URI

#### 7.4.14a.2 <semanticFanOutPoint> operations

Semantic resource discovery is used to find resources in a CSE based on the semantic descriptions contained in the content attribute of <semanticDescriptor> resources.  Since an overall semantic description (logical tree) may be distributed across a set of <semanticDescriptor> resources, the procedure requires that the set of related resources is first retrieved and then the descriptors are aggregated and submitted for processing as a single logical tree.

When using <semanticFanOutPoint>, the logical tree is distributed across the descriptors of the members of the parent <group> resource. The Group Hosting CSE indicates support and availability of semantic functionality  by setting the semanticSupportIndicator attribute of the <group> resource to TRUE.

Targeting the <semanticFanOutPoint> virtual resource results in creating and distributing retrieve operations to all the related resources, as described in section 7.4.14a.2.1. This results in an aggregated descriptor containing the overall logical tree.

##### 7.4.14a.2.1 Create and distribute  <semanticDescriptor> Retrieve requests to each member, construct logical tree

For each member hosting CSE, the group hosting CSE shall perform the following steps:

- The primitive parameters From and To shall be mapped to corresponding Retrieve Requests to be sent out to each member of the group. The primitive parameter From shall be directly used. The prefix of primitive parameter To i.e. <URI of group resource>/semanticFanOutPoint shall be replaced by hierarchical URIs derived from the attribute memberIDs of the group resource.

In addition, the group hosting CSE shall generate a unique group request identifier, add it as a primitive parameter to the Request and locally store the group request identifier as per the local policy.

- The group hosting CSE shall execute "Compose Request primitives" using the primitive parameter semanticsFilter set to FALSE.

c)	"Send the Request to the receiver CSE".

d)	"Wait for Response primitives".

During semanticFanOutPoint manipulation, each member hosting CSE receiving a Request sent from the group hosting CSE shall check if the Request contains a Group Request Identifier parameter. If the Request contains a Group Request Identifier parameter, the member hosting CSE shall compare the Group Request Identifier parameter to the Group Request Identifier locally stored. If a match is found, the member hosting CSE shall reject the request with the Response Status Code indicating "GROUP_REQUEST_IDENTIFIER_EXISTS" error in the Response primitive. Otherwise, the member hosting CSE shall continue with the operations according to the Request and locally store the Group Request Identifier parameter.

#### 7.4.14a.3 <semanticFanOutPoint> resource specific procedure on CRUD operations

##### 7.4.14a.3.1 Introduction

This sub-clause describes <semanticFanOutPoint> resource specific behaviour for CRUD operations.

##### 7.4.14a.3.2 Create

Originator:

The < semanticFanOutPoint> resource shall not support Create operations via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order.

a)	"Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

g)	"Send the Response primitive".

##### 7.4.14a.3.3 Retrieve

Originator:

No primitive specific operations.

Receiver:

The following primitive specific operations shall be performed by the Group Hosting CSE after Recv-6.2 "Check existence of the addressed resource"

1) Check that the semanticSupportIndicator of the parent <group> resource is set to TRUE.

2) Check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

2)	Fanout <semanticDescriptor> Retrieve Request to each CSE hosting sub-groups or members, refer to 7.4.14a.2.1 “Create and distribute <semanticDescriptor> Retrieve Requests to each member”.

3)  Aggregate <semanticDescriptor> Retrieve Responses from its member resources and deliver the content to the SPARQL engine.

4) Perform Recv-6.7 “Create a success response" where the Response shall include the SPARQL engine result.

50 The Receiver shall perform Recv-6.8 and the procedure is terminated.

##### 7.4.14a.3.4 Update

Originator:

The < semanticFanOutPoint> resource shall not support Update operations via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order.

a)	"Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

g)	"Send the Response primitive".

##### 7.4.14a.3.5 Delete

Originator:

The < semanticFanOutPoint> resource shall not support Delete operations via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order.

a)	"Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

g)	"Send the Response primitive".

### -----------------------End of change 5---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?