| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#22.3 |
| Source:* | TS-0004 Rapportuer |
| Date:* | 2016-04-27 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Reason for Change/s:* | In release 1, enum value assignment for m2m:resourceType and m2m:memberType are aligned. This CR proposes to keep that alignment in release 2. |
| CR against: Release* | R2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / <Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2.5.0 |
| Clauses/Sub Clauses* | 6.3.4.2.1, 6.3.4.2.11 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In release 1, enum assignments for m2m:resourceType and m2m:menberType are aligned. Also, if a resource is announceable then it use the same numbering scheme in the form of 100xx.

In TS-0004 v2.5.0, however, it doesn’t follow the same numbering convention as shown in the next page.

This CR proposes to keep this alignment between two enum data types, except 24 (mixed) for menberType. This has been defined since release 1 and thus better not to change it.

Summary of the proposed changes:

- For m2m:resourceName, assignment should start from 25 for any new resorce. If the resoufrce is annauceable, then use the same numbering convention (100xx). Make 24 reserved.

- For m2m:meberType, use exact the same assignment as m2m:resourceType except for 24(mixed).

Note: Virtual resources are not assigned (pollingChannelURI, fanOutPoint, latest and oldest) in release 1. The same assumption is used for release 2 (semanticFanOutPoint, notificationTargetSelfReference, policyDecisionPoint).

In R01, WG3 agreed to assign value 0 for mixed.

Enum assignments in TS-0004 v2.5.0:

| Value | m2m:resourceType | m2m:memberType |
| --- | --- | --- |
| 1 | accessControlPolicy | accessControlPolicy |
| 2 | AE | AE |
| 3 | container | container |
| 4 | contentInstance | contentInstance |
| 5 | CSEBase | CSEBase |
| 6 | delivery | delivery |
| 7 | eventConfig | eventConfig |
| 8 | execInstance | execInstance |
| 9 | group | group |
| 10 | locationPolicy | locationPolicy |
| 11 | m2mServiceSubscriptionProfile | m2mServiceSubscriptionProfile |
| 12 | mgmtCmd | mgmtCmd |
| 13 | mgmtObj | mgmtObj |
| 14 | node | node |
| 15 | pollingChannel | pollingChannel |
| 16 | remoteCSE | remoteCSE |
| 17 | request | request |
| 18 | schedule | schedule |
| 19 | serviceSubscribedAppRule | serviceSubscribedAppRule |
| 20 | serviceSubscribedNode | serviceSubscribedNode |
| 21 | statsCollect | statsCollect |
| 22 | statsConfig | statsConfig |
| 23 | subscription | subscription |
| 24 | semanticDescriptor | notificationTargetMgmtPolicyRef |
| 25 | dynamicAuthorizationConsultation | notificationTargetPolicy |
| 26 | - | policyDeletionRules |
| 27 | - | notificationTargetSelfReference |
| 10001 | accessControlPolicyAnnc | accessControlPolicyAnnc |
| 10002 | AEAnnc | AEAnnc |
| 10003 | containerAnnc | containerAnnc |
| 10004 | contentInstanceAnnc | contentInstanceAnnc |
| 10009 | groupAnnc | groupAnnc |
| 10010 | locationPolicyAnnc | locationPolicyAnnc |
| 10013 | mgmtObjAnnc | mgmtObjAnnc |
| 10014 | nodeAnnc | nodeAnnc |
| 10016 | remoteCSEAnnc | remoteCSEAnnc |
| 10018 | scheduleAnnc | scheduleAnnc |
| 10019 | semanticDescriptorAnnc | - |
| 24 | - | mixed |

Proposed assignments:

| Value | m2m:resourceType | m2m:memberType |
| --- | --- | --- |
| 0 | - | mixed |
| 1 | accessControlPolicy | accessControlPolicy |
| 2 | AE | AE |
| 3 | container | container |
| 4 | contentInstance | contentInstance |
| 5 | CSEBase | CSEBase |
| 6 | delivery | delivery |
| 7 | eventConfig | eventConfig |
| 8 | execInstance | execInstance |
| 9 | group | group |
| 10 | locationPolicy | locationPolicy |
| 11 | m2mServiceSubscriptionProfile | m2mServiceSubscriptionProfile |
| 12 | mgmtCmd | mgmtCmd |
| 13 | mgmtObj | mgmtObj |
| 14 | node | node |
| 15 | pollingChannel | pollingChannel |
| 16 | remoteCSE | remoteCSE |
| 17 | request | request |
| 18 | schedule | schedule |
| 19 | serviceSubscribedAppRule | serviceSubscribedAppRule |
| 20 | serviceSubscribedNode | serviceSubscribedNode |
| 21 | statsCollect | statsCollect |
| 22 | statsConfig | statsConfig |
| 23 | subscription | subscription |
| 24 | semanticDescriptor | semanticDescriptor |
| 25 | notificationTargetMgmtPolicyRef | notificationTargetMgmtPolicyRef |
| 26 | notificationTargetPolicy | notificationTargetPolicy |
| 27 | policyDeletionRules | policyDeletionRules |
| 28 | flexContainer | flexContainer |
| 29 | timeSeries | timeSeries |
| 30 | timeSeriesInstance | timeSeriesInstance |
| 31 | role | role |
| 32 | token | token |
| 33 | trafficCharacteristics | trafficCharacteristics |
| 34 | trafficPattern | trafficPattern |
| 35 | dynamicAuthorizationConsultation | dynamicAuthorizationConsultation |
| 10001 | accessControlPolicyAnnc | accessControlPolicyAnnc |
| 10002 | AEAnnc | AEAnnc |
| 10003 | containerAnnc | containerAnnc |
| 10004 | contentInstanceAnnc | contentInstanceAnnc |
| 10009 | groupAnnc | groupAnnc |
| 10010 | locationPolicyAnnc | locationPolicyAnnc |
| 10013 | mgmtObjAnnc | mgmtObjAnnc |
| 10014 | nodeAnnc | nodeAnnc |
| 10016 | remoteCSEAnnc | remoteCSEAnnc |
| 10018 | scheduleAnnc | scheduleAnnc |
| 10024 | semanticDescriptorAnnc | semanticDescriptorAnnc |
| - | notificationTargetMgmtPolicyRef | notificationTargetMgmtPolicyRef |
| - | notificationTargetPolicy | notificationTargetPolicy |
| - | policyDeletionRules | policyDeletionRules |
| 10028 | flexContainerAnnc | flexContainerAnnc |
| 10029 | timeSeriesAnnc | timeSeriesAnnc |
| 10030 | timeSeriesInstanceAnnc | timeSeriesInstanceAnnc |
| - | role | role |
| - | token | token |
| 10033 | trafficCharacteristicsAnnc | trafficCharacteristicsAnnc |
| 10034 | trafficPatternAnnc | trafficPatternAnnc |
| 10035 | dynamicAuthorizationConsultationAnnc | dynamicAuthorizationConsultationAnnc |

### -----------------------Start of change 1-------------------------------------------

##### m2m:resourceType

Table 6.3.4.2.1-1: Interpretation of resourceType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | accessControlPolicy |  |
| 2 | AE |  |
| 3 | container |  |
| 4 | contentInstance |  |
| 5 | CSEBase |  |
| 6 | delivery |  |
| 7 | eventConfig |  |
| 8 | execInstance |  |
| 9 | group |  |
| 10 | locationPolicy |  |
| 11 | m2mServiceSubscriptionProfile |  |
| 12 | mgmtCmd |  |
| 13 | mgmtObj |  |
| 14 | node |  |
| 15 | pollingChannel |  |
| 16 | remoteCSE |  |
| 17 | request |  |
| 18 | schedule |  |
| 19 | serviceSubscribedAppRule |  |
| 20 | serviceSubscribedNode |  |
| 21 | statsCollect |  |
| 22 | statsConfig |  |
| 23 | subscription |  |
| 24 | semanticDescriptor |  |
| 25 | notificationTargetMgmtPolicyRef |  |
| 26 | notificationTargetPolicy |  |
| 27 | policyDeletionRules |  |
| 28 | flexContainer |  |
| 29 | timeSeries |  |
| 30 | timeSeriesInstance |  |
| 31 | role |  |
| 32 | token |  |
| 33 | trafficCharacteristics |  |
| 34 | trafficPattern |  |
| 35 | dynamicAuthorizationConsultation |  |
| 10001 | accessControlPolicyAnnc |  |
| 10002 | AEAnnc |  |
| 10003 | containerAnnc |  |
| 10004 | contentInstanceAnnc |  |
| 10009 | groupAnnc |  |
| 10010 | locationPolicyAnnc |  |
| 10013 | mgmtObjAnnc |  |
| 10014 | nodeAnnc |  |
| 10016 | remoteCSEAnnc |  |
| 10018 | scheduleAnnc |  |
| 10024 | semanticDescriptorAnnc |  |
| 10028 | flexContainerAnnc |  |
| 10029 | timeSeriesAnnc |  |
| 10030 | timeSeriesInstanceAnnc |  |
| 10033 | trafficCharacteristicsAnnc |  |
| 10034 | trafficPatternAnnc |  |
| 10035 | dynamicAuthorizationConsultationAnnc |  |
| NOTE: See clause 6.4.1 "Request message parameter data types" |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

##### m2m:memberType

Used for memberType attribute in <group> resource.

Table 6.3.4.2.11-1: Interpretation of memberType

| Value | Interpretation | Note |
| --- | --- | --- |
| 0 | mixed | A mixture of all the resource types (except mixed itself). |
| 1 | accessControlPolicy |  |
| 2 | AE |  |
| 3 | container |  |
| 4 | contentInstance |  |
| 5 | CSEBase |  |
| 6 | delivery |  |
| 7 | eventConfig |  |
| 8 | execInstance |  |
| 9 | group |  |
| 10 | locationPolicy |  |
| 11 | m2mServiceSubscription |  |
| 12 | mgmtCmd |  |
| 13 | mgmtObj |  |
| 14 | node |  |
| 15 | pollingChannel |  |
| 16 | remoteCSE |  |
| 17 | request |  |
| 18 | schedule |  |
| 19 | serviceSubscribedAppRule |  |
| 20 | serviceSubscribedNode |  |
| 21 | statsCollect |  |
| 22 | statsConfig |  |
| 23 | subscription |  |
| 24 | semanticDescriptor |  |
| 25 | notificationTargetMgmtPolicyRef |  |
| 26 | notificationTargetPolicy |  |
| 27 | policyDeletionRules |  |
| 28 | flexContainer |  |
| 29 | timeSeries |  |
| 30 | timeSeriesInstance |  |
| 31 | role |  |
| 32 | token |  |
| 33 | trafficCharacteristics |  |
| 34 | trafficPattern |  |
| 35 | dynamicAuthorizationConsultation |  |
| 10001 | accessControlPolicyAnnc |  |
| 10002 | AEAnnc |  |
| 10003 | containerAnnc |  |
| 10004 | contentInstanceAnnc |  |
| 10009 | groupAnnc |  |
| 10010 | locationPolicyAnnc |  |
| 10013 | mgmtObjAnnc |  |
| 10014 | nodeAnnc |  |
| 10016 | remoteCSEAnnc |  |
| 10018 | scheduleAnnc |  |
| 10024 | semanticDescriptorAnnc |  |
| 10028 | flexContainerAnnc |  |
| 10029 | timeSeriesAnnc |  |
| 10030 | timeSeriesInstanceAnnc |  |
| 10033 | trafficCharacteristicsAnnc |  |
| 10034 | trafficPatternAnnc |  |
| 10035 | dynamicAuthorizationConsultationAnnc |  |
| NOTE: See clause 7.4.13 "Resource Type group" |

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?