| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#23 |
| Source:* | Huawei Technologies Co.,Ltd. |
| Date:* | 2016-05-06 |
| Contact:* | Jiaxin Yin, yinjiaxin@huawei.com |
| Reason for Change/s:* | The CR is to add stage 3 procedure support for the arc contribution on group responses |
| CR against: Release* | Release Two |
| CR against: WI* | Active WI-0031 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v2.4.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

It’s agreed in TS-0001 that the behaviour of the group hosting CSE when aggregating member responses pertaining to a fan out request is subject to the response type, result expiration time and result persistence parameter. The parameters could guide the group hosting CSE when aggregated responses should be sent and whether or not the following member responses should be aggregated or discarded.

The proposed contribution is to add the stage 3 support for such feature.

### -----------------------Start of change 1-------------------------------------------

##### 7.4.14.2.5	Aggregation of member responses

After receiving the member responses from the member hosting CSE, the group hosting CSE shall respond the Originator with the aggregated response once all member responses has been received by the group hosting CSE. Otherwise if Response Type, Result Expiration Time or Result Persistence is set in the request, the group hosting CSE shall respond following the indication from the parameters.

If Response Type is set to blockingRequest, the group hosting CSE shall respond only once with the aggregated response before the time indicated in the Result Expiration Time reaches. The group hosting CSE shall discard the member responses received afterwards.

If Response Type is set to nonBlockingRequestSynch, after locally create the <request> resource, the group hosting CSE shall include the aggregated response in the operationResult and set the requestStatus of the <request> resource to TRUE before the Result Expiration Time  expires. The group hosting CSE shall then continue aggregating the member responses received after the Result Expiration Time within the Result Persistence and update the operationResult correspondingly.

If Response Type is set to nonBlockingRequestAsynch, the group hosting CSE shall notify the Originator with the aggregated response before the Result Expiration Time expires. The group hosting CSE shall then continue aggregating the member response received after the Result Expiration Time within the Result Persistence and notify the Originator with the aggregated response which contains member responses that have not been delivered to the Originator.

If Response Type is set to flexBlocking, the group hosting CSE shall keep aggregating the member responses until Result Expiration Time. If all member responses are received, the group hosting CSE shall respond the request with the aggregated response. If only part of the member responses are received , the group hosting CSE shall locally create a <request> resource from the received request, and response to the Originator with the reference to the created <request> resource as well as the currently aggregated responses. Then within Result Persistence, the group hosting CSE shall keep aggregating the remaining member responses and update the aggregated response in the operationResult of the <request> resource. Or if notificationTarget is provided in the request, the group hosting CSE shall continue aggregate the remaining member response and notify the Originator with the aggregated response with the Result Persistence.

### If any of the parameter is missing from the request, the group hosting CSE shall determine by its local policy on the time to respond.-----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### <fanOutPoint> resource specific procedure on CRUD operations

##### Introduction

This sub-clause describes <fanOutPoint> resource specific behaviour for CRUD operations.

##### Create

A Create operation sent to a <fanOutPoint> is fanned out to the members (if any) of the parent <group>. It is equivalent to sending a Create to each member and therefore results in new resources being created as children of these existing members.

If the Create is sent to a hierarchical URI containing a fanOutPoint and an additional path relative to that fanOutPoint then the new resources are not created as immediate children of the members, rather they are created as children of descendents of those members (as determined by the relative path).

Originator:

Primitive specific operation after Orig-1.0 "Compose Request primitive" and before Orig-2.0 "Send the Request to the receiver CSE": In the case the Originator wants to subscribe to all the member resources of the group and the originator wants the group hosting CSE to aggregate all the notifications come from its member hosting CSEs, the Originator shall include notificationForwardingURI attribute in the <subscription> resource.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator".

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent <group> resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent <group> resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Validate the type of resource to be created, refer to clause 7.4.14.2.1.

Sub-group creation for members residing on the same CSE, refer to clause 7.4.14.2.2.

Assign URI for aggregation of notification, refer to clause 7.4.14.2.3.

Fanout Request to each member, refer to clause 7.4.14.2.4.

Aggregation of member responses, refer to clause 7.4.14.2.5.

##### Retrieve

Originator:

No primitive specific operations.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator".

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6 "Announce/De-announce the resource" in the generic procedure:

- Sub-group creation for members residing on the same CSE, refer to 7.4.14.2.2.

- Fanout Request to each member, refer to 7.4.14.2.4.

3)	Aggregation of member responses, refer to clause 7.4.14.2.5.

##### Update

Originator:

No primitive specific operations.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator".

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Sub-group creation for members residing on the same CSE , refer to 7.4.14.2.2.

- Fanout Request to each member. See Clause 7.4.14.2.4.

- Aggregation of member responses, refer to clause 7.4.14.2.5.

##### Delete

The primitive deletes the member resources and their child resources belonging to an existing <group> resource.

Originator:

No primitive specific operations.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and Recv-6.3 "Check authorization of the Originator": The To parameter consists of the URI of the group resource plus a suffix consisting of /fanOutPoint or /fanOutPoint/plus any additional appended relative address.

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Sub-group creation for members residing on the same CSE , refer to 7.4.14.2.2

- Fanout Request to each member. See Clause 7.4.14.2.4

- Aggregation of member responses, refer to clause 7.4.14.2.5.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?