| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23.0 |
| Source:* | KETI |
| Date:* | 2016-05-13 |
| Contact:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.kr Sungchan Choi, KETI, csc@keti.re.kr Jaeho Kim, KETI, jhkim@keti.re.kr |
| Reason for Change/s:* | Loss of generality of xs:list type elements between XML and JSON serialization |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v1.7.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution introduces a issue regarding the mapping of elements defined as xs:list type between XML and JSON serialization. Elements defined as xs:list type in XSD are represented in XML serialization as a string where any two values next to each other are separated with a single namespace, while it is represented in JSON as an array where values are enclosed in a square brackets ([]). These definitions are loss of generality which may result in parsing problems from XML to JSON serialization in implementation perspective.

In current oneM2M specification, an element that is defined as having an xs:list type in the corresponding XSD is represented as a string with a single space to separate different value for containing array type data. For example, for labels attribute,  it is used in this way: <labels>VALUE_1 VALUE_2 VALUE_3</labels>. However, standard XML represents array type data as a list, taking labels attribute as an example, it would look like this:

<labels>VALUE_1</labels>

<labels>VALUE_2</labels>

<labels>VALUE_3</labels>.

But this list representation of <lables> is currently not defined in oneM2M specification as below: <labels>VALUE_1</labels>

<labels>VALUE_2</labels>

<labels>VALUE_3</labels>.

In addition, oneM2M specification defines that if an element is defined as having an xs:list type in the corresponding XSD then it is serialized in the JSON member as an array. If that is the case, the labels attribute in JSON is represented as “labels”: [“VALUE_1”, “VALUE_2”, “VALUE_3”].

Attribute labels is defined as XSD type of m2m:labels, which is a list of value defined as XSD type of xs:token. The base type of token is normalizedStrings whose base type is string.

| Taking attribute accessControlOriginators as another example, attribute accessControlOriginators is defined as a list of xs:anyURI, whose value can be absolute or relative, and may have an optional fragment identifier (i.e. it may be an IRI Reference), as defined in TS-0004 specification. The values of attribute accessControlOriginators are represented as in XML serialization, for example, <acr><acor>/in-cse/cae123 /in-cse/mn-cse/cae345</acor><acop>63</acop></acr>, where a namespace is used to separate two different string value next to each other, while represented as in JSON serialization, for example, “acr”: { “acor”: [”/in-cse/cae123”, “/in-cse/mn-cse/cae345”], “acop”:63}. |  |  |  |  |
| --- | --- | --- | --- | --- |

### -----------------------Start of change--------------------------------------------------------

## JSON serialization

### Method

The structure of the top-level primitive object shall be determined by the data type definitions in clause 6 and clause 7 of the present document, as follows:

- If an element is defined as having an xs:list type in the corresponding XSD then it is serialized in the JSON member as an normalizedString.

Table 6.3.2 1: Data Types incorporated from XML Schema

| xs:normalizedString | normalizedString represents white space normalized strings. The ·value space· of normalizedString is the set of strings that do not contain the carriage return (#xD), line feed (#xA) nor tab (#x9) characters. The lexical space· of normalizedString is the set of strings that do not contain the carriage return (#xD), line feed (#xA) nor tab (#x9) characters. The base type of normalizedString is string. |
| --- | --- |

-----------------------End of change------------------------------------------------------------

Following issues we encountered in 2nd OneM2M Interoperability Event, we request to oneM2M PRO WG to clarify the representation of data defined as xs:list type.

- Element defined as a xs:list complex type contains members, e.g. accessControlRule,

- Element defined as a xs:list type contains members defined as xs:list, e.g. accessControlOriginator

|  | XML | JSON |
| --- | --- | --- |
|  | Representation of Value | oneM2M Definition status | Representation of value mapped from XML |
|  |  |  | Option-1 | Status | Option-2 | Status |
| labels | <labels>VALUE_1 VALUE_2 VALUE_3</labels> | Defined | “labels”: “VALUE_1 VALUE_2 “VALUE_3” | Not defined |  |  |
|  | <labels>VALUE_1</labels> <labels>VALUE_2</labels> <labels>VALUE_3</labels> | Not Defined | “labels”: [“VALUE_1”, “VALUE_2”, “VALUE_3”] | Defined |  |  |
|  | <labels>VALUE_1</labels> | Not Defined | “labels”: [“VALUE_1”] | Not Clear | “labels”: “VALUE_1” | Not Clear |
| privileges | <accessControlRule> <accessControlOriginator> /in-cse/cae123 /in-cse/mn-cse/cae345 </accessControlOriginator> <accessControlOperation>63 </accessControlOperation> </accessControlRule> | Defined | “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae123”, “/in-cse/mn-cse/cae345” ], “accessControlOperation”:63 }] | Defined | “accessControlRule”: [{ “accessControlOriginator”: ”/in-cse/cae123 /in-cse/mn-cse/cae345”, “accessControlOperation”:63 }] | Not Defined |
| accessControlPolicy | <privileges> <accessControlRule> <accessControlOriginator> /in-cse/cae123 /in-cse/mn-cse/cae345 </accessControlOriginator> <accessControlOperation>63 </accessControlOperation> </accessControlRule> <accessControlRule> <accessControlOriginator> /in-cse/cae456 /in-cse/mn-cse/cae789 </accessControlOriginator> <accessControlOperation>63 </accessControlOperation> </accessControlRule> </privileges> <selfPrivileges> <accessControlRule> <accessControlOriginator> /in-cse/cae123 /in-cse/mn-cse/cae345 </accessControlOriginator> <accessControlOperation>63 </accessControlOperation> </accessControlRule> <accessControlRule> <accessControlOriginator> /in-cse/cae456 /in-cse/mn-cse/cae789 </accessControlOriginator> <accessControlOperation>63</accessControlOperation> </accessControlRule> </selfPrivileges> | Defined | “privileges”: { “accessControlRule”:[{ “accessControlOriginator”: [ ”/in-cse/cae123”, “/in-cse/mn-cse/cae345” ],“accessControlOperation”:63 }], “accessControlRule”:[{ “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:63 }] }, “selfPrivileges”: { “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:63 }] , “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:63 }] } | Defined | “privileges”: { “accessControlRule”:[{ “accessControlOriginator”: [ ”/in-cse/cae123”, “/in-cse/mn-cse/cae345” ],“accessControlOperation”:63 }, { “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:63 }] }, “selfPrivileges”: { “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:63 }, { “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:63 }] } |  |