| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com |
| Date:* | 2016-05-15 |
| Contact:* | As above |
| Reason for Change/s:* | Data format for Role-ID and Token-ID |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0019 Dynamic Authorization MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 and 2.5.0 |
| Clauses/Sub Clauses* | 6.3.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This is a draft version of TS-0004 CR which adds definitions of m2m:roleID and m2m:tokenID.

### Add the following rows to Table 6.3.3-1

### -----------------------Start of change 1 (clause 6.3.3)---------------

| m2m:roleID | Role-ID | 1234abcd@role-issuer.com | An xs:NCName (the issuerRelativeID) and an FQDN (the issuerID) separated by the ‘@’ character |
| --- | --- | --- | --- |
| m2m:tokenID | Token-ID | 1234abcd@token-issuer.com | An xs:NCName (the issuerRelativeID) and an FQDN (the issuerID) separated by the ‘@’ character |

### -----------------------End of change 1 (clause 6.3.3)---------------