| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23.1 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Nobuyuki Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Date:* | 2016-06-01 |
| Contact:* | As above |
| Reason for Change/s:* | This CR specifies how the End-to-End Security of Primitives (ESPrim) feature uses the NOTIFY to exchange ESPrim Objects. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 End-to-End Security and Group Authentication MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 and 2.5.0 |
| Clauses/Sub Clauses* | New clause 7.5.1.2.x “Notification for End-to-End Security of Primitives (ESPrim)” New clause 7.6 “Security Procedures”, new sub-clause 7.6.x “Procedure for applying End-to-End Security of Primitives (ESPrim)” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR specifies how the End-to-End Security of Primitives (ESPrim) feature uses the NOTIFY to exchange ESPrim objects with a Receiver.

R01: sequence of events is shown with a single table

R02: sequence of steps is shown with 3 tables, one table for each communication mode: blockingRequest, nonBlockingRequestSynch and nonBlockingRequestAsynch. Also separated the columns for each procedure (inner primitive steps, ESData process steps and outer process steps) into a column for Originator steps and a column for Receiver steps.

R03:

- Re-arranging of where text will be locaeted

  - Created a new clause 7.6 “Security Procedures”.

  - Moved ESPrim details into a sub-clause7.6.x “Procedure for applying End-to-End Security of Primitives (ESPrim)”.

NOTE: 	Clause 7.6 could include details needed for other security procedures. The author is discussing this with other SEC WG4 members.

  - Clause 7.5.1.2.x “Notification for transport of ESPrim Objects” now comprises references to steps of 7.6.x.

- Changes to details now in clause 7.6.x

  - Replaced tables with a single figure. The basic flow is unchanged, but ignores all details which are independent of ESPrim.

  - The Receiver has also been separated into Hosting CSE (receiving the outer request to its <CSEBase> or an <AE> resource) and the Target of the inner request (which may be the Hosting CSE or an AE registered to the Hosting CSE).

- References to step numbers are highlighted with pink background to ensure they are easily identified and double checked for agreement of the CR.

### -----------------------Start of change 1 ---------------

##### 7.5.1.2.x Notification for transport of ESPrim Objects

Notification is used for transport of ESPrim Objects protecting an exchange of inner primitives, as part of 7.6.x “Procedure for applying End-to-End Security of Primitives (ESPrim)”.

NOTE 1:	The inner request primitive can request any operation (Create, Retrieve, Update, Delete, Notify) allowed by the resource addressed by the inner request primitive. The  composing or processing of the inner request primitive and  the corresponding inner response primitive follows the general procedures in clause 7.2.2, and is not addressed further in the present clause.

Originator:

When the originator is to secure an exchange of inner primitives, then the Receiver shall apply the following steps in order:

- Encrypt the inner request primitive to form an ESPrim Object as described in step E of clause 7.6.x.

- Form the Notify request from the ESPrim Object as described in step F of clause 7.6.x.

- Deliver the Notify request to the Receiver as described in step G and H of clause 7.6.x.

Receiver:

When a Receiver receives a notification request transporting an ESPrim Object, then the Receiver shall apply the following steps in order:

- Process the Notify request to extract the ESPrim Object as described in step I of clause 7.6.x.

- Decrypt the ESPrim Object to form the inner request primitive as described in step J of clause 7.6.x.

- The inner request primitive is processed, resulting in an inner response primitive. See Note 1.

- Encrypt the inner response primitive to form an ESPrim Object as described in step L of clause 7.6.x.

- Form a successful Notify response as described in step M of clause 7.6.x.

- Deliver the Notify request to the Originator as described in step N of clause 7.6.x.

Originator:

When the Originator receives a notification response transporting an ESPrim Object, then the Receiver shall perform the following steps in order:

- Process the Notify request to extract the ESPrim Object as described in step O of clause 7.6.x.

- Decrypt the ESPrim Object to form the inner request primitive as described in step P of clause 7.6.x.

- The inner response primitive is processed. See Note 1.

Error cases are addressed in clause 7.6.x.

### -----------------------End of change 1 ---------------

### -----------------------Start of change 2 ---------------

## 7.6	Security Procedures

### 7.6.1	Introduction

oneM2M TS-0003 [7] specifies a range of security procedures. Clause 7.6 describes how to use the security procedures as part of the general procedures, common operations, resource type-specific procedures and primitive-specific procedures. The following security procedures are described:

- End-to-End security of primitives (ESPrim): securing a primitive so that CSEs (forwarding the primitive) do not need to be trusted with the confidentiality and integrity of the primitive.

Editor’s note: this list should be updated when new procedures are added.

### -----------------------End of change 2 ---------------

### ----------------------- Start of change 3---------------

### 7.6.x Procedure for applying End-to-End Security of Primitives (ESPrim)

End-to-End Security of Primitives (ESPrim) provides an interoperable framework for securing oneM2M primitives so CSEs (forwarding the primitive) do not need to be trusted with the confidentiality and integrity of the primitive. ESPrim provides mutual authentication, confidentiality, integrity protection and a freshness guarantee (bounding the age of ESPrims). Credential management aspects and data protection aspects for ESPrim are specified in oneM2M TS-0003 [7]. Architecture-level-details for the transport of ESPrim are specified in oneM2M TS-0001[6].

The primitive to be secured is called the inner primitive. All operations (Create, Retrieve, Update, Delete, or Notify) are allowed for an inner request primitive and inner response primitive. The inner primitives are encrypted to form an ESPrim Object. A Notify Request and corresponding Notify Response primitives (called the outer request primitive and outer response primitive) are used to transport the ESPrim Objects containing this encrypted inner request primitive and inner response primitive respectively.

There are three parallel procedures which must be considered when using ESPrim to protect primitives:

- Inner primitive processing: The general procedure for the inner request primitive and corresponding inner response primitive.

- ESPrim processing: Encrypting inner primitives to form ESPrim objects, and decrypting ESPrim objects to obtain the inner primitives.

- Outer primitive processing: The general procedure for the outer request primitive and corresponding outer response primitive used to transport the ESPrim objects.

There are three actors impacted:

- Originator: The CSE or AE which originates the inner primitive procedure, the ESPrim protocol and the outer Notify primitive procedure.

- Hosting CSE: The Hosting CSE from the perspective of the outer primitive procedure, hosting the <CSEBase> or <AE> resource of the Target.

- Target CSE or AE: The CSE or AE terminating the ESPrim protocol and inner primitive procedure. The Target shall be either the Hosting CSE or an AE registered to the Hosting CSE. The Target also applies some processing of the outer primitive procedure: extracting the ESPrim objects form the outer request primitives, and composing the outer response primitives.

Other Receiver CSEs on the delivery path (apart from the Originator and Hosting CSE) process and forward the outer Notify primitives according to the general procedure in clause 7.2.2.2. These Receiver CSEs do not process the ESPrim Objects nor the inner primitives. The procedures for these Receiver CSEs are not affected when ESPrim is being used.

The present clause describes the relationship between the steps of the general procedures applied to the inner primitives, the ESPrim processing and the general procedures applied to the outer primitives. The description assumes that the Originator and Target have established a pairwiseESPrimKey and steps have been performed for establishing a sessionESPrimKey at the Originator (phases A and B in clause 8.4.2 of oneM2M TS-0003 [7]).

Figure 7.5.1.2.x-1 and the following text describe the procedure for applying ESPrim to protect an exchange of inner primitives.

Figure 7.6.x-1: Procedure for applying End-to-End Security of Primitives (ESPrim) to protect an exchange of inner primitives

Originator:

- The Originator’s inner primitive processing shall apply Orig-1.0 “Compose of a Request primitive” to compose the inner request primitive. The inner request should not include the delivery-related parameters Response Type, Event Category, and Delivery Aggregation.

NOTE 1:	Delivery-related parameters Response Type, Event Category, and Delivery Aggregation in the inner request (composed at step A) will be ignored – see step K. When appropriate, these parameters are provided in the outer request primitive only (composed at step F).

- The Originator shall not apply Orig-2.0 "Send a Request primitive to the Receiver CSE", but instead shall pass the inner request primitive to the Originator’s ESPrim processing for further processing in Step E.

- The Originator’s inner primitive processing shall apply Orig-3.0 "Check Response Type". The Response Type is blockingRequest, see step A.

- The Originator’s inner primitive processing shall apply Orig-4.0 “Wait for Response primitive”, entering a waiting state until the inner response primitive is received (at step P).

- The Originator’s ESPrim processing shall apply ESPrim encryption to the inner request primitive, resulting in an ESPrim Object. The ESPrim encryption process is specified in oneM2M TS-0003 [7]. The ESPrim Object is passed to the Originator’s outer primitive processing. The Originator’s ESPrim processing enters waiting state until the corresponding ESPrim Object is received (at step O)

- The Originator’s outer primitive processing shall apply Orig-1.0 “Compose of a Request primitive” to compose the outer request primitive. The outer request primitive shall include the following parameters:

- Operation: Notify (N)

- To: 		An address of the <CSEBase> or <AE> resource associated with the Target.

- From: 	An address of the Originator.

- Request Identifier: may be independent of the Request Identifier in the inner request primitive.

- Content: a notification data containing a securityInfo element with child elements

  - securityInfoType:	“5” (ESPrim Object).

  - esprimObject:			the ESPrim Object generated at step E.

The outer request primitive may include further optional parameters as described in clause 11.4.2 of TS-0001 [6], including the delivery-related parameters Response Type, Event Category, and Delivery Aggregation.

- The general procedures in clause 7.2.2.1 and clause 7.2.2.2 are followed for delivering the outer Notify request primitive from the Originator to the Hosting CSE of the addressed resource, in accordance with the communication mode of the outer request primitive. The outer Notify request primitive may be forwarded by one or more transit CSEs, which are not shown in Figure 7.6.x-1.  The Originator’s outer primitive processing enters a waiting state until the corresponding outer response primitive is received (at step N). The details of the delivery to and from the Hosting CSE have no impact on any other steps.  The present step includes all Receiver steps in clause 7.2.2.2 up to Recv-6.4. If any errors are encountered during this step, then the Notify request primitive is rejected with a Response Status Code indicating the appropriate error code.

Hosting CSE:

- The Hosting CSE’s outer primitive processing applies Recv-6.5 “Create/Update/Retrieve/Delete/Notify operation is performed” to the outer Notify request primitive. This triggers "Notify re-targeting” (clause 7.3.3.9), and the Hosting CSE passes the outer request primitive to the Target identified by the To parameter:

- If the To parameter is an address for the Hosting CSE’s <CSEBase> resource, then the Target is the Hosting CSE.

- If the To parameter is an address for an <AE> resource, then the Target is the associated AE.

If any errors are encountered during this step, then the Notify request primitive is rejected with a Response Status Code indicating the appropriate error code. The Hosting CSE’s outer request processing enters waiting state until the corresponding outer response primitive is received at step M.

Target:

- The Target’s outer primitive processing shall examine the securityInfoType element of the securityInfo element of the notification data in the Content parameter of the outer Notify request primitive.  The value “5” of the securityInfoType indicates that the securityInfo element contains an ESPrim object. The Target shall extract the ESPrim Object contained in the esprimObject element of the securityInfo element and pass the ESPrim Object to the Target’s ESPrim processing.

- The Target’s ESPrim processing shall apply ESPrim decryption to the ESPrim Object, resulting in the verified inner request primitive. The ESPrim decryption process is specified in oneM2M TS-0003 [7].

- If the ESPrim processing fails to complete, then a Response Status Code indicating "ESPRIM_DECRYPTION_ERROR" error is returned to the Hosting CSE’s outer primitive processing, and the call flow skips to step M.

- If the ESPrim integrity verification fails, then a Response Status Code indicating "BAD_REQUEST" error is returned to the Hosting CSE’s outer primitive processing, and the call flow skips to step M.

- If decryption is successful, then the verified inner request primitive is passed to the Target’s inner primitive processing, and the Target’s ESPrim processing enters waiting state until the corresponding inner response primitive processing Object is received (at step M).

- The Target shall process the verified inner request primitive according to the general procedure for Receiver, see clause 7.2.2.2.

- The Target shall ignore delivery-related parameters in the inner primitive, such as the Response Type, Event Category, or Delivery Aggregation. See Note 1.

An inner response primitive is returned to the Target’s ESPrim processing.

NOTE 2: 	This call flow does not distinguish between successful and unsuccessful inner response primitives. Both will have ESPrim encryption applied prior to delivery back to the Originator.

- The Target’s ESPrim processing shall apply ESPrim encryption to the inner response primitive, resulting in an ESPrim Object. The ESPrim encryption process is specified in oneM2M TS-0003 [7]. If the ESPrim processing fails to complete, then a Response Status Code indicating "ESPRIM_ENCRYPTION_ERROR" error is returned to the Hosting CSE’s outer primitive processing. If the ESPrim processing is successful, then the ESPrim Object is passed to the Hosting Target’s outer primitive processing.

- If the Target’s ESPrim processing returned a Response Status Code indicating an error, then the   Hosting CSE’s outer primitive processing forms an error Notify response as described in clause 7.3.3.13. If the Target’s ESPrim processing returned an ESPrim Object, then the Target’s outer primitive processing forms a successful Notify Response as described in clause 7.3.3.12, with the Content containing a securityInfo element with the following child elements:

  - securityInfoType:	“5” (ESPrim Object).

  - esprimObject:			the ESPrim Object received from the Target’s ESPrim processing.

The outer response primitive is passed to the Hosting CSE’s outer primitive processing.

Hosting CSE:

- The general procedures in clauses, 7.2.2.1 and 7.2.2.2 are followed for delivering the outer response primitive from the Hosting CSE to the Originator, in accordance with the communication mode of the outer response primitive. The outer Notify response primitive may be forwarded by one or more transit CSEs, which are not shown in Figure 7.6.x-1.

Originator:

- The Originator’s outer primitive processing shall apply Orig-6.0 “Process Response primitive” to the outer response primitive, extracting the ESPrim Object and forwarding this to the Originator’s ESPrim processing.

- The Originator’s ESPrim processing shall apply ESPrim decryption to the ESPrim Object, resulting in the verified inner response primitive. The ESPrim decryption process is specified in oneM2M TS-0003 [7]. If decryption is successful, then the verified inner response primitive is passed to the Originator’s inner primitive processing.

- The Originator’s inner primitive processing shall apply Orig-6.0 “Process Response primitive” to the verified inner response primitive.

### ----------------------- End of change 3 -------------