| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23.2 |
| Source:* | KETI |
| Date:* | 2016-06-08 |
| Contact:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.kr Sungchan Choi, KETI, csc@keti.re.kr Jaeho Kim, KETI, jhkim@keti.re.kr |
| Reason for Change/s:* | Loss of generality of xs:list type elements between XML and JSON serialization |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v1.7.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution introduces a issue regarding the mapping of elements defined as xs:list type between XML and JSON serialization. Elements defined as xs:list type in XSD are represented in XML serialization as a string where any two values next to each other are separated with a single space, while it is represented in JSON as an array where values are enclosed in a square brackets ([]).

In current oneM2M specification, an element that is defined as having an xs:list type in the corresponding XSD is represented as a string with a single space to separate different value for containing array type data. Taking labels attribute as an example,  it is represented as

<labels>VALUE_1 VALUE_2 VALUE_3</labels>.

However, standard XML represents array type data as a list which is not clearly defined in oneM2M specification, it represents labels attribute as:

<labels>VALUE_1</labels>

<labels>VALUE_2</labels>.

| In addition, oneM2M specification defines that if an element is defined as having an xs:list type in the corresponding XSD then it is serialized in the JSON member as an array. If that is the case, the labels attribute in JSON can be represented as “labels”: [“VALUE_1”, “VALUE_2”, “VALUE_3”]. |  |  |  |
| --- | --- | --- | --- |

The below table summarizes definitions from standard XML, JSON, and oneM2M specification (TS-0004).

|  | Standard XML | oneM2M XML Serialization | oneM2M JSON Serialization |
| --- | --- | --- | --- |
| Specification for xs: list | a sequence of elements encloded in an angle brackets(<>), e.g. <labels>VALUE_1</labels> <labels>VALUE_2</labels> | an unbounded list of strings of any length separated by a space, e.g. <labels>VALUE_1 VALUE_2</labels> | Array of list strings enclosed in a square brackets ([]), e.g. “labels”: [“VALUE_1”, “VALUE_2”] |

For an oneM2M implementation e.g. an IN-CSE, which supports only JSON serialization, the IN-CSE has to handle the convertion from JSON to XML when IN-CSE receives requests represented in XML (e.g. HTTP POST request) and is requested to get response in XML serialization, and vice versa.

During the 2nd oneM2M interoperability event, we found that different oneM2M implementations especially IN-CSE or ASN-CSE have different representation on the xs:list type attributes in request/response and they have different rules to parse the received request either in XML or JSON representation. The different representation and different parsing rules for the xs:list type attributes are thought the main reason that caused the parsing failure of interoperability tests.

Based on these ambiguity issues, we think there is great need to clearly specify the xs:list type attributes including examples to be present in Annex section of TS-0004 so that all oneM2M implementations are able to follow a consistent representation rule for xs:list type attributes, and handling procedures for those request/response that are not represented in correct way as defined in oneM2M XML/JSON serialization, e.g. reject the requests or respond with error message etc. We propose to add examples for xs:list type attributes in XML and JSON serialization, specifically in Annex L in TS-0004.

### -----------------------Start of change----------------------------------------------------

Annext L (informative): Examples for list type attributes in XML and JSON serialization

The representation of xs:list type attributes are clarified into three categories:

- Element defined as a complex xs:list type contains sub-elements with specific data type, e.g. accessControlRule which contains a xs:list type element accessControlOriginator, should be represented as a sequence of elements in XML serialization and as an array of elements in JSON serialization, respectively, e.g.

(XML serialization)

…

<accessControlRule>

<accessControlOriginator>/in-cse/cae123 /in-cse/mn-cse/cae345</accessControlOriginator>

<accessControlOperation>63</accessControlOperation>

</accessControlRule>

<accessControlRule>

<accessControlOriginator>/in-cse/cae456 /in-cse/mn-cse/cae789</accessControlOriginator>

<accessControlOperation>63</accessControlOperation>

</accessControlRule>

…

Or (JSON serialization)

...

“accessControlRule”: [

{

“accessControlOriginator”: [”/in-cse/cae123”, “/in-cse/mn-cse/cae345”],

“accessControlOperation”:[63]

},

{

“accessControlOriginator”: [”/in-cse/cae456”, “/in-cse/mn-cse/cae789”],

“accessControlOperation”:[63]

}]

…

- Element defined as a xs:list type containing a list of string values, e.g. accessControlOriginator includes a list of URIs, should be represented in an unbounded list of strings separated by a space and as an array of elements in JSON serialization, respectively, e.g.

(XML serialization)

…

<accessControlOriginator>/in-cse/cae123 /in-cse/mn-cse/cae345</accessControlOriginator>

…

Or (JSON serialization)

…

“accessControlOriginator”: [”/in-cse/cae123”, “/in-cse/mn-cse/cae345”]

…

- Element defined as a xs:list type containing a single value should be represented as a string, and as an array of elements in JSON serialization, respectively, e.g.

- (XML serialization)

- …

- <labels>VALUE_1</labels>

- …

- Or (JSON serialization)

- ...

- “labels”:[“VALUE_1”]

...

|  | XML | JSON | Status in oneM2M Specification |
| --- | --- | --- | --- |
|  | Representation of xs:list type attributes | Status in oneM2M Specification | Representation of mapping from XML |  |
|  |  |  | Option-1 | Status | Option-2 |  |
| labels | <labels>VALUE_1 VALUE_2 VALUE_3</labels> | Defined | N/A | N/A | “labels”: “VALUE_1 VALUE_2 “VALUE_3” |  |
|  | <labels>VALUE_1</labels> <labels>VALUE_2</labels> <labels>VALUE_3</labels> |  | “labels”: [“VALUE_1”, “VALUE_2”, “VALUE_3”] | Defined | N/A | N/A |
|  | <labels>VALUE_1</labels> |  | “labels”: [“VALUE_1”] | Defined | “labels”: “VALUE_1” |  |
|  | <labels>[“VALUE_1”, “VALUE_2”, “VALUE_3”]</labels> |  | N/A | N/A | N/A | N/A |
| accessControlOperations | <accessControlRule> <accessControlOriginator> /in-cse/cae123 /in-cse/cae234 /in-cse/mn-cse/cae345 </accessControlOriginator> <accessControlOperation> 2 31 63 </accessControlOperation></accessControlRule> |  | { “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae123”, “/in-cse/cae234”, “/in-cse/mn-cse/cae345” ],“accessControlOperation”:[2, 31,63] }] } | Defined(mapping Enumeration to integer instead of string) | { “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae123”, “/in-cse/cae234”, “/in-cse/mn-cse/cae345” ],“accessControlOperation”:[“2”, “31”,”63”] }] } |  |
| memberType | <group> <memberType>2 3 4</memberType> <memberIDs>/mn-cse/cnt-582759912 /mn-cse/cnt-582769893</memberIDs> <maxNrOfMembers>20</maxNrOfMembers> </group> |  | { “group”:{ “memberType”:[2, 3, 4], “memberIDs”:[ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789”, ”/in-cse/cae456/cnt102”], “maxNrOfMembers”: [20] } } | Defined | { “group”:{ “memberType”:[“2”, “3”, “4”], “memberIDs”:[ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789”, ”/in-cse/cae456/cnt102”], “maxNrOfMembers”: [“20”] } } |  |
| notificationEventType | <eventNotificationCriteria> <notificationEventType>1 2 </notificationEventType> </eventNotificationCriteria> |  | { “eventNotificationCriteria”: { “notificationEventType”:[1, 2] }, “notificationURI”:”/ mn-cse/ae-CAE340304071” } | Defined | { “eventNotificationCriteria”: { “notificationEventType”:[“1”, “2”] }, “notificationURI”:”/ mn-cse/ae-CAE340304071” } |  |
| accessControlPolicy | <privileges> <accessControlRule> <accessControlOriginator> /in-cse/cae123 /in-cse/mn-cse/cae345 </accessControlOriginator> <accessControlOperation>63 </accessControlOperation> </accessControlRule> <accessControlRule> <accessControlOriginator> /in-cse/cae456 /in-cse/mn-cse/cae789 </accessControlOriginator> <accessControlOperation>63 </accessControlOperation> </accessControlRule> </privileges> <selfPrivileges> <accessControlRule> <accessControlOriginator> /in-cse/cae123 /in-cse/mn-cse/cae345 </accessControlOriginator> <accessControlOperation>63 </accessControlOperation> </accessControlRule> <accessControlRule> <accessControlOriginator> /in-cse/cae456 /in-cse/mn-cse/cae789 </accessControlOriginator> <accessControlOperation>63</accessControlOperation> </accessControlRule> </selfPrivileges> | Defined | “privileges”: { “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae123”, “/in-cse/mn-cse/cae345” ],“accessControlOperation”:[63] }, { “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:[63] }] }, “selfPrivileges”: { “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae123”, “/in-cse/mn-cse/cae345” ],“accessControlOperation”:[63] }, { “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:[63] }] } | Defined | “privileges”: { “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae123”, “/in-cse/mn-cse/cae345” ],“accessControlOperation”:[63] }], “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:[63] }] }, “selfPrivileges”: { “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae123”, “/in-cse/mn-cse/cae345” ],“accessControlOperation”:[63] }], “accessControlRule”: [{ “accessControlOriginator”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ],“accessControlOperation”:[63] }] } |  |
| eventNotificationCriteria | <eventNotificationCriteria> <notificationContentType>1 2 4</notificationContentType> s<creator>20160519T090000</creator> </eventNotificationCriteria> |  | { "eventNotificationCriteria": [{"notificationContentType": [1, 2, 4], "cra": "20160519T090000" }] } | Defined | { "eventNotificationCriteria": {"notificationContentType": [1, 2, 4], "cra": "20160519T090000" } } |  |
|  | <eventNotificationCriteria> <notificationContentType>1 2 </notificationContentType> <creator>20160519T090000</creator> </eventNotificationCriteria> <eventNotificationCriteria> <notificationContentType>4</notificationContentType> <creator>20160519T091000</creator> </eventNotificationCriteria> |  | { "eventNotificationCriteria": [{"notificationContentType": [1, 2], "cra": "20160519T090000" }, { "notificationContentType": [4], "cra": "20160519T091000" }] } | Defined | { "eventNotificationCriteria": [{ “notificationContentType": [1, 2], "cra": "20160519T090000" }], [{ "notificationContentType": [4], "cra": "20160519T091000" }] } |  |

*Defined: indicates effective representations to xs:list type attributes, i.e.all oneM2M implementations should follow the defined representations for xs:list type attributes.

When receiving attributes defined as xs:list type with representation that are not defined in oneM2M TS-0004, the hosting CSE should reject the request and respond with a specific error message, e.g. “Ineffective request representation”.

-----------------------End of change---------------------------------------------------------------------------------------------------------