| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23.5 |
| Source:* | KETI |
| Date:* | 2016-06-29 |
| Contact:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.kr SeungMyeong Jeong, sm.jeong@keti.re.kr Sungchan Choi, KETI, csc@keti.re.kr Jaeho Kim, KETI, jhkim@keti.re.kr |
| Reason for Change/s:* | Adding examples resource and attribute representation in XML and JSON into TS-0004 Annex |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v1.7.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

We propose to add an Annex Y in TS-0004 to include examples for resources and attributes including list typed ones represented in XML and JSON, respectively. Those examples would help oneM2M implementation developers to understand deeply the representation of oneM2M resources and attributes.

## -----------------------Start of change 1--------------------------------------------

Annex Y (informative): Examples for list type attributes in XML and JSON serialization

Rules defined in TS-0004 for attribute data type and multiplicity are shown as below:

Table 1 Rules for attributes

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| accessControlRules | m2m:accessControlRule | 0..n | minOccurs="0" maxOccurs="unbounde" |
| accessControlRules | accessControlOriginators | list of xs:anyURI | 1 |  |
|  | accessControlOperations | m2m:accessControlOperations | 1 |  |
| labels | m2m:labels | 0..1 |  |
| memberType | m2m:memberType |  | minOccurs="0" |
| memberIDs | list of xs:anyURI |  | minOccurs="0" |
| maxNrOfMembers | xs:positiveInteger |  | minOccurs="0" |
| eventNotificationCriteria | m2m:eventNotificationCriteria |  | minOccurs="0" |
| eventNotificationCriteria | notificationEventType | m2m:notificationEventType | 0..4 | minOccurs="0" maxOccurs="4" |

Interpretations defined in TS-0004 for notificationEventType, accessControlOperations and memberType are listed as following:

Table 2 Interpretation of notificationEventType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Update_of_Resource | Default |
| 2 | Delete_of_Resource |  |
| 3 | Create_of_Direct_Child_Resource |  |
| 4 | Delete_of_Direct_Child_Resource |  |

Table 3 Interpretation of accessControlOperations

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | CREATE |  |
| 2 | RETRIEVE |  |
| 4 | UPDATE |  |
| 8 | DELETE |  |
| 16 | NOTIFY |  |
| 32 | DISCOVERY |  |

Table 4 Interpretation of memberType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | accessControlPolicy |  |
| 2 | AE |  |
| 3 | container |  |
| 4 | contentInstance |  |
| 5 | CSEBase |  |
| 6 | delivery |  |
| 7 | eventConfig |  |
| 8 | execInstance |  |
| 9 | group |  |
| 10 | locationPolicy |  |
| 11 | m2mServiceSubscription |  |
| 12 | mgmtCmd |  |
| 13 | mgmtObj |  |
| 14 | node |  |
| 15 | pollingChannel |  |
| 16 | remoteCSE |  |
| 17 | request |  |
| 18 | schedule |  |
| 19 | serviceSubscribedAppRule |  |
| 20 | serviceSubscribedNode |  |
| 21 | statsCollect |  |
| 22 | statsConfig |  |
| 23 | subscription |  |
| 10001 | accessControlPolicyAnnc |  |
| 10002 | AEAnnc |  |
| 10003 | containerAnnc |  |
| 10004 | contentInstanceAnnc |  |
| 10009 | groupAnnc |  |
| 10010 | locationPolicyAnnc |  |
| 10013 | mgmtObjAnnc |  |
| 10014 | nodeAnnc |  |
| 10016 | remoteCSEAnnc |  |
| 10018 | scheduleAnnc |  |
| 24 | mixed | A mixture of the resource types from 1 to 23, 10001 to 10004, 10009 to 10010, 10013 to 10014 and 10016 to 10018 as listed above. |

The representation of xs:list type attributes are clarified into three categories:

- Element defined as a complex xs:list type contains sub-elements with specific data type: e.g. accessControlRule contains a xs:list type element accessControlOriginators, is represented as a sequence of elements in XML serialization and as an array of elements in JSON serialization, respectively.

Representation in XML serialization:

…

<acr>

<acor>/in-cse/cae123 /in-cse/mn-cse/cae345</acor>

<acop>63</acop>

</acr>

<acr>

<acor>/in-cse/cae456 /in-cse/mn-cse/cae789</acor>

<acop>63</acop>

</acr>

…

Representation in JSON serialization:

…

[ “acr”:

{

“acor”: [”/in-cse/cae123”, “/in-cse/mn-cse/cae345”],

“acop”:63

},

“acr”:

{

“acor”: [”/in-cse/cae456”, “/in-cse/mn-cse/cae789”],

“acop”:63

}

]

…

- Element defined as a xs:list type containing a list of string values: is represented in an unbounded list of strings separated by a space and as an array of elements in JSON serialization, respectively.

Representation in XML serialization:

<acor>/in-cse/cae123 /in-cse/mn-cse/cae345</acor>

Representation in JSON serialization:

“acor”: [”/in-cse/cae123”, “/in-cse/mn-cse/cae345”]

- Element defined as a xs:list type containing a single value is represented as a string and as an array of elements in JSON serialization, respectively.

Representation in XML serialization:

<lbl>VALUE_1</lbl>

Representation in JSON serialization:

“lbl”:[“VALUE_1”]

Table 5 shows examples of resource and attributes including xs:list type attributes represented in XML and JSON, respectively.

Table 5 Attributes representation examples

|  | XML | JSON |
| --- | --- | --- |
|  | Representation of xs:list type attributes | Standard Definition Status | Representation of mapping from XML | Standard Definition Status |
| labels | <lbl>VALUE_1 VALUE_2 VALUE_3</lbl> | Defined | “lbl”: [“VALUE_1”, “VALUE_2”, “VALUE_3”] | Defined |
|  | <lbl>VALUE_1</lbl> <lbl>VALUE_2</lbl> <lbl>VALUE_3</lbl> | Not supported |  |  |
|  | <lbl>VALUE_1</lbl> | Defined | “lbl”: [“VALUE_1”] | Defined |
| memberType | <grp> <mt>0</mt> <mid> /in-cse/cae456 /in-cse/mn-cse/cae789 /in-cse/cae456/cnt102 </mid> <mnm>20</mnm> </grp> | Defined | { “grp”:{ “mt”:24, “mid”:[ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789”, ”/in-cse/cae456/cnt102”], “mnm”:20 } } | Defined |
|  | <grp> <mt>3</mt> <mid> /mn-cse/cnt-582759912 /mn-cse/cnt-582769893 </mid> <mnm>20</mnm> </grp> | Defined | { “grp”:{ “mt”:3, “mid”:[ ”/mn-cse/cnt-582759912”, “/mn-cse/cnt-582769893”], “mnm”:20 } } | Defined |
| accessControlPolicy | <pv> <acr> <acor> /in-cse/cae123 /in-cse/mn-cse/cae345 </acor> <acop>63</acop> </acr> <acr> <acor>/in-cse/cae456 /in-cse/mn-cse/cae789 </acor> <acop>63</acop> </acr> </pv> <pvs> <acr> <acor>/in-cse/cae123 /in-cse/mn-cse/cae345 </acor> <acop>63</acop> </acr> <acr> <acor>/in-cse/cae456 /in-cse/mn-cse/cae789 </acor> <acop>63</acop> </acr> </pvs> | Defined | “pv”: {[ “acr”: { “acor”: [ ”/in-cse/cae123”, “/in-cse/mn-cse/cae345” ], “acop”:63 }, “acr”: { “acor”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ], “acop”:63 } ]}, “pvs”: {[ “acr”: { “acor”: [ ”/in-cse/cae123”, “/in-cse/mn-cse/cae345” ], “acop”:63 }, “acr”: { “acor”: [ ”/in-cse/cae456”, “/in-cse/mn-cse/cae789” ], “acop”:63 } ]} | Defined |
| eventNotificationCriteria | <enc> <net>1</net> <net>3</net> <net>4</net> <cra>20160519T090000</cra> </enc> | Defined | { "enc":{[ "net”: 1, "net”: 3, "net”: 4], "cra": "20160519T090000"} } | Defined |
|  | <enc> <net>1 3 4</net> <cra>20160519T090000</cra> </enc> | Not Supported |  |  |

*Defined: indicates permitted representations for xs:list type attributes, i.e.all oneM2M implementations follow the defined representations for xs:list type attributes.

*Not Supported: indicated not permitted representations for xs:list type attributes.

When receiving a request containing attributes defined as xs:list type with representation that are not defined in oneM2M TS-0004, the hosting CSE will reject the request and respond with a specific error message, e.g. “Ineffective request representation”.

## -----------------------End of change 1-----------------------------------------------------------------------------------------