| Input Contribution |
| --- |
| Meeting ID* | PRO 22.0 |
| Title:* | sensor measure values content type |
| Source:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Uploaded Date:* | 2016-03-06 |
| Document(s) Impacted* | TS-0004 v.2.x. |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG3 members shall determined appropriate place to put proposed text in TS-0004. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

The content of <contentInstance> or <timeSeriesData> is left as implementation dependent.

But it is important to have standard way to share data measured by sensors on machie to machine communication.

This contribution to propose to define the content type which can be used to share measured and collected data from devices.

PRO-2016-0072 is provided for better understanding of this proposal.

R01: changed from Normative to Informative to be consistent with wordings.

The one of possible benefits can be use with content-based discovery. If the data is stored in same formats, the M2M Application can easily retrieve targeted data using QueryString  '$.sensingData[1].metric eq temperature'.

R02: As the result of offline discussion, the need to identify the source of data using some ID, and  to verify the integrity of the message level is identified, and the data format was extended to support it as optional field.

R03: provides reason to add this based on related requiments:

| OSR-037 | The oneM2M System shall enable an M2M Application to request to send data, in a manner independent of the Underlying Network, to the M2M Applications of a group of M2M Devices and M2M Gateways in geographic areas that are specified by the M2M Application. | Not implemented in Rel-1 |
| --- | --- | --- |
| OSR-089 | The oneM2M System shall enable the cancellation of continuous data collection and/or the deletion of collected data when pre-defined conditions are met. | Targeted for Release 2 |
| OSR-084 | The oneM2M System shall be able to handle an event notification from an authorized M2M Application which triggers actions to be performed on the M2M Device (ex. Turn on or off the monitoring). | Targeted for Release 2 |
| SER-023 | Where a Hardware Security Module (HSM) is supported, the oneM2M System shall be able torely on the HSM to provide local security. | Partly implemented in Rel-1 |

(Following texts are proposed to be added.)

R04: Add more explaination about how the proposed data type is used with <contentInstance> or <timeSeriesInstance> resource.

Annex x(Informative): 
General purpose representation of measured sensing data

x.1 Introduction

Present clause specifies the MIME content type which can be used to as the content attribute of the <contentInstance> or <timeSeriesInstace> resource.

x.2 oneM2M sensor measured data content type

x.2.1	data structure

Each measured data by sensor consit with following set of information.

- measured timestamp: timestamp when the data is measured by the sensor.

- metric: unique identifier among data which is stored in same container (e.g. <container> or <timeSeries> resource).

- measured value: the value of measured by the sensor which is identifed by the metric.

- data type of measured value (optional): the data type for representation of measured data.

- unit (optional): unit for measured value  (ex. "meter" or "kilo-meter").

Note that the oneM2M sensor measured data content type may include multiple set of  measured data.

Table x.2.1-1: Type Definition of m2m:sensingData

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| sensingData | m2m:sensingData | 1 | array of measured data |
| sensingData/item | m2m:array | 0..n | array item with measured data |
| sensingData/item/timestamp | m2m:timestamp | 1 | timestamp to indicate when the value is measured. |
| sensingData/item/metric | xs:string | 1 | identifier for the sensor. |
| sensingData/item/value | xs:string | 1 | string represented measured value (ex. "20” , “hot”) |
| sensingData/item/unit | xs:string | 0..1 | unit string for measured value |

x.2.2	Serialization of oneM2M sensor measured data

The m2m:sensingData can be serialized either XML or JSON as specified in clause 8 "Representation of primitives in data transfer".

x.2.2	Example of oneM2M sensor measured data

This is the example fo m2m:sensingData serialized in JSON.

Following example shows the case sensor "temperature" measured "15.34 C" at "2016-03-08T20:30:34.000Z", and "location" measured the location "latitude: 43.617127, longitude: 7.053190".

Example start

{"sensingData":

[

{

"timestamp":"2016-03-08T20:30:34.000Z",

"metric":"temperature",

"value":"1.534e+1",

"unit": "C"

},

{

"timestamp":"2016-03-08T20:30:34.000Z",

"metric":"location",

"value":"43.617127, 7.053190"

}

]

}

Example ends

# Comments

REQ-2015-0620

REQ-2015-0595R04