| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23.1 |
| Source:* | FUJITSU |
| Date:* | 2016-05-29 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | AE or remoteCSE may become tempolary disconnected state, and it resume the connectivity later. This CR proposed to change regarding STE functionality which is introduced as ARC-2015-2339R05. |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V.2.4.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

AE or remoteCSE may become tempolary disconnected state, and it resume the connectivity later. This CR proposed to change regarding STE functionality which is introduced as ARC-2015-2339R05.

R01: changed to trigger the forwarding process.

R02: Withdrawn CHANGE 03, and added CHANGE04 for clarify requestReachability attribute is used to determine bidirectional communication channel.

R03: Change 04 adjusts conditions by adding ‘otherwise’ .

### -----------------------Start of change 1-------------------------------------------

#### 7.4.4.2	<remoteCSE> resource specific procedure on CRUD operations

The entire CSE registration procedure including <CSE> resource creation procedure below is defined in 10.1.1.2.1 [6] ("CSE registration procedure").

##### 7.4.4.2.1	Create

Originator:

No change from the generic procedures in clause 7.2.2.1 with the following exception:

- An AE shall not originate a Create <remoteCSE> resource request.

Receiver:

- Primitive specific operation on Recv-1.0 "Check the syntax of received message":If the request is received over the Mca reference point, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the response status code 'OPERATION_NOT_ALLOWED'.

- "Send the Response primitive"

NOTE: Determination of the reference point is to the discretion of the Receiver CSE implementation.

##### 7.4.4.2.2	Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.1.

##### 7.4.4.2.3	Update

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

Same as the generic procedures in clause 7.2.2.2 except one addition:

As a part of Recv-6.5: "Create/Update/Retrieve/Delete/Notify operation is performed" procedure, If the pointOfAccess attribute is updated and there are any messages in the buffer for store-and-forward procedure, Receiver shall trigger the forwarding process to send all buffered messages.

##### 7.4.4.2.4	Delete

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.1.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 7.4.5.2	<AE> resource specific procedure on CRUD+N operations

This sub-clause describes AE resource specific behaviour for CRUD+N operations.

The entire AE registration procedure including <AE> resource creation procedure below is defined in clause 10.1.1.2.2 of the oneM2M TS-0001 [6] ("Application Entity registration procedure").

##### 7.4.5.2.1	Create

Originator:

No change from the generic procedures in clause 7.2.2.1 with the with the following exception:

A CSE shall not originate a Create <AE> resource request.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received over Mcc or Mcc' reference point, the Receiver CSE shall execute the following steps in order.

  - a)	"Create an unsuccessful Response primitive" with the Response Status Code 'OPERATION_NOT_ALLOWED'.

  - "Send the Response primitive".

NOTE:Determination of the reference point is to the discretion of the Receiver CSE implementation.

Otherwise,

  - No change from the generic procedures in clause 7.2.2.2.

##### 7.4.5.2.2	Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### 7.4.5.2.3	Update

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

Same as the generic procedures in clause 7.2.2.2 except one addition:

As a part of Recv-6.5: "Create/Update/Retrieve/Delete/Notify operation is performed" procedure, If the pointOfAccess attribute is updated with new value and there are any messages in the buffer for store-and-forward procedure, Receiver shall trigger the forwarding process to send all buffered messages.

##### 7.4.5.2.4 	Delete

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### 7.4.5.2.5	Notify

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver(Registrar CSE):

Same as the generic procedures in clause 7.2.2.2  except one addition:

As a part of Recv-6.5: "Create/Update/Retrieve/Delete/Notify operation is performed" procedure, If the AE which receives the Notification was not reachable, then the Receiver may return "TARGET_NOT_REACHABLE", or put the Notification into the buffer until the AE become reachable again.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 4---------------------------------------------

#### Notify re-targeting

If the Operation Excution Time is given in the request, the Hosting CSE should perform the following procedures at the time and shall not perform the procedures before the time.

When the Hosting CSE receives a Notify request primitive targeting (i.e., To parameter) its <AE> resource, the Hosting CSE re-targets the primitive to the AE.

If one or more <pollingChannel> resource exist on the <AE> then the Notification shall be stored into the buffer which is associated with the <pollingChannel> resource.

Otherwise, if the value of pointOfAccess attribute is NULL, but the value of requestReachability attribute is set as TRUE, then received Notification shall be stored into the buffer for store-and-forward procedure using bidirectional communication channels.

If the value of pointOfAccess attribute contains one or more addresses, following steps are performed:.

- Get pointOfAccess attribute value of the corresponding <AE> resource. If there is no available pointOfAccess address then the Hosting CSE shall send the Notify response primitive with a Response Status Code indicating "TARGET_NOT_REACHABLE" error.

If the forwarding Notification to the first address retrieved from pointOfAccess value is failed due to "Target not reachable", iterate with the next address.

If the Hosting CSE cannot forward it in the end, then it send the Notify response primitive with a Response Status Code indicating "TARGET_NOT_REACHABLE" error.

### -----------------------End of change 4---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?