| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#23.6 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2016-07-07 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | There are minor erros in m2m:flexContainerResource and m2m:announcedFlexContainerResource datra types. |
| CR against: Release* | R2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / <Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2.6.0 |
| Clauses/Sub Clauses* | 6.3.5.38, 6.3.5.39 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number> : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes minor corrections to two data types, m2m:flexContainerResource and m2m:announcedFlexContainerResource.

For the m2m:flexContainerResource, m2m:announceableResource are used as the extension base. However, creationTime, expirationTime and lastModifiedTime in the flexContainer resource are optional while they are mandatory in the m2m:announceableResource. This means m2m:announceableResource can not be used as the extension base. Corresponding change required in the XSD as well.

| Element Path | Element Data Type | Multiplicity |
| --- | --- | --- |
|  |  | m2m:announceableResource | m2m:flexContainerResource |
| @resourceName | xs:NCName | 1 | 1 |
| resourceType | m2m:resourceType | 1 | 1 |
| resourceID | m2m:ID | 1 | 1 |
| parentID | m2m:nhURI | 1 | 1 |
| accessControlPolicyIDs | m2m:acpType | 0..1 | 0..1 |
| creationTime | m2m:timestamp | 1 | 0..1 |
| expirationTime | m2m:timestamp | 1 | 0..1 |
| lastModifiedTime | m2m:timestamp | 1 | 0..1 |
| labels | m2m:labels | 0..1 | 0..1 |
| announceTo | list of xs:anyURI | 0..1 | 0..1 |
| announcedAttribute | list of xs:NCName | 0..1 | 0..1 |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 | 0..1 |
| stateTag | xs:nonNegativeInteger | - | 1 |
| containerDefinition | xs:anyURI | - | 1 |
| creator | m2m:ID | - | 0..1 |
| ontologyRef | xs:anyURI | - | 0..1 |

The same shall apply to the m2m:announcedFlexContainerResource Corresponding change required in the XSD.

| Element Path | Element Data Type | Multiplicity |
| --- | --- | --- |
|  |  | m2m:announcedResource | m2m:announcedFlexContainerResource |
| @resourceName | xs:NCName | 1 | 1 |
| resourceType | m2m:resourceType | 1 | 1 |
| resourceID | m2m:ID | 1 | 1 |
| parentID | m2m:nhURI | 1 | 1 |
| accessControlPolicyIDs | m2m:acpType | 0..1 | 0..1 m2m:announcedResource needs correction. This is mandatory in the announced variant.) |
| creationTime | m2m:timestamp | 1 | 0..1 |
| expirationTime | m2m:timestamp | 1 | 0..1 |
| lastModifiedTime | m2m:timestamp | 1 | 0..1 |
| labels | m2m:labels | 0..1 | 0..1 |
| link | xs:anyURI | 1 | 1 |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 | 0..1 |
| stateTag | xs:nonNegativeInteger | - | 1 |
| containerDefinition | xs:anyURI | - | 1 |
| ontologyRef | xs:anyURI | - | 0..1 |

### -----------------------Start of change 1---------------------------------------------

#### m2m:flexContainerResource

This data type is used as base type of all <flexContainer> specializations listed in clause 9.6.1.2.2 of TS-0001 [6]. It includes the attributes commonly used by all <flexContainer> resource type specializations.

It consists of the common attributes shown in Table 7.4.37.1-1 and the resource specific  attributes shared by all <flexContainer> specializations shown in Table 7.4.37.1-2.

Table 6.3.5.38-1: Type Definition of m2m:flexContainerResource

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| @resourceName | xs:NCName | 1 |  |
| resourceType | m2m:resourceType | 1 |  |
| resourceID | m2m:ID | 1 |  |
| parentID | m2m:nhURI | 1 |  |
| accessControlPolicyIDs | m2m:acpType | 0..1 |  |
| creationTime | m2m:timestamp | 0..1 |  |
| expirationTime | m2m:timestamp | 0..1 |  |
| lastModifiedTime | m2m:timestamp | 0..1 |  |
| labels | m2m:labels | 0..1 |  |
| announceTo | list of xs:anyURI | 0..1 |  |
| announcedAttribute | list of xs:NCName | 0..1 |  |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 |  |
| stateTag | xs:nonNegativeInteger | 1 |  |
| creator | m2m:ID | 0..1 |  |
| containerDefinition | xs:anyURI | 1 |  |
| ontologyRef | xs:anyURI | 0..1 |  |

#### m2m:announcedFlexContainerResource

This data type is used as base type of the announced variants of announceable <flexContainer> specializations listed in clause 9.6.1.2.2 of TS-0001 [6]. It includes the attributes commonly used by all announced <flexContainer> resource type specializations. Note that some specializations of the <flexContainer> resource are announceable while others are not announceable.

It consists of the common attributes shown in Table 7.4.37.1-1 and the resource specific attributes shared by all announced <flexContainer> specializations shown in Table 7.4.37.1-2.

Table 6.3.5.39-1: Type Definition of m2m:announcedFlexContainerResource

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| @resourceName | xs:NCName | 1 |  |
| resourceType | m2m:resourceType | 1 |  |
| resourceID | m2m:ID | 1 |  |
| parentID | m2m:nhURI | 1 |  |
| accessControlPolicyIDs | m2m:acpType | 1 |  |
| creationTime | m2m:timestamp | 0..1 |  |
| expirationTime | m2m:timestamp | 0..1 |  |
| lastModifiedTime | m2m:timestamp | 0..1 |  |
| labels | m2m:labels | 0..1 |  |
| link | xs:anyURI | 1 |  |
| dynamicAuthorizationConsultationIDs | list of xs:anyURI | 0..1 |  |
| stateTag | xs:nonNegativeInteger | 0..1 |  |
| containerDefinition | xs:anyURI | 1 |  |
| ontologyRef | xs:anyURI | 0..1 |  |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?