| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#23.6 |
| Source:* | Qualcomm (TIA) |
| Date:* | 2016-07-08 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com |
| Reason for Change/s:* | This CR proposes miscellaneous corrections to TS-0004 identified during XSD development. |
| CR against: Release* | R2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / <Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2.6.0 |
| Clauses/Sub Clauses* | Multiple clauses, see the summary table in the introduction. |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes miscellaneous corrections to TS-0004 to address the issues identified in PRO-2016-0226-PRO23_changes_of_XML_schemas_to_align_with_TS-0004. The summary of the changes are shown in the table below.

| # | CR# | Clause | Comments and proposed resolutions |
| --- | --- | --- | --- |
|  | N/A | XSD | NOTE: Shall all standardized <flexContainer> specializations be included into m2m:resourceWrapper? Proposed resolution: This is addressed in a separate contribution, see PRO-2016-0263-primitiveContent_in_XSD. |
|  | 0075R08- | XSD | NOTE: Unclear how to enable flexContainer specializations as child resource of CSEBase, remoteCSE, and AE resource in the XSD. Proposed resolution: This is addressed in a separate contribution, see PRO-2016-0263-primitiveContent_in_XSD. |
|  | 0128R02 | 7.4.38 | NOTE 1: The missingDataList is not a list of missingData defined in subscription Proposed resolution: The missingData and missingDataList are two different attributes. The naming for missingdata may be confusing. If we want to change the naming to missingDataConfig or something, we need a CR in ARC. Nobu will talk to Jason (Huawei). If we don’t change the name in ARC, then we should clarify this in TS-0004 and/or XSD. The missingDataList is the list of the dataGenerationTime value representing the missing Time Series Data in descending order by time if the periodicInterval is set and the missingDataDetect is TRUE. The missingData includes two values: a minimum specified missing number of the Time Series Data within the specified window duration, and the window duration. |
|  | 0128R02 | Table 8.2.4-1 | NOTE 2: short name for <timeSeries> resource shall be renamed from “tsi” to “ts”. Short name for <timeSeriesAnnc> resource shall be renamed from “tsia” to “tsa” Proposed resolution: This has been fixed in V2.6.0 already by the rapporteur. No further action required. |
|  | 0142R03 | Table 8.2.4-1 | NOTE 1: short name “rl” for role is already assigned to rateLimit. It is suggested to use “rol” instead. Proposed resolution: This has been fixed in V2.6.0 already by the rapporteur. No further action required. |
|  | 0142R03 | Table 8.2.4-1 | NOTE 2: some complex types members used for <role> and <token> have same long names e.g. notBefore and notAfter, but have different short names assigned. This violates the one-to-one mapping requirement of the long/short mapping table. Proposed resolution: This has been addressed by CATR in PRO-2016-0261-TS-0004_CR_Role_and_Token_Short_Name_Alignment_R2. |
|  | 0143R05 | 6.3.5.42 | NOTE 1: The purpose of data type m2m:tokenObject is unclear. The data type definition states “Used for tokenObject attribute in <token> resource and for Tokens parameter in a request”. However, tokenObject attribute and Tokens parameter have data type m2m:dynAuthJWT assigned. Proposed resolution: This has been addressed by CATR in PRO-2016-0262-TS-0004_CR_Token_Structure_Alignment_R2. |
|  | 0143R05 | 6.3.5.41 | NOTE 2: m2m:tokenPermission is a complex type which is applied as xs:list for the permissions attribute. This does not work. Permissions must be assigned a new complex data type. Suggested short name: “pm” Proposed resolution: This has been addressed by CATR in PRO-2016-0262-TS-0004_CR_Token_Structure_Alignment_R2. |
|  | 0143R05 | 6.3.5.41 | NOTE 3: Short name for resourceIDs subelement of m2m:tokenPermision is missing. It is suggested to use “ris” Proposed resolution: This has been addressed by CATR in PRO-2016-0262-TS-0004_CR_Token_Structure_Alignment_R2. |
|  | 0143R05 | 6.3.5.42 | NOTE 4: if m2m:tokenObject is obsolete, the short names for its elements should be removed. Proposed resolution: This has been addressed by CATR in PRO-2016-0262-TS-0004_CR_Token_Structure_Alignment_R2. |
|  | 0154R03 | 6.3.5.42 | NOTE 1: data type m2m:dynAuthlocalTokenIdAssignments should be renamed to m2m:dynAuthLocalTokenIdAssignments Proposed resolution: Correct datatype name as suggested above. Addressed in this CR. See change 3. |
|  | 0154R03 | 6.3.5.45 | NOTE 2: data type m2m:dynAuthDASRequest used for data type DASRequest subelement of m2m:dynAuthTokenReqInfo is not defined in this contribution. Proposed resolution: Datatype was defined as m2m:dynAuthDasRequest in PRO-2016-180R02. The name shall be corrected. In addition, we need to change securedDASRequest to securedDasRequest. Addressed in this CR. See change 4. |
|  | 0154R03 | Table 8.2.2-1 | NOTE 3: the new localTokenIDs primitive parameter added and the localTokenID subelement were assigned the same short name “lti”. It is suggested to keep “lti” for localTokenID and reassign “ltids” for localTokenIDs. Proposed resolution: This has been fixed in V2.6.0 already by the rapporteur. No further action required. |
|  | 0154R03 | 6.3.5.43 | NOTE 4: short name for "localTokenIdAssignment" is missing. It is suggested to assign "ltia". Proposed resolution: Need to add a short name for localTokenIdAssignment. Addressed in this CR. Has been included into Change 1. |
|  | 0154R03 | 6.3.5.45 | NOTE 5: short name for "dasInfo" is missing. It is suggested to assign "dasi". Proposed resolution: Need to add a short name for dasInfo. Addressed in this CR. Has been included into Change 1. |
|  | 0154R03 |  | NOTE 6: replace dasInfo/uri with dasInfo/URI since URI subelement name is already defined Proposed resolution: Use caps for subelement name. Addressed in this CR. Has been included into Change 1. |
|  | 0154R03 |  | NOTE 7: short name for "securedDASRequest" is missing. It is suggested to assign "sdr". Proposed resolution: Need to add a short name for securedDASRequest. In addition, we need to change securedDASRequest to securedDasRequest. Addressed in this CR. Has been included into Change 1. |
|  | 0154R03 |  | NOTE 8: In mapping table, localTokenId needs to be replaced with localTokenID. Proposed resolution: Need to correct element name. Addressed in this CR. Has been included into Change 1. |
|  | 0179R03 |  | NOTE: short name for "securityInfo" is missing. It is suggested to assign "seci". Proposed resolution: Need to add a short name for securityInfo. Addressed in this CR. Has been included into Change 1. |
|  | 0180R02 | 6.3.5.48 | NOTE 1: data type assigned to the escertkeMessage subelement, xs:binaryBase64, was replaced with xs:base64Binary. This needs to be corrected in TS-0004v2_6_0 too. Proposed resolution: This has been fixed in V2.6.0 already by the rapporteur. No further action required. |
|  | 0180R02 |  | NOTE 2: m2m:receiverE2ERandObject not defined in this contribution. Pending PRO-2016-183R0x defines data type m2m:receiverE2ERandObject Proposed resolution: Implement datatype definition given in PRO-2016-0183R06 (which was agreed at PRO#23.2) in the next XSD version v2_7_0. TS-0004 not affected. |
|  | 0180R02 |  | NOTE 3: eSPrimObject: Different capitalization between element name and data type. Not sure this was intended. May need to be corrected in TS-0004. Proposed resolution: Use notation esprimObject consistently. Addressed in this CR. Has been included into Change 5. |
|  | 0180R02 |  | NOTE 4: m2m:eSPrimObject is not defined in this contribution, also not defined in pending PRO-2016-183R0x. Proposed resolution: Datatype m2m:esprimObject is missing. It will be defined in a separate CR to TS-0004. |
|  | 0197R01 | XSD | NOTE: This should be corrected for Rel-1 versions of the above XSD files too (for alignment with TS-0001v1.13.0) Proposed resolution: Optional presence of the creator attribute: Corresponding changes are required for Release 1 XSDs. No impact on TS-0004 itself. |
|  | 0181R02 | 7.4.7 | NOTE: TS-0004 defines semanticDescriptor as child resource of contentInstance. TS-0001v2_9_0 does not show any child resources for contentInstance or contentInstanceAnnc. Should semanticDescriptorAnnc be added as child resource of contentInstanceAnnc? Proposed resolution: In TS-0001 v2.9.0 Section 9.6.7 does have <semanticDescriptor> as a child resource of <contentInstance>. (Note that there is a typo for the table title of Table 9.6.7-1.) No action for TS-0004 required. CDT-contentInstance-v2_6_0.xsd has been updated accordingly. |
|  | 0215R02 | 7.4.31 | NOTE: This CR does not address the following issue raised in PRO-2016-0141-PRO22_changes_of_XML_schemas_to_align_with_TS-0004 with CDT-notificationTargetPolicy-v2_5_0.xsd: “data type of rulesRelationship attribute is differently defined in TS-0001 (single value, AND or OR) and TS-0004 (“list of xs:token”). Should data type m2m:logicalOperator be applied to this attribute?” Proposed resolution: m2m:logicalOperator should be applied. Addressed in this CR. See change 2. |
|  | 0077R02 | Table 8.2.5-1 | NOTE: “This CR [PRO-2016-0077R02-on-demand_discovery_support] introduces a new short name for “filterCriteria” subelement of “IPEDiscoveryRequest” as “fcr”. The short name should be replaced by “fc*”. There already exists the “filterCriteria” element with short name “fc” that shall be reused.” Proposed resolution: Addressed in this CR. See change 1. |

----------------------- Start of change 1 -------------------------------------------

### Complex data types members

In protocol bindings complex data types member names shall be translated into short names of Table 8.2.5-1.

Table 8.2.5-1: Complex data type member short names

| Member Name | Occurs in | Short Name |
| --- | --- | --- |
| createdBefore | filterCriteria, eventNotificationCriteria | crb |
| createdAfter | filterCriteria, eventNotificationCriteria | cra |
| modifiedSince | filterCriteria, eventNotificationCriteria | ms |
| unmodifiedSince | filterCriteria, eventNotificationCriteria | us |
| stateTagSmaller | filterCriteria, eventNotificationCriteria | sts |
| stateTagBigger | filterCriteria, eventNotificationCriteria | stb |
| expireBefore | filterCriteria, eventNotificationCriteria | exb |
| expireAfter | filterCriteria, eventNotificationCriteria | exa |
| labels | filterCriteria, eventNotificationCriteria | lbl * |
| resourceType | filterCriteria | ty * |
| sizeAbove | filterCriteria, eventNotificationCriteria | sza |
| sizeBelow | filterCriteria, eventNotificationCriteriay | szb |
| contentType | filterCriteria | cty |
| limit | filterCriteria | lim |
| attribute | filterCriteria, eventNotificationCriteria | atr |
| notificationEventType | eventNotificationCriteria | net |
| operationMonitor | eventNotificationCriteria, notificationEvent | om |
| representation | notificationEvent | rep |
| filterUsage | filterCriteria | fu |
| eventCatType | eventCat | ect |
| eventCatNo | eventCat | ecn |
| number | batchNotify | num |
| duration | batchNotify | dur |
| notification | aggregatedNotification, Request Primitive Content | sgn |
| notificationEvent | notification | nev |
| verificationRequest | notification | vrq |
| subscriptionDeletion | notification | sud |
| subscriptionReference | notification | sur |
| creator | notification | cr* |
| notificationForwardingURI | notification | nfu* |
| IPEDiscoveryRequest | notification | idr |
| filterCriteria | IPEDiscoveryRequest | fc* |
| operation | operationMonitor, dynAuthDasRequest | op* |
| originator | operationMonitor, IPEDiscoveryRequest, dynAuthDasRequest | or* |
| accessId | externalID | aci |
| MSISDN | externalID | msd |
| action | actionStatus | acn |
| status | actionStatus | sus |
| childResource | All except execInstance, announced resource, management resources from firmware | ch |
| accessControlRule | privileges, selfPrivileges | acr |
| accessControlOriginators | accessControlRule | acor |
| accessControlOperations | accessControlRule | acop |
| accessControlContexts | accessControlRule | acco |
| accessControWindow | accessControlContexts | actw |
| accessControlIpAddresses | accessControlContexts | acip |
| ipv4Addresses | accessControlIpAddress | ipv4 |
| ipv6Addresses | accessControlIpAddress | ipv6 |
| accessControlLocationRegion | accessControlContexts | aclr |
| countryCode | accessControlLocationRegion | accc |
| circRegion | accessControlLocationRegion | accr |
| name | attribute, anyArgType, mgmtLinkRef, childResourceRef, contentRef | nm* |
| specializationID | childResourceRef | spid |
| value | attribute | val |
| type | anyArgType | typ |
| maxNrOfNotify | rateLimit | mnn |
| timeWindow | rateLimit | tww |
| scheduleEntry | scheduleElement | sce |
| aggregatedNotification | Request Primitive Content | agn |
| attributeList | Request Primitive Content | atrl |
| securityInfo | Request Primitive Content, Response Primitive Content | seci |
| aggregatedResponse | Response Primitive Content | agr |
| resource | Response Primitive Content | rce |
| URIList | Response Primitive Content | uril |
| anyArg | resetArgsType, rebootArgsType, uploadArgsType, downloadArgsType, softwareInstallArgsType softwareUpdateArgsType, softwareUninstallArgsType, execReqArgsListType | any |
| fileType | downloadArgsType | ftyp |
| URI | resourceWrapper, dynAuthTokenReqInfo | uri |
| URL | downloadArgsType | url* |
| username | uploadArgsType, downloadArgsType, softwareUpdateArgsType, softwareUninstallArgsType, | unm |
| password | uploadArgsType, downloadArgsType, softwareUpdateArgsType, softwareUninstallArgsType, | pwd |
| filesize | downloadArgsType | fsi |
| targetFile | downloadArgsType | tgf |
| delaySeconds | downloadArgsType | dss |
| successURL | downloadArgsType | surl |
| startTime | downloadArgsType | stt |
| completeTime | downloadArgsType | cpt |
| UUID | softwareInstallArgsType softwareUpdateArgsType, softwareUninstallArgsType, | uuid |
| executionEnvRef | softwareInstallArgsType softawareUpdateArgsType, softwareUninstallArgsType, | eer |
| version | softwareUninstallArgsType | vr* |
| reset | execReqArgsListType | rst |
| reboot | execReqArgsListType | rbo* |
| upload | execReqArgsListType | uld |
| download | execReqArgsListType | dld |
| softwareInstall | execReqArgsListType | swin |
| softwareUpdate | execReqArgsListType | swup |
| softwareUninstall | execReqArgsListType | swun |
| tracingOption | deliveryMetaData | tcop |
| tracingInfo | deliveryMetaData | tcin |
| responseTypeValue | responseTypeInfo | rtv |
| notificationURI | responseTypeInfo | nu |
| timeOfDay | deletionContexts | tod |
| locationRegions | deletionContexts | lr |
| URIReference | contentRef | urir |
| semanticsFilter | filterCriteria | smf |
| missingDataList | timeSeries | mdl |
| missingData | eventNotificationCriteria | md |
| version | tokenObject | tkvr |
| tokenID | tokenObject, dynAuthLocalTokenIdAssignments | tkid |
| holder | tokenObject | tkhd |
| issuer | tokenObject | tkis |
| notBefore | tokenObject | tknb |
| notAfter | tokenObject | tkna |
| tokenName | tokenObject | tknm |
| audience | tokenObject | tkau |
| permissions | tokenObject | tkps |
| extension | tokenObject | tkex |
| tokenObject | tokens | tkob |
| localTokenIdAssignment | dynAuthLocalTokenIdAssignments | ltia |
| localTokenID | dynAuthLocalTokenIdAssignments | lti |
| dasInfo | dynAuthTokenReqInfo | dasi |
| dasRequest | dynAuthTokenReqInfo | daq |
| securedDasRequest | dynAuthTokenReqInfo | sdr |
| filterOperation | filterCriteria | fo |
| targetedResourceType | dynAuthDasRequest | trt |
| originatorIP | dynAuthDasRequest | oip |
| ipv4Address | dynAuthDasRequest | ip4 |
| ipv6Address | dynAuthDasRequest | ip6 |
| originatorLocation | dynAuthDasRequest | olo |
| originatorRoleIDs | dynAuthDasRequest | orid |
| requestTimestamp | dynAuthDasRequest | rts |
| targetedResourceID | dynAuthDasRequest | trid |
| proposedPrivilegesLifetime | dynAuthDasRequest | ppl |
| roleIDsFromACPs | dynAuthDasRequest | rfa |
| tokenIDs | dynAuthDasRequest | tids |
| dynamicACPInfo | dynAuthDasResponse | dai |
| grantedPrivileges | dynAuthDasResponse | gp |
| privilegesLifetime | dynAuthDasResponse | pl |
| tokens | dynAuthDasResponse | tkns |
| securityInfoType | securityInfo | sit |
| dasRequest | securityInfo | dreq |
| dasResponse | securityInfo | dres |
| e2eRandObject | securityInfo | ero |
| esprimObject | securityInfo | epo |
| escertkeMessage | securityInfo | eckm |
| NOTE: * marked short names have been already assigned in attribute Table 8.2.3-1. |

----------------------- End of change 1 -------------------------------------------

----------------------- Start of change 2 -------------------------------------------

### Resource Type <notificationTargetPolicy>

#### Introduction

This is a child resource of the <CSEBase> resource. This resources represents a policy to be followed by the Hosting CSE to manage Notification Targets of a resource subscription. Each policy has Notification Target deletion rules.

The detailed description can be found in clause 9.6.32 in TS-0001 Functional Architecture [6].

Table 7.4.31.1-1: Data type definition of <notificationTargetPolicy> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| notificationTargetPolicy | CDT- notificationTargetPolicy-v2_6_0.xsd |  |

Editor’s Note: XSD for this resource type is TBD

Table 7.4.31.1-2: Universal/Common Attributes of <notificationTargetPolicy> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| expirationTime | O | O |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| lastModifiedTime | NP | NP |
| labels | O | O |
| creator | O | NP |

Table 7.4.31.1-3: Resource Specific Attributes of <notificationTargetPolicy> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| action | O | NP | m2m:notificationTargetPolicyAction | No default |
| policyLabel | O | O | xs:token | No default |
| rulesRelationship | O | O | m2m:logicalOperator | This attribute shall have a value either “AND” or “OR” when more than one <policyDeletionRules> child resource is specified. |

Table 7.4.31.1-4: Child resources of <notificationTargetPolicy>  resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <policyDeletionRules> | [variable] | 0..2 | Clause 7.4.32 |
| <subscription> | [variable] | 0..n | Clause 7.4.8 |

#### <notificationTargetPolicy> resource specific procedure on CRUD operations

This clause describes <serviceSubscribedAppRule> resource specific primitive behaviour for CRUD operations.

##### Create

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Update

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Delete

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

----------------------- End of change 2 -------------------------------------------

----------------------- Start of change 3 -------------------------------------------

#### m2m:dynAuthLocalTokenIdAssignments

Used for Assigned Token Identifiers parameter of a response primitive.

Table 6.3.5.43-1: Type Definition of m2m:dynAuthLocalTokenIdAssignments

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| localTokenIdAssignment | anonymous | 1..n |  |
| localTokenIdAssignment/localTokenID | xs:NCName | 1 |  |
| localTokenIdAssignment/tokenID | m2m:tokenID | 1 |  |

----------------------- End of change 3 -------------------------------------------

----------------------- Start of change 4 -------------------------------------------

#### m2m:dynAuthTokenReqInfo

Used for Token Summary provided by a Dynamic Authorization Server to an Originator as part of the “Process Token Request Information” in clause 7.3.1.Y.

Table 6.3.5.45-1: Type Definition of m2m: dynAuthTokenReqInfo

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| dasInfo | anonymous | 1..n |  |
| dasInfo/URI | xs:anyURI | 1 | Dynamic Authorization Server URI |
| dasInfo/dasRequest | m2m:dynAuthDasRequest | 0..1 | Information to send to the DAS |
| dasInfo/securedDasRequest | m2m:dynAuthJWT | 0..1 | Secured Information to send to the DAS |

----------------------- End of change 4 -------------------------------------------

----------------------- Start of change 5 -------------------------------------------

#### m2m:securityInfo

Table 6.3.5.48-1: Type Definition of m2m:securityInfo

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| securityInfoType | m2m:securityInfoType | 1 |  |
| dasRequest | m2m:dynAuthDasRequest | 0..1 | This element shall only be present if securityInfoType is set to a value of “1” (Dynamic Authorization Request) |
| dasResponse | m2m:dynAuthDasResponse | 0..1 | This element shall only be present if securityInfoType is set to a value of “2” (Dynamic Authorization Response) |
| e2eRandObject | m2m:receiverE2ERandObject | 0..1 | This element shall only be present if securityInfoType is set to a value of “4” (Receiver E2E Rand Object Response) |
| esprimObject | m2m:esprimObject | 0..1 | This element shall only be present if securityInfoType is set to a value of “5” (ESPrim Object) |
| escertkeMessage | xs:base64Binary | 0..1 | This element shall only be present if securityInfoType is set to a value of “6” (ESCertKE Message) |

----------------------- End of change 5 -------------------------------------------

----------------------- Start of change 6 -------------------------------------------

----------------------- End of change 6 -------------------------------------------

----------------------- Start of change 7 -------------------------------------------

----------------------- End of change 7 -------------------------------------------

----------------------- Start of change 8 -------------------------------------------

----------------------- End of change 8 -------------------------------------------

----------------------- Start of change 9 -------------------------------------------

----------------------- End of change 9 -------------------------------------------

----------------------- Start of change 10 -------------------------------------------

----------------------- End of change 10 -------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?