| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#23.6 |
| Source:* | KETI(Korea Electronics Technology Institute) |
| Date:* | 2016-07-08 |
| Contact:* | SeungMyeong JEONG, KETI, sm.jeong@keti.re.kr Sungchan Choi, KETI, csc@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.kr |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v1.8.0 |
| Clauses/Sub Clauses* | 6.2.4 oneM2M resource addressing |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes addressing scheme for virtual resources. Strictly speaking, resource ID does not use resource type name(e.g. <latest>) for addressing. However, virtual resources does not have its own representation (especially, resourceName and resourceID). It is suggested to use virtual resource “type” name as long and short both for addressing.

Also, some editorial clean-ups are included.

### -----------------------Start of change 1-------------------------------------------

### oneM2M Resource Addressing

- Authorized oneM2M entities can operate on a oneM2M resource by addressing the resource ID as the target address(i.e. To parameter) in a request primitive. There are two resource addressing methods:Structured resource ID (used in Hierarchical Addressing): the ID is constructed as a relative path from the CSEBase resource via parent resources.

Unstructured resource ID (used in Non-hierarchical Addressing): the ID uniquely identifies the resource in the domain of its Hosting CSE.

For virtual resource addressing, long and short resource type name for a virtual resource type shall be used in Structured and Unstructured mechanisms above.

Furthermore each resource ID can be expressed in either

- CSE-relative format; or

- SP-relative format; or

- Absolute format.

A single attribute of the targeted oneM2M resource shall be addressable adding the sub-address (targeted-attribute-name) following a "#" character after the resource address.

The address appearing in 'ChildResourceRef' may be used as in SP relative format, if it is obvious which SP or CSE-ID should be added.

The syntax of the Resource Identifier (resource-ID) in ABNF notion [20] is as follows:

resource-identifier = (hierarchical-resource-address / non-hierarchical-resource-address) [ "#" targeted-attribute-name ]

hierarchical-resource-address = [ CSE-ID] 1*("/" resource-name)

non-hierarchical-resource-address = [ CSE-ID] "/" unstructured-ID

unstructured-ID = 1*unreserved

resource-name = 1*unreserved

When including hierarchical resource IDs into the Content parameter of response primitives (cf. clause 7.5.2), the resource Hosting CSE shall select the appropriate format of the ID depending on the location of the Originator. If the Originator of the request primitive is registered to the Hosting CSE, the CSE-relative format of hierarchical resource ID applies. If the Originator of the request primitive is not registered to the Hosting CSE but belongs to the same SP domain, the CSE-relative format applies. If the Originator of the request primitive belongs to a different SP domain, the Absolute format of hierarchical resource ID applies.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?