| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 24.3 |
| Source:* | C-DOT |
| Date:* | 2016-09-12 |
| Contact:* | Siddharth Trikha (strikha@cdot.in), Poornima Trivedi (poornima@cdot.in) |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V1.8.0 |
| Clauses/Sub Clauses* | 7.5.1.2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to enhance the clarity regarding the content of the NOTIFY request corresponding to the subscription.

In the “representation” object of NOTIFY request for subscription, there are 3 possible notificationContentTypes:

- modifiedAttributes

- allAttributes

- resourceID

as per section 6.3.5.13, representation can be of “xs:anyType”

m2m:notification Table 6.3.5.13-1: Type Definition of m2m:notification Element Path Element Data Type Multiplicity Note notificationEvent (anonymous) 0..1 notificationEvent/representation xs:anyType 0..1 Representation of resource modification or response primitive in XML/JSON representation. notificationEvent/operationMonitor (anonymous) 0..1 notificationEvent/operationMonitor/operation m2m:operation 1 m2m:operation This element shall only be present if the operationMonitor parent element is present. Otherwise it shall not. notificationEvent/operationMonitor/originator m2m:ID 1 m2m:ID This element shall only be present if the operationMonitor parent element is present. Otherwise it shall not. notificationEvent/notificationEventType m2m:notificationEventType 1 verificationRequest xs:boolean 0..1 subscriptionDeletion xs:boolean 0..1 subscriptionReference xs:anyURI 1 creator m2m:ID 0..1 notificationForwardingURI xs:anyURI 0..1

But in order to ensure that there is one understanding of content types for originator and receiver, it should be clearly mentioned that what object a given content type maps to.

- modifiedAttributes maps to partial resource (m2m:resourceType)

- allAttributes maps to complete resource(m2m:resourceType)

- resourceID maps to structured or unstructured resource id (m2m:uri)

| Modified Attributes |
| --- |
| m2m:sgn{ rep: { m2m:cont{ label:”LABEL 1” } } | m2m:sgn{ rep: { label:”LABEL 1” } |
| All Attributes |
| m2m:sgn{ rep: { m2m:cont{ resourceType:3 resourceID:R343 currentByteSize: 10 currNrOfInstance:10 …………….. } } | m2m:sgn{ rep: { resourceType:3 resourceID:R343 currentByteSize: 10 currNrOfInstance:10 …………….. } |
| ResourceID |
| m2m:sgn{ rep:{ m2m:uri{ resourceID : “R0” } } } | m2m:sgn{ rep:{ resourceID: “R0” } } |

This CR also includes changes from qualcomm contribution PRO-2016-0358 as decided in PRO 25

### -----------------------Start of change 1-------------------------------------------

##### 7.5.1.2.2	Notification for modification of subscribed resources

When the notification message is forwarded or aggregated by transit CSEs, the Originator or a transit CSE shall check whether there are notification policies to enforce between subscription resource Hosting CSE and the notification target. In that case, the transit CSE as well as the Originator shall process Notify request primitive(s) by using the corresponding policy and send processed Notify request primitive(s) to the next CSE with notification policies related to the enforcement so that the transit CSE is able to enforce the policy defined by the subscriber. The notification policies related to the enforcement at this time is verified by using the subscription reference in the Notify request primitive. In the notification policies, the latestNotify attribute is only enforced in the transit CSE as well as the Originator.

If Event Category parameter is set to ''latest' in the notification request primitive, the transit CSE as well as Originator shall cache the most recent Notify request. That is, if a new Notify request is received by the CSE with a subscription reference that has already been buffered for a pending Notify request, the newer Notify request will replace the buffered older Notify request.

Originator: When an event is generated, the Originator shall execute the following steps in order:

Step 1.0	Check the eventNotificationCriteria attribute of the <subscription> resource associated with the modified resource:

If the eventNotificationCriteria attribute is set, then the Originator shall check whether the corresponding event matches with the event criteria.

If notificationEventType is not set within the eventNotificationCriteria attribute, the Originator shall use the default setting of Update_of_Resource to compare against the event.

If the notificationEventType has either an explicit or default value of  “Update_of_Resource” and the attribute condition is also present then the matching event shall only be detected if one of the attributes in the list has been updated. If the attribute condition is not present then a matching event is generated whenever any attribute has been updated.

If the event matches, go to the step 2.0. Otherwise, the Originator shall discard the corresponding event.

If the eventNotificationCriteria attribute is not configured, the Originator shall use the default setting of Update_of_Resource for notificationEventType and then continue with the step 2.0

Step 2.0	The Originator shall check the notification policy as described in the below steps, but the notification policy may be checked in different order. After checking the notification policy in step 2.0 (i.e., from step 2.1to step 2.6), then continue with step 3.0

Step 2.1	The Originator shall determine the type of the notification per the notificationContentType attribute. The possible values of for notificationContentType attribute are 'Modified Attributes', 'All Attributes', or 'ResourceID'. This attribute may be used joint with eventType attribute in the eventNotificationCriteria to determine if it is the attributes/resourceID of the subscribed-to resource or the attributes/resourceID of the child resource of the subscribed-to resource that shall be returned in the notification.

If the value of notificationContentType is set to 'Modified Attribute', the Notify request primitive shall include the partial resource containing modified attribute(s) only(Refer section 7.2.1.2 for response content description)

If the value of notificationContentType is set to 'All Attributes', the Notify request primitive shall include the complete resource with  all attributes  (Refer section 7.2.1.2 for response content description)

If the value of notificationContentType is set to 'ResourceID', the Notify request primitive shall include the URI  of the resource(Refer section 7.2.1.2 for response content description)

If the notificationContentType attribute is not configured, the default value is set to 'All Attributes'

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?