| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#25 |
| Source:* | InterDigital |
| Date:* | 2016-10-09 |
| Contact:* | Dale Seed (dale.seed@InterDigital.com), Bob Flynn (bob.flynn@InterDigital.com) |
| Reason for Change/s:* | xM2M-Accept field is defined in the MQTT binding but missing in CDT-requestPrimitive-v2_7_0 XSD |
| CR against: Release* | Rel 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | CDT-requestPrimitive-v2_7_0 XSD file |
| Clauses/Sub Clauses* | Element rqp |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: PRO-2016-0396-CR-XSD_Accept_parameter_R1 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

TS0010-MQTT_Protocol_Binding_V2_3_0 Section 6.5.3. mentions that an application can send xM2M-Accept field in requestPrimitive which will indicate the serialization format that the originator is prepared to accept in a Response.

However CDT-requestPrimitive-v2_7_0 does not contain element xM2M-Accept. This contribution proposes adding a corresponding Accept element (acpt).

## ----------------------- Start of change 1 -----------------------

<xs:element name="rqp">

<xs:complexType>

<xs:sequence>

<!-- parameter "Operation"  -->

<xs:element name="op" type="m2m:op" minOccurs="1"/>

<!-- parameter "To" -->

<xs:element name="to" type="xs:anyURI" minOccurs="1"/>

<!-- parameter "From" -->

<xs:element name="fr" type="m2m:ID" minOccurs="1"/>

<!-- parameter "Request Identifier" -->

<xs:element name="rqi" type="m2m:rid" minOccurs="1"/>

<!-- parameter "ResourceType" -->

<xs:element name="ty" type="m2m:ty" minOccurs="0"/>

<!-- parameter "Content" -->

<xs:element name="pc" type="m2m:primitiveContent" minOccurs="0"/>

<!-- parameter "Role" -->

<xs:element minOccurs="0" name="rol" type="xs:anyType"/>

<!-- parameter "Originating Timestamp" -->

<xs:element name="ot" type="m2m:timestamp" minOccurs="0"/>

<!-- parameter "Request Expiration Timestamp" -->

<xs:element name="rqet" type="m2m:absRelTimestamp" minOccurs="0"/>

<!-- parameter "Result Expiration Timestamp" -->

<xs:element name="rset" type="m2m:absRelTimestamp" minOccurs="0"/>

<!-- parameter "Operation Execution Time" -->

<xs:element name="oet" type="m2m:absRelTimestamp" minOccurs="0"/>

<!-- parameter "Response Type" -->

<xs:element name="rt" type="m2m:responseTypeInfo" minOccurs="0"/>

<!-- parameter "Result Persistence" -->

<xs:element name="rp" type="m2m:absRelTimestamp" minOccurs="0"/>

<!-- parameter "Result Content" -->

<xs:element name="rcn" type="m2m:rcn" minOccurs="0"/>

<!-- parameter "Event Category" -->

<xs:element name="ec" type="m2m:ec" minOccurs="0"/>

<!-- parameter "Delivery Aggregation" -->

<xs:element name="da" type="xs:boolean" minOccurs="0"/>

<!-- parameter "Group Request Identifier" -->

<xs:element name="gid" type="xs:string" minOccurs="0"/>

<!-- parameter "Filter Criteria" -->

<xs:element name="fc" type="m2m:fc" minOccurs="0"/>

<!-- parameter "Discovery Result Type" -->

<xs:element name="drt" type="m2m:discResType" minOccurs="0"/>

<!-- parameter "Accept" -->

<xs:element name="acpt" type=" m2m:typeOfContent" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

</xs:element>

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?