| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#25 |
| Source:* | InterDigital |
| Date:* | 2016-10-09 |
| Contact:* | Dale Seed (dale.seed@InterDigital.com), Bob Flynn (bob.flynn@InterDigital.com) |
| Reason for Change/s:* | See the introduction. |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0009-V2.6.1 |
| Clauses/Sub Clauses* | Section 6.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Currently the oneM2M HTTP binding doesn’t support Content Offset and Content Status header parameters. We need to add these since they are supported in the Rel-2 versions of TS-0001 and TS-0004.

As per TS0001 :-

Content Status:   This parameter shall be present in the response to a Retrieve operation when the returned content is partial. More specifically, this parameter takes the value of  partial depending on the Content parameter.

If Response Code is successful then and the  Content parameter is present due to the following case:

Retrieve (R): Content is the retrieved resource content or aggregated contents of discovered resources and the retrieved content is partial

Then Content Status parameter shall be present in the response for a Retrieve (R) operation

Content Offset:   This parameter includes either a starting point which can be used in a subsequent Retrieve request for direct child resource processing in the resource tree or the actual number of child resources, and descendants returned in Content. Its value depends on the information included in the Content Status parameter

If Content Status parameter is complete then this parameter shall not be included

If Content Status parameter is partial then this shall include the offset where processing can restart for the remaining direct child resources in the resource tree.

Then Content Offset parameter shall be present in the response for a Retrieve (R)  operation.

## ----------------------- Start of change 1 -----------------------

### X-M2M-RSC

The X-M2M-RSC header in a HTTP response message shall be mapped to the Response Status Code parameter of response primitives and vice versa only if the mapping between the Response Status Code and the HTTP Status Code is N:1 relationship (e.g., Response Status Code 4000 and 4102 are mapped to HTTP Status Code 400 in the Table 6.3.2-1).

### 6.4.18	X-M2M-ATI

The X-M2M-ATI header in a HTTP response message shall be mapped to the Assigned Token Identifiers parameter of response primitives and vice versa.

The format of the X-M2M-ATI header shall be represented as a sequence of  lti-value:tkid-value pairs separated by a colon “:’ and  multiple pairs appended with ‘+’ character.

For example, the header looks as follows:

X-M2M-ATI: lti-value1:tkid-value1 + lti-value2:tkid-value2 + …

if the XML representation of the Assigned Token Identifiers parameter is given as (using short element names):

<ati>

<ltia>

<lti>lti-value1</lti>

<tkid>tkid-value1</tkid>

</ltia>

<ltia>

<lti>lti-value2</lti>

<tkid>tkid-value2</tkid>

</ltia>

…

</ati>

The data type m2m:dynAuthlocalTokenIdAssignments of the Assigned Token Identifiers parameter is defined in clause 6.3.5.43 of TS-0004 [3].

### 6.4.19	Authorization

If a request primitive includes a Tokens parameter it shall be mapped to the Authorization header.

The Tokens primitive parameter is represented as a space separated list of  JSON Web Signature (JWS) and JSON Web Encryption (JWE) strings in Compact Serialization format of datatype m2m:dynAuthJWT as defined in clause 6.3.3 of TS-0004 [3].

When mapped into the Authorization header, each individual token in the Tokens primitive parameter shall be separated by ‘+’ character.

For example, if the Tokens parameter consists of a list of two JWS/JWE Tokens,

eyJ0eXAiOiJK.eyJpc3MiOiJqb2UiLA0KIC.dBjftJeZ4CVP  eyJ0eXAiOiJK.eyJpc3MiOiJqb2UiLA0KIC.dBjftJeZ4CVP.5eym8TW_c8SuK.SdiwkIr3a.XFBoMYUZo

the Authorization header looks as follows

Authorization: eyJ0eXAiOiJK.eyJpc3MiOiJqb2UiLA0KIC.dBjftJeZ4CVP+ eyJ0eXAiOiJK.eyJpc3MiOiJqb2UiL

A0KIC.dBjftJeZ4CVP.5eym8TW_c8SuK.SdiwkIr3a.XFBoMYUZo

The line break in the above example is for illustrative purposes and shall not be included into the Authorization header.

### 6.4.20	X-M2M-CTO

The X-M2M-CTO header shall be mapped to the Content Offset parameter of response primitives.

### 6.4.21		X-M2M-CTS

The X-M2M-CTS header shall be mapped to the Content Status parameter of response primitives.

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?