| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO 26 |
| Source:* | IL SEONG, HERIT(TTA), kr.il.seong@herit.net Heesuk Park, HERIT(TTA), hspark@herit.net Inseuk Lee, HERIT(TTA), inseuk.lee@herit.net |
| Date:* | 2016-12-06 |
|  | +82-10-7430-1288 |
| Reason for Change/s:* | Correction of inconsistency in semanticSupportIndicator. See the introduction for details |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (use latest agreed version) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v2.7.1 |
| Clauses * | Clause 7.4.13, Clause 8.2.3 XSD : CDT-group-v2_7_0 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version:2016-10-27 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR addresses issues that exist inconsistency in technical specifications TS-0004 and TS-0001. TS-0001 clause  9.6.13 describes resource type of <group> and  Table 9.6.13-2 shows attributes of <group> resource which includes attribute semancticSupportIndicator. Corresponding TS-0004 clause 7.4.13 specify resource type <group> and  Table 7.4.13-3 lists resource specific attributes of <group> resource and attribute semancticSupportIndicator  is missed

For the correction of inconsistency in specifications, we need to change the TS-0004 as follows :

- Add the attribute semancticSupportIndicator to Table 7.4.13-2 Attributes of <group>  in clause 7.4.13

- Add definition of  ‘Short Name’ for semancticSupportIndicator which is described  clause 8.2.3 Table 8.2.3-2( Resource attribute short names(2/6).

- Corresponig XSD file(CTD-group-v2_7_0) should be chaned.(long & short)

There is no impact to other part of TS-0004 and other specifications.

### -----------------------Start of change 1-------------------------------------------

7.4.13 Resource Type <group>

7.4.13.1 Introduction

Table 7.4.13.1-3  Resource Specific Attributes of <group> resource.

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| memberType | O | NP | m2m:memberType | Default value is set to 'MIXED' |
| currentNrOfMembers | NP | NP | xs:nonNegativeInteger | No default (This is generated by the Hosting CSE and limited by the maxNrOfMembers attribute of the <group> resource) |
| maxNrOfMembers | M | O | xs:positiveInteger | No default |
| memberIDs | M | O | list of xs:anyURI | No default This list may contain no members |
| membersAccessControlPolicyIDs | O | O | m2m:listOfURIs | No default |
| memberTypeValidated | NP | NP | xs:boolean | No default (This is generated by the Hosting CSE) |
| consistencyStrategy | O | NP | m2m:consistencyStrategy | Default value is set to 'ABANDON_MEMBER' |
| groupName | O | O | xs:string | No default |
| semanticSupportIndicator | NP | NP | xs:boolean | No default (This is generated by the Hosting CSE |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

8.2.3 Resource attributes

In protocol bindings, resource attributes names shall be translated into short names shown in the following tables.

Table 8.2.3-2: Resource attribute short names (2/6)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| currentByteSize | container | cbs |
| locationID | container | li |
| disableRetrieval | container | disr |
| contentInfo | contentInstance | cnf |
| contentSize | contentInstance | cs |
| contentRef | contentInstance | conr |
| containerDefinition | flexContainer | cnd |
| primitiveContent | request | pc* |
| content | contentInstance, timeSeriesInstance | con |
| cseType | CSEBase, remoteCSE | cst |
| CSE-ID | CSEBase, remoteCSE, service SubscribedNode | csi |
| supportedResourceType | CSEBase | srt |
| notificationCongestionPolicy | CSEBase | ncp |
| source | delivery | sr |
| target | delivery, request | tg |
| lifespan | delivery | Ls |
| eventCat | delivery | ec |
| deliveryMetaData | delivery | dmd |
| aggregatedRequest | delivery | arq |
| eventID | eventConfig, statsCollect | evi |
| eventType | eventConfig | evt |
| evenStart | eventConfig | evs |
| eventEnd | eventConfig | eve |
| operationType | eventConfig | opt |
| dataSize | eventConfig | ds |
| execStatus | execInstance | exs |
| execResult | execInstance | exr |
| execDisable | execInstance | exd |
| execTarget | execInstance, mgmtCmd | ext |
| execMode | execInstance, mgmtCmd | exm |
| execFrequency | execInstance, mgmtCmd | exf |
| execDelay | execInstance, mgmtCmd | exy |
| execNumber | execInstance, mgmtCmd | exn |
| execReqArgs | execInstance, mgmtCmd | exra |
| execEnable | mgmtCmd | exe |
| memberType | group | mt |
| currentNrOfMembers | group | cnm |
| maxNrOfMembers | group | mnm |
| memberIDs | group | mid |
| membersAccessControlPolicyIDs | group | macp |
| memberTypeValidated | group | mtv |
| consistencyStrategy | group | csy |
| semanticSupportIndicator | group | ssi |
| groupName | group, subscription | gn |
| locationSource | locationPolicy | los |
| locationUpdatePeriod | locationPolicy | lou |
| locationTargetID | locationPolicy | lot |
| locationServer | locationPolicy | lor |
| locationContainerID | locationPolicy | loi |
| locationContainerName | locationPolicy | lon |
| locationStatus | locationPolicy | lost |
| serviceRoles | m2mServiceSubscriptionProfile | svr |
| description | mgmtCmd, mgmtObj, all management resources from firmware | dc |
| cmdType | mgmtCmd | cmt |
| mgmtDefinition | mgmtObj, all management resources from firmware | mgd |
| objectIDs | mgmtObj | obis |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

7.4.13 Resource Type <group>

7.4.13.1 Introduction

Table 7.4.13.1-1: Data type definition of <group> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| group | CDT-group-v2_7_0.xsd |  |

File : CDT-group-v2_7_0.xsd(long)

<?xml version="1.0" encoding="UTF-8"?>

<!--

Copyright Notification

The oneM2M Partners authorize you to copy this document, provided that you retain all copyright and other proprietary notices

contained in the original materials on any copies of the materials and that you comply strictly with these terms.

This copyright permission does not constitute an endorsement of the products or services, nor does it encompass the granting of

any patent rights. The oneM2M Partners assume no responsibility for errors or omissions in this document.

짤 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC). All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand

and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations.

No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE,

GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY

PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS.

NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO

ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES.

oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

-->

<xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.onem2m.org/xml/protocols"

xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"

elementFormDefault="unqualified" xmlns:xs="http://www.w3.org/2001/XMLSchema">

<xs:include schemaLocation="CDT-commonTypes-v2_7_0.xsd" />

<xs:include schemaLocation="CDT-subscription-v2_7_0.xsd" />

<xs:include schemaLocation="CDT-semanticDescriptor-v2_7_0.xsd" />

<xs:element name="group" substitutionGroup="m2m:sg_announceableResource">

<xs:complexType>

<xs:complexContent>

<!-- Inherit common attributes for announceable Resources -->

<xs:extension base="m2m:announceableResource">

<xs:sequence>

<!-- Common Attribute, specific to <container>, <contentInstance>, <request> and <delivery> and other resources -->

<xs:element name="creator" type="m2m:ID" minOccurs="0" />

<!-- Resource Specific Attributes -->

<xs:element name="memberType" type="m2m:memberType" />

<xs:element name="currentNrOfMembers" type="xs:nonNegativeInteger" />

<xs:element name="maxNrOfMembers" type="xs:positiveInteger" />

<xs:element name="memberIDs" type="m2m:listOfURIs" />

<xs:element name="membersAccessControlPolicyIDs" type="m2m:listOfURIs" minOccurs="0" />

<xs:element name="memberTypeValidated" type="xs:boolean" />

<xs:element name="consistencyStrategy" type="m2m:consistencyStrategy" minOccurs="0" />

<xs:element name="groupName" type="xs:string" minOccurs="0" />

<xs:element name=”semanticSupportIndicator”type=”xs:boolean”minOccurs=”0” />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="childResource" type="m2m:childResourceRef" maxOccurs="unbounded" />

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:subscription" />

<xs:element ref="m2m:semanticDescriptor" />

</xs:choice>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

<xs:element name="groupAnnc" substitutionGroup="m2m:sg_announcedResource">

<xs:complexType>

<xs:complexContent>

<!-- Inherit common attributes for announced Resources -->

<xs:extension base="m2m:announcedResource">

<!-- Resource Specific Attributes -->

<xs:sequence>

<xs:element name="memberType" type="m2m:memberType" minOccurs="0" />

<xs:element name="currentNrOfMembers" type="xs:nonNegativeInteger" minOccurs="0" />

<xs:element name="maxNrOfMembers" type="xs:positiveInteger" minOccurs="0" />

<xs:element name="memberIDs" minOccurs="0">

<xs:simpleType>

<xs:list itemType="xs:anyURI" />

</xs:simpleType>

</xs:element>

<xs:element name="membersAccessControlPolicyIDs" type="m2m:listOfURIs" minOccurs="0" />

<xs:element name="memberTypeValidated" type="xs:boolean" minOccurs="0" />

<xs:element name="consistencyStrategy" type="m2m:consistencyStrategy" minOccurs="0" />

<xs:element name="groupName" type="xs:string" minOccurs="0" />

<xs:element name=”semanticSupportIndicator”type=”xs:boolean”minOccurs=”0” />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="childResource" type="m2m:childResourceRef" maxOccurs="unbounded" />

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:subscription" />

<xs:element ref="m2m:semanticDescriptor" />

<xs:element ref="m2m:semanticDescriptorAnnc" />

</xs:choice>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

</xs:schema>

File : CDT-group-v2_7_0.xsd(short)

<?xml version="1.0" encoding="utf-8"?>

<!--

Copyright Notification

The oneM2M Partners authorize you to copy this document, provided that you retain all copyright and other proprietary notices

contained in the original materials on any copies of the materials and that you comply strictly with these terms.

This copyright permission does not constitute an endorsement of the products or services, nor does it encompass the granting of

any patent rights. The oneM2M Partners assume no responsibility for errors or omissions in this document.

짤 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC). All rights reserved.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand

and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations.

No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE,

GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY

PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS.

NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO

ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES.

oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

-->

<xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.onem2m.org/xml/protocols" xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns:xs="http://www.w3.org/2001/XMLSchema" elementFormDefault="unqualified">

<xs:include schemaLocation="CDT-commonTypes-v2_7_0.xsd"/>

<xs:include schemaLocation="CDT-subscription-v2_7_0.xsd"/>

<xs:include schemaLocation="CDT-semanticDescriptor-v2_7_0.xsd"/>

<xs:element name="grp" substitutionGroup="m2m:sg_announceableResource">

<xs:complexType>

<xs:complexContent>

<!-- Inherit common attributes for announceable Resources -->

<xs:extension base="m2m:announceableResource">

<xs:sequence>

<!-- Common Attribute, specific to <container>, <contentInstance>, <request> and <delivery> and other resources -->

<xs:element name="cr" type="m2m:ID" minOccurs="0"/>

<!-- Resource Specific Attributes -->

<xs:element name="mt" type="m2m:memberType"/>

<xs:element name="cnm" type="xs:nonNegativeInteger"/>

<xs:element name="mnm" type="xs:positiveInteger"/>

<xs:element name="mid" type="m2m:listOfURIs"/>

<xs:element name="macp" type="m2m:listOfURIs" minOccurs="0"/>

<xs:element name="mtv" type="xs:boolean"/>

<xs:element name="csy" type="m2m:consistencyStrategy" minOccurs="0"/>

<xs:element name="gn" type="xs:string" minOccurs="0"/>

<xs:element name=”ssi” type= ”xs:boolean”minOccurs=”0” />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="ch" type="m2m:childResourceRef" maxOccurs="unbounded"/>

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:sub"/>

<xs:element ref="m2m:smd"/>

</xs:choice>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

<xs:element name="grpA" substitutionGroup="m2m:sg_announcedResource">

<xs:complexType>

<xs:complexContent>

<!-- Inherit common attributes for announced Resources -->

<xs:extension base="m2m:announcedResource">

<!-- Resource Specific Attributes -->

<xs:sequence>

<xs:element name="mt" type="m2m:memberType" minOccurs="0"/>

<xs:element name="cnm" type="xs:nonNegativeInteger" minOccurs="0"/>

<xs:element name="mnm" type="xs:positiveInteger" minOccurs="0"/>

<xs:element name="mid" minOccurs="0">

<xs:simpleType>

<xs:list itemType="xs:anyURI"/>

</xs:simpleType>

</xs:element>

<xs:element name="macp" type="m2m:listOfURIs" minOccurs="0"/>

<xs:element name="mtv" type="xs:boolean" minOccurs="0"/>

<xs:element name="csy" type="m2m:consistencyStrategy" minOccurs="0"/>

<xs:element name="gn" type="xs:string" minOccurs="0"/>

<xs:element name=”ssi” type=” xs:boolean”minOccurs=”0” />

<!-- Child Resources -->

<xs:choice minOccurs="0" maxOccurs="1">

<xs:element name="ch" type="m2m:childResourceRef" maxOccurs="unbounded"/>

<xs:choice minOccurs="1" maxOccurs="unbounded">

<xs:element ref="m2m:sub"/>

<xs:element ref="m2m:smd"/>

<xs:element ref="m2m:smdA"/>

</xs:choice>

</xs:choice>

</xs:sequence>

</xs:extension>

</xs:complexContent>

</xs:complexType>

</xs:element>

</xs:schema>

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf))

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?