| CHANGE REQUEST |
| --- |
| Meeting ID:* | PRO 27 |
| Source:* | Catalina Mladin, Convida Wireless, Mladin.Catalina@ConvidaWireless.com Dale Seed, Convida Wireless, Seed.Dale@ConvidaWireless.com Michael Starsinic, Convida Wireless, Starsinic.Michael@ConvidaWireless.com |
| Date:* | 2017-02-03 |
| Reason for Change/s:* | Providing the Stage 3 Definition of the Trigger Payload |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0058 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 release 3 (version TBD) |
| Clauses * | 5.2.1, 9, Annex B |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

ARC-2016-044R02-3GPP_Trigger_Payload updated TS-0001 to provide the details of the contents of the trigger Payload.  ARC-2017-xxxx updates the trigger payload definition in TS-0001 with additional details.  A stage 3 binding has not yet been created.

This contribution provides the stage 3 binding of the trigger payload contents.  JSON, XML, and CBOR formats are allowed.

R01 Changes:

- In the text before the table, more clearly explained what happens when payload is not present (i.e. trigger recipient establishes network connection).

- Aligned table format with the table format used for other resources in TS-0004.

- Added trigger payload for the types of serialization types supported (i.e. XML, JSON, CBOR)

- Moved short names into the existing short names section 8.2 of TS-0004

- Removed the “N” in executeCRUDN caused confusion.

- Changed WebSock…  WebSocket…

- Fixed table numbering 9.2-1    9.2.1-1

### -----------------------Start of change 1-------------------------------------------

### Interfaces to the underlying networks

The CSEs access the network service functions provided by the underlying networks such as 3GPP, 3GPP2 and WLAN via Mcn reference point. Protocol bindings to the Mcn reference point are described in clause 9. The following services are provided by the underlying networks:

Device triggering (see Annex B)

Location request (see Annex G)

Device Management (see clause 7.3.4)

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# Mcn procedures

## Introduction

The following clauses describe procedural details and message format bindings for various Mcn procedures.

## Triggering

### Introduction

A trigger request to an underlying network may include an optional payload. If the trigger has no  payload, the trigger recipient shall only re-establish a network connection to allow the IN-CSE to send requests to the trigger recipient.

If the trigger has an optional trigger payload, the trigger recipient shall use the trigger payload fields to determine the appropriate actions to perform. It is assumed that the recipient knows what actions to perform based on inspection of the payload. The trigger payload fields are described in Table 9.2.1-1.

Table 9.2.1-1: Trigger payload short names and field descriptions

| Field Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | establish Connection | registration Request | execute CRUD |  |  |
| triggerPurpose | M | M | M | m2m:triggerPurpose | If a trigger has a payload then this field is mandatory. If a trigger does not have a payload then the default triggerPurpose is establishConnection |
| triggerInfoAddress | O | O | M | xs:anyURI | No default When the triggerPurpose is “establishConnection”, and this field is provided, then this field is the unstructured CSE-Relative-Resource-ID of the <remoteCSE> or <AE> resource where the trigger recipient’s pointOfAccess needs to be updated. When the triggerPurpose is “establishConnection”, and this field is not provided, it is assumed that a network connection needs to be established but the PoA on the registrar CSE does not need to be updated. When the triggerPurpose is “registrationRequest”, and this field is provided, then this field is the unstructured CSE-Relative-Resource-ID of the Registrar CSE’s <cseBase> resource that the trigger recipient shall register to. When the triggerPurpose is “registrationRequest”, and this field is not provided, it is assumed the address of the Registrar CSE is provisioned in the trigger recipient. The provisioning method is outside the scope of this specification. When the triggerPurpose is “executeCRUD”, this field is mandatory and shall be configured with the unstructured CSE-Relative-Resource-ID of the resource that the CRUD operation is to be performed on. |
| triggerInfoAddressFQDN | O | O | O | xs:string | No default When the triggerPurpose is “establishConnection” and triggerInfoAddress is included, this field is the FQDN of the node hosting the <remoteCSE> or <AE> resource where the trigger recipient’s pointOfAccess needs to be updated. When the triggerPurpose is “registrationRequest”, and triggerInfoAddress is included, this field is the FQDN of the node hosting the <cseBase> resource that the trigger recipient shall register to. When the triggerPurpose is “executeCRUD”, this field is configured with the FQDN of the node that hosts the resource that the CRUD operation is to be performed on. |
| triggerInfoAddressIpv4addr | O | O | O | m2m:ipv4 | No default When the triggerPurpose is “establishConnection” and triggerInfoAddress is included, this field is the IPv4 address of the node hosting the <remoteCSE> or <AE> resource where the trigger recipient’s pointOfAccess needs to be updated. When the triggerPurpose is “registrationRequest”, and triggerInfoAddress is included, this field is the Ipv4 address of the node hosting the <cseBase> resource that the trigger recipient shall register to. When the triggerPurpose is “executeCRUD”, the field is configured with the Ipv4 Address of the node that hosts the resource that the CRUD operation is to be performed on. |
| triggerInfoAddressIpv6addr | O | O | O | m2m:ipv6 | No default When the triggerPurpose is “establishConnection” and triggerInfoAddress is included, this field is the Ipv6 address of the node hosting the <remoteCSE> or <AE> resource where the trigger recipient’s pointOfAccess needs to be updated. When the triggerPurpose is “registrationRequest”, and triggerInfoAddress is included, this field is the Ipv6 address of the node hosting the <cseBase> resource that the trigger recipient shall register to. When the triggerPurpose is “executeCRUD”, the field is configured with the Ipv6 Address of the node that hosts the resource that the CRUD operation is to be performed on. |
| httpBindingSupported | NP | NP | O | xs:boolean | 0: Not Supported (Default) 1: Supported When the triggerPurpose is “registrationRequest”, this field indicates if the trigger sender supports the HTTP protocol binding. |
| httpPortNo | NP | NP | O | xs:unsignedShort | No default When the triggerPurpose is “registrationRequest”, this field indicates what port number can be used to reach the trigger sender when using HTTP. If HTTP is supported and this field is not included, port 80 is assumed. |
| coapBindingSupported | NP | NP | O | xs:boolean | 0: Not Supported (Default) 1: Supported When the triggerPurpose is “registrationRequest”, this field indicates if the trigger sender supports the CoAP protocol binding. |
| coapPortNo | NP | NP | O | xs:unsignedShort | No default When the triggerPurpose is “registrationRequest”, this field indicates what port number can be used to reach the trigger sender when using CoAP. If CoAP is supported and this field is not included, port 5683 is assumed. |
| mqttBindingSupported | NP | NP | O | xs:boolean | 0: Not Supported (Default) 1: Supported When the triggerPurpose is “registrationRequest”, this field may be included, otherwise it is not included. It indicates if the trigger sender supports the MQTT protocol binding. |
| mqttPortNo | NP | NP | O | xs:unsignedShort | No default When the triggerPurpose is “registrationRequest”, this field indicates what port number can be used to reach the trigger sender when using MQTT. If MQTT is supported and this field is not included, port 1883 is assumed. |
| webSocketBindingSupported | NP | NP | O | xs:boolean | 0: Not Supported (Default) 1: Supported When the triggerPurpose is “registrationRequest”, this field indicates if the trigger sender supports the WebSocket protocol binding. |
| webSocketPortNo | NP | NP | O | xs:unsignedShort | No default When the triggerPurpose is “registrationRequest”, this field indicates what port number can be used to reach the trigger sender when using WebSocket. If WebSocket is supported and this field is not included, port 80 is assumed. |
| triggerInfoOperation | NP | NP | M | m2m:operation | No default See clause 6.3.4.2.5 |
| targetedResourceType | NP | NP | M | ms: resourceType | No default See clause 6.3.4.2.1 |
| triggerInfoAE-ID | O | O | O | m2m:ID | No default This field is included in the payload when to trigger an ASN-AE |
| xmlSupported | O | O | O | xs:boolean | 0: Not Supported (Default) 1: Supported This field defines whether or not the trigger sender supports XML serialization in requests from the trigger recipient. |
| jsonSupported | O | O | O | xs:boolean | 0: Not Supported (Default) 1: Supported This field defines whether or not the trigger sender supports JSON serialization in requests from the trigger recipient. |
| cborSupported | O | O | O | xs:boolean | 0: Not Supported (Default) 1: Supported This field defines whether or not the trigger sender supports CBOR serialization in requests from the trigger recipient.. |

Note: Mandatory payload fields are only mandatory if the trigger payload is present.

The trigger payload may be serialized in XML, JSON or CBOR format.  How the trigger sender knows the type of trigger payload serializations supported by the trigger recipient is outside the scope of this document and is assumed to be via pre-provisioning.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

(normative): 3GPP MTC Interworking

  - Device triggering

    - Providing device triggering service by means of 3GPP networks

Introduction

3GPP Underlying Network has defined a dedicated interface for requesting device triggering. The normative references for applicable interfaces are as follows: 3GPP TS 23.682 [15]. The specification for the interface Tsp is described in 3GPP TS 29.368 [16]. Tsp interface uses Diameter Base Protocol as specified in IETF RFC 3588 [13], in order to use such an interface the CSE shall act as a Diameter client as described in IETF RFC 6733 [14].

Before the CSE initiates the device triggering, the CSE and MTC-IWF shall execute the procedures once as specified in 3GPP TS29.368 [16].

Device action request command

When a CSE needs to issue a device triggering request to the MTC-IWF, the CSE shall send a Device-Action-Request (DAR) command (for detail, see TS 29.368 [16]). The following list provides the parameters mapping between the oneM2M and 3GPP.

Either External-Id or MSISDN:  the CSE maps it to the M2M-Ext-ID, see clause 6.2.

SCS identifier: the CSE maps it to the CSE-ID, see clause 6.2.

Application Port Identifier: the CSE maps it to Trigger-Recipient-ID, see clause 6.2.

Payload: the CSE maps it to the Trigger Payload, see clause 9.2.  The payload is provided to the 3GPP network as an OctetString via the payload AVP of the DAR command.

Device action answer command

As a result of device triggering request to MTC-IWF, the CSE receives a Device-Action-Answer (DAA) command (for detail, see TS 29.368 [16]).

Device notification request command

As a report of the result for device triggering delivery by 3GPP network, the CSE receives a Device-Notification-Request (DNR) command (for detail, see TS 29.368 [16]).

Device notification answer command

As a result of device notification request to MTC-IWF, the CSE sends a Device-Notification-Answer (DNA) command (for detail, see TS 29.368 [16]).

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

##### 6.3.4.2.x m2m:triggerPurpose

Used in definining trigger purpose in trigger payload

Table 6.3.4.2.x-1: Interpretation of m2m: triggerPurpose

| Value | Interpretation | Note |
| --- | --- | --- |
| 0 | establishConnection |  |
| 1 | registrationRequest |  |
| 2 | executeCRUD |  |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### Trigger payload fields

Trigger payload fields shall be translated into short names of Table 8.2.6-1.

Table 8.2.6-1: Trigger payload field short names

| Field name | Short Name |
| --- | --- |
| triggerPurpose | tpe |
| triggerInfoAddress | tia |
| triggerInfoAddressFQDN | tiaf |
| triggerInfoAddressIpv4addr | tia4 |
| triggerInfoAddressIpv6addr | tia6 |
| HttpBindingSupported | hbs |
| HttpPortNo | hpn |
| CoapBindingSupported | cpbs |
| CoapPortNo | cppn |
| MqttBindingSupported | mtbs |
| MqttPortNo | mtpn |
| WebSocketBindingSupported | wbs |
| WebSocketPortNo | wpn |
| triggerInfoOperation | tio |
| targetedResourceType | tgrt |
| triggerInfoAE-ID | taei |
| xmlSupported | xsp |
| jsonSupported | jsp |
| cborSupported | csp |

### -----------------------End of change 5-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?