| CHANGE REQUEST |
| --- |
| Meeting:* | PRO TP32.2 |
| Source:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Date:* | 2017-12-20 |
| Contact:* | BeiXu，Huawei，Echo.xubei@huawei.com |
| Reason for Change/s:* | Add new function of multicast group |
| CR against: Release* | <Release3> |
| CR against: WI* | Active < WI-0031 - Optimized Group-based Operation > MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V3_5_0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR is add new feature multicast group according to the TS-0001.

R02:  Restructure sections base on comments from PRO 32.2

R03: Update the procedure base on the comments in PRO session.

R04: Add the example for the update procedure.

R05&R06: Editoral update.

### -----------------------Start of change 1-------------------------------------------

## Informative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf)

[i.2]	Fielding, Roy Thomas (2000): "Architectural Styles and the Design of Network-based Software Architectures", Doctoral dissertation, University of California, Irvine.

[i.3]	OMA-TS-REST_NetAPI_NotificationChannel: "Open Mobile Alliance; RESTful Network API for Notification Channel", OMA-TS-REST_NetAPI_NotificationChannel-V1_0.

[i.4]	OMA-TS-MLP: "Open Mobile Alliance; Mobile Location Protocol", OMA-TS-MLP-V3_4-20130226-C Version 3.4.

[i.5]	W3C Resource Description Framework https://www.w3.org/RDF/.

[i.6]	W3C SPARQL Query Language for RDF https://www.w3.org/TR/rdf-sparql-query/.

[i.7]	IETF RFC 7515: "JSON Web Signature (JWS)", 2015.

[i.8]	IETF RFC 7516: "JSON Web Encryption (JWE)", 2015.

[i.9]	IETF RFC 7518: "JSON Web Algorithms (JWA)", 2015.

[i.x]                     IETF RFC 3171: “IANA Guidelines for IPv4 Multicast Address Assignments”, 2001

[i.y]                     IETF RFC 4291: “IP Version 6 Addressing Architecture”, 2006

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

###### 7.5.3	Multicast group procedures

7.5.3.1	Multicast group CREATE procedure

7.5.3.1.0  Common procedure

The Group Hosting CSE shall perform the following operations:

- The Group Hosting CSE shall check the multicastCapability attribute of each remote Member Hosting CSE’s <remoteCSE> resource.

- If at least two remote Member Hosting CSEs support multicast capability MBMS, then the Group Hosting CSE shall create  3GPP  MBMS multicast group for the members that support MBMS multicast capability, and refer to 7.5.3.1.1;

- If at least two remote Member Hosting CSEs support multicast capability IP, then the Group Hosting CSE shall create IP multicast group for the members that support IP multicast capability, and  refer to 7.5.3.1.2;

- Table 7.5.3.1.0-1:  Elements of Multicast Group Information Data Object

| Element Name | Description |
| --- | --- |
| groupID | Indicates the <group> resource identifier that the Multicast Group Information Data Object applies to. |
| multicastType | Indicates the type of multicasting supported by the group members. Different multicast types within one group shall be created as different data objects. |
| externalGroupID | It is used only for 3GPP MBMS multicast groups. Has the same value as the attribute externalGroupID of the related <localMulticastGroup> resources, see clause 7.4.xx. Different external Group IDs within one multicast type shall be created as different data objects. |
| multicastAddress | Has the same value as the attribute multicastAddress of the related <localMulticastGroup> resources, see clause 7.4.xx |
| multicastGroupFanoutTarget | Has the same value as the attribute multicastGroupFanoutTarget of the related <localMulticastGroup> resources, see clause 7.4.xx |
| memberList | Contains all the members of the memberLists of the related <localMulticastGroup> resources. |
| groupServiceServerAddress | It is used only for 3GPP MBMS multicast group. A group hosting CSE that supports MBMS Multicast will have this value provisioned by the 3GPP service provider. See TS-0001[6] clause 10.2.7.13. |
| TMGI | It is used only for 3GPP MBMS multicast group.Has the same value as the attribute TMGI of the related <localMulticastGroup> resources, see clause 7.4.xx |
| TMGIExpiration | It is used only for 3GPP MBMS multicast group. Indicates the duration of the TMGI expiration time. See TS-0001[6] clause 10.2.7.13. |
| responseTimeWindow | Has the same valued as the attribute responseTimeWindow of the related <localMulticastGroup> resources, see clause 7.4.xx |

##### 7.5.3.1.1	3GPP MBMS group creation procedure

The Group Hosting CSE shall perform the operations which are specified in clause 10.2.7.13.1 of TS-0001[6] and in clause 7.7.3.1 of TS-0026 [43]:

- Get the externalGroupID of the <remoteCSE>  resource for each member whose externalGroupID exists, send 3GPP Allocate TMGI Request [51] to the group Service Server Address as local configuration over Mcn reference point.

- When the Group Hosting CSE receives the corresponding response from 3GPP network:

  - If the response indicates failure, then the Group Hosting CSE shall stop the multicast group create procedure.

  - If the response indicates success, then the Group Hosting CSE shall get the TMGI and TMGIExpiration from the response.

- Locally create a Multicast Group Information data object for each distinct externalGroupID: set its groupID to the value of the created <group>, assign the multicastType to MBMS, allocate a multicastAddress, set the externalGroupID to the same value as the externalGroupID of the <remoteCSE>  resources, set the memberList to the members that belong to this multicast group, set the groupServiceServerAddress to the value provisioned by the 3GPP service provider,  set the TMGI and TMGIExpiration to the values in the response from 3GPP network, set responseTimeWindow according to local policy. Assign a{fanout-segment} string, and set the multicastGroupFanoutTarget to /{groupHostingCSE-ID}/ {fanout-segment}.

Note: For a guide to an allocation scheme of IPv4 and IPv6 multicast address spaces, reference may be made to standard documents such as RFC 3171 [i.x] and RFC 4291 [i.y].

- Send a CREATE <localMulticastGroup> primitive to each Member Hosting CSE in the multicast group.

- Prepare the attributes of the <localMulticastGroup> resource according to the Multicast Group Information and send <localMulticastGroup> create request to each Member Hosting CSE in the multicast group. See clause 7.2.2.1.

- When the Group Hosting CSE receives the corresponding response from each Member Hosting CSE:

  - If at least two Member Hosting CSEs respond successfully, the Group Hosting CSE shall remove the member ID(s) from the memberList for any Member Hosting CSEs whose response indicates failure.

  - If no Member Hosting CSEs responds successfully, the Group Hosting CSE shall delete the local Multicast Group Information data object.

  - If only one Member Hosting CSEs responds successfully, the Group Hosting CSE shall delete the local Multicast Group Information data object and send a <localMulticastGroup> delete request to that Member Hosting CSE. See clause 7.2.2.1

##### 7.5.3.1.2	IP multicast group creation procedure

The Group Hosting CSE shall perform the operations which are specified in clause 10.2.7.13.1 of TS-0001[6]:

- Locally create a Multicast Group Information data object: set its groupID to the value of the created <group>, assign the multicastType to IP,  allocate a multicastAddress,  set the memberList to the members that belong to this multicast group, set responseTimeWindow according to local policy. Assign a{fanout-segment} string, and set the multicastGroupFanoutTarget to /{groupHostingCSE-ID}/ {fanout-segment}.

Note: For a guide to an allocation scheme of IPv4 and IPv6 multicast address spaces, reference may be made to standard documents such as RFC 3171 [i.x] and RFC 4291 [i.y].

- Send a CREATE <localMulticastGroup> primitive to each Member Hosting CSE in the multicast group.

  - Prepare the attributes of the <localMulticastGroup> resource according to the Multicast Group Information and send <localMulticastGroup> create request to each Member Hosting CSE in the multicast group. See clause 7.2.2.1

- When the Group Hosting CSE receives the corresponding response from each Member Hosting CSE:

  - If at least two Member Hosting CSEs respond successfully, the Group Hosting CSE shall remove the member ID(s) from the memberList for any Member Hosting CSEs whose response indicates failure.

  - If no Member Hosting CSE responds successfully, the Group Hosting CSE shall delete the Multicast Group Information locally.

  - If only one Member Hosting CSEs responds successfully, the Group Hosting CSE shall delete the local Multicast Group Information data object and send a <localMulticastGroup> delete request to that Member Hosting CSE. See clause 7.2.2.1

#### 7.5.3.2	Multicast group UPDATE procedure

If the memberIDs attribute of the <group> resource was updated, the receiver shall check the multicastCapability attribute of each remote Member Hosting CSE’s <remoteCSE> resource according to the new memberIDs and then make modifications to the <localMulticastGroup> resources on the remote Member Hosting CSEs as appropriate.

For example, the memberIDs in the <group> resource is illustrated in Table 7.5.3.2-1. Table 7.5.3.2-1 shows the old and new memberIDs in the example:

- Table 7.5.3.2-1:  memberIDs Example of <group> resource

|  | Member Hosting CSE1 | Member Hosting CSE2 | Member Hosting CSE3 | Member Hosting CSE4 | Member Hosting CSE5 | Member Hosting CSE6 | Member Hosting CSE7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Old memberIDs | /CSE1/aa | /CSE2/aa | /CSE3/aa | /CSE4/aa | /CSE5/aa | NA | NA |
| New memberIDs | /CSE1/aa | NA | /CSE3/aa /CSE3/bb | /CSE4/aa | NA | /CSE6/aa | /CSE7/aa |

The old Multicast Group Information data objects of this group are illustrated in Table 7.5.3.2-2:

- Table 7.5.3.2-2:  Multicast Group Information Data Object Example of <group> resource

| Group | multicastGroupType | memberList | externalGroupID |
| --- | --- | --- | --- |
| /CSEXX/group1 | IP | /CSE1/aa /CSE2/aa |  |
| /CSEXX/group1 | MBMS | /CSE3/aa /CSE4/aa /CSE5/aa | 12345678901 |

- If there are fewer than two new Member Hosting CSEs supporting multicast, the receiver shall delete all the local Multicast Group Information data objects and send  <localMulticastGroup> delete requests to each old Member Hosting CSE before updated. See clause 7.2.2.1.1

- If there are at least two new Member Hosting CSEs supporting multicast, the receiver shall create new local Multicast Group Information data objects according to the new Member Hosting CSEs.

In this example, the new Multicast Group Information is illustrated in table Table 7.5.3.2-3. The IP multicast is deleted because there is only one Member Hosting CSE (CSE1) left. The two MBMS multicast group data objects are created because there are two different externalGroupIDs.

- Table 7.5.3.2-3:  Multicast Group Information Data Object Example of <group> resource

| Group | multicastGroupType | memberList | externalGroupID |
| --- | --- | --- | --- |
| /CSEXX/group1 | MBMS | /CSE6/aa /CSE7/aa | 12345678902 |
| /CSEXX/group1 | MBMS | /CSE3/aa /CSE3/bb /CSE4/aa | 12345678901 |

- The receiver compares each new Multicast Group Information data objects with the each of the old data objects:

  - If a Member Hosting CSE exists in one of the new data objects and does not exist in any of the old ones, the receiver shall send a <localMulticastGroup> create request to that Member Hosting CSE. See clause 7.2.2.1.1

  - If a Member Hosting CSE exists in an old data object and does not exist in any of the new ones,  the receiver shall send a <localMulticastGroup> delete request to that Member Hosting CSE. See clause 7.2.2.1.1

  - If a Member Hosting CSE exists in both a new data object and an old one, the receiver shall compare the memberIDs in the two data objects. If the result is different, the receiver shall send a <localMulticastGroup> update request to the Member Hosting CSE, see clause 7.2.2.1.1.

In this example, the operations for each Member Hosting CSE are illustrated in Table 7.5.3.2-4.

- Table 7.5.3.2-4:  <localMulticastGroup> Operation for Member Hosting CSEs Example

| Member Hosting CSE | Operation in the Request |
| --- | --- |
| CSE1 | DELETE |
| CSE2 | DELETE |
| CSE3 | UPDATE |
| CSE4 | NA |
| CSE5 | DELETE |
| CSE6 | CREATE |
| CSE7 | CREATE |

- When the Group Hosting CSE receives the corresponding response from each Member Hosting CSE in the new Multicast Group Information data object, the receiver shall remove the member ID(s) from the memberList for any Member Hosting CSEs whose response indicates failure:

In this example, the responses for each Member Hosting CSE are illustrated in table Table 7.5.3.2-5.

- Table 7.5.3.2-5:  <localMulticastGroup> Operation Result for Member Hosting CSEs Example

| Member Hosting CSE | Operation in the Request | Result indicating in the Response |
| --- | --- | --- |
| CSE1 | DELETE | Failure |
| CSE2 | DELETE | Success |
| CSE3 | UPDATE | Failure |
| CSE4 | NA | NA |
| CSE5 | DELETE | Failure |
| CSE6 | CREATE | Failure |
| CSE7 | CREATE | Success |

  - If at least two Member Hosting CSEs exist in the data object, the receiver shall keep the Multicast Group Information data object;

  - If no Member Hosting CSE exists in the data object, the receiver shall delete the Multicast Group Information locally.

  - If only one Member Hosting CSEs exists in the data object, the receiver shall delete the local Multicast Group Information data object and send a <localMulticastGroup> delete request to that Member Hosting CSE. See clause 7.2.2.1

In this example, the new Multicast Group Information is illustrated after the response process in table Table 7.5.3.2-6.

- Table 7.5.3.2-6:  Multicast Group Information Data Object Example of <group> resource

| Group | multicastGroupType | memberList | externalGroupID |
| --- | --- | --- | --- |
| /CSEXX/group1 | MBMS | /CSE3/aa /CSE4/aa | 12345678901 |

  - The receiver shall delete all the old Multicast Group Information data object;

#### 7.5.3.3	Multicast group DELETE procedure

If there are one or more Multicast Group Information data objects associated with the deleted group, the receiver shall delete all the Multicast Group Information data objects and send <localMulticastGroup> delete requests to each Member Hosting CSE, refer to the clause 7.2.1.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 7.4.13.2	<group> resource specific procedure on CRUD operations

##### 7.4.13.2.0	Introduction

This clause describes <group> resource specific procedure on Resource Hosting CSE for CRUD operations.

##### 7.4.13.2.1 Create

Originator:

For members which are of type <group>, the Originator shall suffix the  ‘/fopt’ to that ‘memberID‘ during group creation if the Originator wants to fan-out the group request to each member of that sub-<group>, else the Originator shall not  suffix the  ‘/fopt’ to that ‘memberID‘.

Receiver:

Primitive specific operation after Recv-C-6.4 "Check validity of resource representation for the given resource type" and before Recv-C-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed". See clause 7.2.2.2.

- Primitive specific operation: Validate the provided attributes. It shall also check whether the number of URIs present in the memberIDs attribute of the group resource representation does not exceed the maximum as specified by the maxNrOfMembers attribute. If the maximum is exceeded, the request shall be rejected with a Response Status Code indicating "MAX_NUMBER_OF_MEMBER_EXCEEDED" error. If there are duplicate members in the memberIDs attribute then the duplicate members are removed before creation of the <group> resource.
If the memberType attribute of the <group> resource is not "MIXED", the Hosting CSE shall also verify that all the member IDs including sub-groups in the attribute memberIDs of the <group> resource representation provided in the request shall conform to the memberType of the group resource. To validate a resource type of a member, the Hosting CSE shall check the resourceType attribute of the resource which is indicated by the member ID. To check the resourceType attribute, the Hosting CSE may retrieve the member resource. When a member ID is virtual resource, the Hosting CSE shall check the resourceType attribute of the parent resource. If the resource type of the parent allows this child virtual resource type, the Hosting CSE checks whether the virtual resource type matches with the memberType attribute of the group. If they match, then the Hosting CSE considers that the virtual member resource is validated. If the resourceType cannot be retrieved due to lack of privilege, the request shall be rejected with a Response Status Code indicating "RECEIVER_HAS_NO_PRIVILEGE" error.

In the case that the <group> resource contains sub-group member resources, the receiver shall retrieve the memberType of the sub-group member resources to validate the memberType. If the memberType cannot be retrieved due to lack of privilege, the request shall be rejected with a Response Status Code indicating "RECEIVER_HAS_NO_PRIVILEGE" error. If the sub-group member resources are temporarily unreachable, the receiver shall set the memberTypeValidated attribute of the <group> resource to FALSE and return the result to the originator in the response of the request. As soon as any unreachable sub-group resource becomes reachable, the receiver shall perform the memberType validation procedure. The originator may get to know the validation result by subscribing to the created resource if the memberTypeValidated attribute is FALSE. Upon unsuccessful validation, the receiver shall delete the <group> resource if the consistencyStrategy of the <group> resource is ABANDON_GROUP, or remove the inconsistent members from the <group> resource if the consistencyStrategy attribute is ABANDON_MEMBER, or set the memberType attribute of the <group> resource to "MIXED" if the consistencyStrategy attribute is SET_MIXED.

The memberTypeValidated attribute shall be set to TRUE if all the members have been validated successfully. If a member validation for the memberType of the <group> resource is unsuccessful, then the Hosting CSE shall perform the following:

- If the consistencyStrategy of the <group> resource is ABANDON_GROUP then the request shall be rejected with a Response Status Code indicating "GROUP_MEMBER_TYPE_INCONSISTENT" error.

If the consistencyStrategy of the <group> resource is ABANDON_ MEMBER then remove the inconsistent members and create the <group> resource and the memberTypeValidated attribute shall be set to TRUE.

If the consistencyStrategy of the <group> resource is SET_ MIXED then set the memberType attribute of the <group> resource to "MIXED" and create the <group> resource and the memberTypeValidated attribute shall be set to TRUE.

After Recv-6.7 "Create a success response", the receiver shall perform multicast group creation procedure if the Group Hosting CSE supports multicast. See clause 7.5.3.1.

##### 7.4.13.2.2 Retrieve

No primitive specific operations.

##### 7.4.13.2.3 Update

Originator:

If the Originator intends to update memberIDs attribute ,for members which are of type <group>,  the Originator shall suffix the  ‘/fopt’ to that ‘memberID‘ during group updation  if the Originator wants to fan-out the group request to each member of that sub-<group> ,else the Originator shall not  suffix the  ‘/fopt’ to that ‘memberID‘.

Receiver:

- Primitive specific operation after Recv-6.4 "Check validity of resource representation for the given resource type" and before Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed ". See clause 7.2.2.2.Primitive specific operation: If the memberType attribute of the <group> resource is not "MIXED", the Hosting CSE shall verify that all the member IDs including sub-groups in the attribute memberIDs of the <group> resource representation provided in the request shall conform to the memberType of the <group> resource. Virtual member resource validation shall be done as specified in the group creation procedure (clause 7.4.13.2.1 step 1).

In the case that the <group> resource contains sub-group member resources, the receiver shall retrieve the memberType of the sub-group member resource to validate the memberType. If the memberType cannot be retrieved due to lack of privilege, the request shall be rejected with a Response Status Code indicating "RECEIVER_HAS_NO_PRIVILEGE" error. If the sub-group member resources are temporarily unreachable, the receiver shall set the memberTypeValidated attribute of the <group> resource to FALSE and return the result to the originator in the response of the request. As soon as any unreachable sub-group resource becomes reachable, the receiver shall perform the memberType validation procedure. The Originator may get to know the validation result by subscribing to the created resource if the memberTypeValidated attribute is FALSE. Upon unsuccessful validation, the receiver shall delete the <group> resource if the consistencyStrategy of the <group> resource is ABANDON_GROUP, or remove the inconsistent members from the <group> resource if the consistencyStrategy attribute is ABANDON_MEMBER, or set the memberType attribute of the <group> resource to "MIXED" if the consistencyStrategy attribute is SET_MIXED.

The memberTypeValidated attribute shall be set to TRUE if all the members have been validated successfully. If a member validation for the memberType of the <group> resource is unsuccessful, then the Hosting CSE shall perform the following:

- If the consistencyStrategy of the <group> resource is ABANDON_GROUP then the request shall be rejected with a Response Status Code indicating "GROUP_MEMBER_TYPE_INCONSISTENT" error.

If the consistencyStrategy of the <group> resource is ABANDON_ MEMBER then remove the inconsistent members and update the <group> resource and the memberTypeValidated attribute shall be set to TRUE.

If the consistencyStrategy of the <group> resource is SET_ MIXED then set the memberType attribute of the <group> resource to "MIXED" and update the <group> resource and the memberTypeValidated attribute shall be set to TRUE.

Primitive specific operation: The Hosting CSE shall check whether the number of provided memberIDs in the attribute members exceeds the limitation of maxNrOfMembers. The Hosting CSE shall also check whether the value provided in the maxNrOfMembers attribute is smaller than the currentNrOfMembers attribute value. If any of the condition is true, the Hosting CSE shall reject the request with Response Status Code indicating "MAX_NUMBER_OF_MEMBER_EXCEEDED". error.

After Recv-10.0 "Send Response Primitive", the receiver shall perform multicast group UPDATE procedure if the Group Hosting CSE supports multicast. See clause 7.5.3.2.

##### 7.4.13.2.4 Delete

After Recv-10.0 "Send Response Primitive", the receiver shall perform multicast group DELETE procedure if the Group Hosting CSE supports multicast. See clause 7.5.3.3.

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?